| Input Contribution |
| --- |
| Meeting ID* | TST#26 |
| Title:* | TS-0018 TPs for Retrieve operation of resources under CSEBase |
| Source:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Sookhyun Jeon, TTA, shjeon@tta.or.kr |
| Uploaded Date:* | 2016-12-04 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes TPs for retrieve operation of resources under CSEBase.

## -----------------------Start of change 1--------------------------------------------

## Group CSE

## Data Management and Repository (DMR)

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/013 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the TARGET_RESOURCE_ADDRESS resource under CSEBase |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the <CSEBase> resource and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing the resource TARGET_RESOURCE_ADDRESS } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/013_01 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/013_02 | TS-0001 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/BV/013_03 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/013_04 | TS-0001 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/BV/013_05 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/013_06 | TS-0001 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/013_07 | TS-0001 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/BV/013_08 | TS-0001 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/BV/013_09 | TS-0001 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/BV/013_10 | TS-0001 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/BV/013_11 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/013_12 | TS-0001 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/BV/013_13 | TS-0001 10.2.15.3 | 21 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/BV/013_14 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/014 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to retrieve the resource TARGET_RESOURCE_ADDRESS without having privileges for the RETRIEVE operation |
| Reference | TS-0001 10.1.2 - item 14 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the <CSEBase> resource and the AE not having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4103 (ACCESS_DENIED) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/014_01 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BO/014_02 | TS-0001 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/BO/014_03 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BO/014_04 | TS-0001 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/BO/014_05 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BO/014_06 | TS-0001 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/BO/014_07 | TS-0001 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/BO/014_08 | TS-0001 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/BO/014_09 | TS-0001 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/BO/014_10 | TS-0001 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/BO/014_11 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BO/014_12 | TS-0001 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/BO/014_13 | TS-0001 10.2.15.3 | 21 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/BO/014_14 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/015 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the ATTRIBUTE of TARGET_RESOURCE_ADDRESS resource (“To” option) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the <CSEBase> resource and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_ATTRIBUTE_ADDRESS and From set to AE_ID and no Content attribute } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributeList containing ATTRIBUTE attribute } | IUT ( AE |
| Notes: TARGET_ATTRIBUTE_ADDRESS = TARGET_RESOURCE_ADDRESS # ATTRIBUTE ATTRIBUTE = Common attribute for all RESOURCE_TYPE resources listed in the table below |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/015_01 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/015_02 | TS-0001 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/BV/015_03 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/015_04 | TS-0001 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/BV/015_05 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/015_06 | TS-0001 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/015_07 | TS-0001 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/BV/015_08 | TS-0001 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/BV/015_09 | TS-0001 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/BV/015_10 | TS-0001 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/BV/015_11 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/015_12 | TS-0001 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/BV/015_13 | TS-0001 10.2.15.3 | 21 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/BV/015_14 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/016 |
| --- | --- |
| Test objective | Check that the IUT returns successfully the ATTRIBUTE of TARGET_RESOURCE_ADDRESS resource (“Content” option) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the <CSEBase> resource and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing attribute containing name set to ATTRIBUTE and no value name } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributeList containing the attribute ATTRIBUTE attribute } | IUT ( AE |
| Notes: ATTRIBUTE = Common attribute for all RESOURCE_TYPE resources listed in the table below |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/016_01 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/016_02 | TS-0001 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/BV/016_03 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/016_04 | TS-0001 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/BV/016_05 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/016_06 | TS-0001 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/016_07 | TS-0001 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/BV/016_08 | TS-0001 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/BV/016_09 | TS-0001 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/BV/016_10 | TS-0001 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/BV/016_11 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/016_12 | TS-0001 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/BV/016_13 | TS-0001 10.2.15.3 | 21 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/BV/016_14 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BV/017 |
| --- | --- |
| Test objective | Check that the IUT returns successfully multiple attributes of TARGET_RESOURCE_ADDRESS resource |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the <CSEBase> resource and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing attribute containing name set to ATTRIBUTE_1 name and no value and attribute containing name set to AATTRIBUTE_2 name and no value } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 2000 (OK) and Content attribute containing attributeList containing the attribute ATTRIBUTE_1 attribute and the attribute ATTRIBUTE_2 attribute } | IUT ( AE |
| Notes: ATTRIBUTE_1 = Common attribute for all RESOURCE_TYPE resources listed in the table below ATTRIBUTE_2 = Common attribute for all RESOURCE_TYPE resources listed in the table below |

| TP Id | Reference | RESOURCE_TYPE |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BV/017_01 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/017_02 | TS-0001 10.2.1.2 | 2 (AE) |
| TP/oneM2M/CSE/DMR/RET/BV/017_03 | TS-0001 10.2.4.2 | 3 (container) |
| TP/oneM2M/CSE/DMR/RET/BV/017_04 | TS-0001 10.2.5.3 | 6 (delivery) |
| TP/oneM2M/CSE/DMR/RET/BV/017_05 | TS-0001 10.2.7.3 | 9 (group) |
| TP/oneM2M/CSE/DMR/RET/BV/017_06 | TS-0001 10.2.10.1.2 | 10 (locationPolicy) |
| TP/oneM2M/CSE/DMR/RET/BV/017_07 | TS-0001 10.2.8.3 | 12 (mgmtCmd) |
| TP/oneM2M/CSE/DMR/RET/BV/017_08 | TS-0001 10.2.14.2 | 14 (node) |
| TP/oneM2M/CSE/DMR/RET/BV/017_09 | TS-0001 10.2.2.2 | 16 (remoteCSE) |
| TP/oneM2M/CSE/DMR/RET/BV/017_10 | TS-0001 10.2.20.2 | 17 (request) |
| TP/oneM2M/CSE/DMR/RET/BV/017_11 |  | 18 (schedule) |
| TP/oneM2M/CSE/DMR/RET/BV/017_12 | TS-0001 10.2.15.11 | 21 (statsCollect) |
| TP/oneM2M/CSE/DMR/RET/BV/017_13 | TS-0001 10.2.15.3 | 21 (statsConfig) |
| TP/oneM2M/CSE/DMR/RET/BV/017_14 | TS-0001 10.2.11.3 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/018 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to retrieve a non-existing attribute of the TARGET_RESOURCE_ADDRESS resource (“single” attribute case) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the <CSEBase> resource containing no attribute ATTRIBUTE and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing ATTRIBUTE name } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/018_01 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_02 | TS-0001 10.2.1.2 | 2 (AE) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_03 | TS-0001 10.2.4.2 | 3 (container) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_04 | TS-0001 10.2.5.3 | 6 (delivery) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_05 | TS-0001 10.2.7.3 | 9 (group) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_06 | TS-0001 10.2.10.1.2 | 10 (locationPolicy) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_07 | TS-0001 10.2.8.3 | 12 (mgmtCmd) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_08 | TS-0001 10.2.14.2 | 14 (node) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_09 | TS-0001 10.2.2.2 | 16 (remoteCSE) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_10 | TS-0001 10.2.20.2 | 17 (request) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_11 |  | 18 (schedule) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_12 | TS-0001 10.2.15.11 | 21 (statsCollect) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_13 | TS-0001 10.2.15.3 | 21 (statsConfig) | labels |
| TP/oneM2M/CSE/DMR/RET/BO/018_14 | TS-0001 10.2.11.3 | 23 (subscription) | labels |

| TP Id | TP/oneM2M/CSE/DMR/RET/BO/019 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when the AE tries to retrieve a non-existing attribute of the TARGET_RESOURCE_ADDRESS resource (“multiple” attributes case) |
| Reference | TS-0001 10.1.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE under the <CSEBase> resource containing no attribute ATTRIBUTE_1 and no attribute ATTRIBUTE_2 and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Content attribute containing attributeList containing attribute containing name set to ATTRIBUTE_1 name and no value and attribute containing name set to AATTRIBUTE_2 name and no value } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4004 (NOT_FOUND) } | IUT ( AE |

| TP Id | Reference | RESOURCE_TYPE | ATTRIBUTE_1 | ATTRIBUTE_2 |
| --- | --- | --- | --- | --- |
| TP/oneM2M/CSE/DMR/RET/BO/019_01 | TS-0001 10.2.21.2 | 1 (accessControlPolicy) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_02 | TS-0001 10.2.1.2 | 2 (AE) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_03 | TS-0001 10.2.4.2 | 3 (container) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_04 | TS-0001 10.2.5.3 | 6 (delivery) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_05 | TS-0001 10.2.7.3 | 9 (group) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_06 | TS-0001 10.2.10.1.2 | 10 (locationPolicy) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_07 | TS-0001 10.2.8.3 | 12 (mgmtCmd) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_08 | TS-0001 10.2.14.2 | 14 (node) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_09 | TS-0001 10.2.2.2 | 16 (remoteCSE) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_10 | TS-0001 10.2.20.2 | 17 (request) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_11 |  | 18 (schedule) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_12 | TS-0001 10.2.15.11 | 21 (statsCollect) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_13 | TS-0001 10.2.15.3 | 21 (statsConfig) | labels | announceTo |
| TP/oneM2M/CSE/DMR/RET/BO/019_14 | TS-0001 10.2.11.3 | 23 (subscription) | labels | announceTo |

## -----------------------End of change 1--------------------------------------------