| Input Contribution |
| --- |
| Meeting ID* | TST 26 |
| Title:* | TS-0018-Test Purposes contribution REG |
| Source:* | Easy Global Market |
| Uploaded Date:* | 2016-12-05 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some additional TPs for group REG of the TS-0018 – Test Suite Structure and Test Purposes.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2.2	Group CSE

## 7.2.2.1		Registration (REG)

| TP Id | TP/oneM2M/CSE/REG/BV/006 |
| --- | --- |
| Test objective | Check that the IUT refuses registration of already registered AE (C-AE-ID-STEM provided by AE) |
| Reference | TS-0001 10.1.1.2.2 – step 4, 9.6.19 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a AE resource containing a AE-ID resource set to C-AE-ID-STEM } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and From set to C-AE-ID-STEM } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4005 (OPERATION_NOT_ALLOWED) } | IUT ( AE |

| TP Id | TP/oneM2M/CSE/REG/BV/007 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE re-registration (allowed M2M-SP-assigned AE-ID, S-AE-ID-STEM provided by AE) |
| Reference | TS-0001 10.1.1.2.2 – case b, 9.6.19 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource containing a ServiceSubscribedNode resource containing RuleLinks attribute pointing to a ServiceSubscribedAppRule resource containing applicableCredIDs attribute set to None and allowedApp-IDs attribute indicating APP-ID and allowedAEs attribute indicating a value starting with ‘S’ and containing wildcard } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing Resource-Type set to 2 (AE) and From set to S-AE-ID-STEM and Content <AE> containing App-ID attribute set to APP-ID } | IUT ( AE |
|  | then { the IUT sends a UPDATE request to the IN-CSE containing Resource-Type set to 10002 (AEAnnc) and To set to IN-CSE-ID / S-AE-ID-STEM and From set to ‘/S’ and Content <AEAnnc> containing App-ID attribute set to APP-ID and nodeLink attribute set to ??? and Labels indicating ‘Credential-ID:None’ } | IUT ( IN-CSE |
|  | then { the IUT receives a Response message from IN-CSE containing Response Status Code set to 2004 (UPDATED) and Content <AEAnnc> containing App-ID attribute set to APP-ID and nodeLink attribute set to ??? and Labels indicating ‘Credential-ID:None’ } | IUT ( IN-CSE |

================ End of  1st  Part: Test Purposes ==================

# Comments

4005 (OPERATION_NOT_ALLOWED), 
4105 (CONFLICT) or 
4000 (BAD_REQUEST) ?

I’m not sure what is the most appropriate because it isn’t stated explicitely.