| Input Contribution |
| --- |
| Meeting ID* | TST#26 |
| Title:* | New guide added to WI-0054 developers guide series |
| Source:* | Patricia Martigne, ORANGE patricia.martigne@orange.com Maciek Goluch, ORANGE Andreas Kraft, DT |
| Uploaded Date:* | 2016-12-07 |
| Document(s) Impacted* | TR-xxxx |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to be incorporated into the document. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

It is proposed to add a developers’ guide  to the series proposed in WI-0054.

------------------------------------------------------------Start of CHANGE 1 ----------------------------------

5	Scope

The guideline analyzes and implements some simple examples showing how to map it into an oneM2M service platform using Release 2. It describes for basic use cases, some procedures and scenarios, including diagrams, message flows, message traces samples, resource description samples, etc.

9 scenarios are foreseen, described in different Technical Reports.

- The TR-0025 covers a simple scenario of a remote lights control based on oneM2M release 1. It enables the remote control of lights through a smartphone embedding an application that gains access to an oneM2M compliant service platform using HTTP binding and XML serialization. Such deployment of oneM2M standard of present use cases requires the execution of common procedures like Registration, Discovery, Group management, etc. The proposed work item proposes to update and align the TR-0025 with the oneM2M release 2.

- The second Technical report is to provide a simple use case in a similar way as described in TR-0025 light control). This TR will be the opportunity to address release 2 and also to take into account other protocol binding and serialization. It is foressen to present a scenario of sensing temperature and related actuator, using CoAP Protocol binding and JSON serialization

- The third Technical Report is to provide guideline to developers to implement security as specified by oneM2M TS-0003, using a simple use case as example. It will address the initial security provisioning for enrolment with a Service Provider, and the operational phase relying on a Security Association Establishment process to implement secure connection and access control services for basic use cases.

As example, it could be considered use cases implementing a service with:-

- Authentiction

- Authorisation

- Secure communications

- The fourth Technical Report is to describe how developer can quickly implement semantic functionnaluty of the release 2. The intended work is to describe a basic scenario where Smart Appliances implementing the SAREF ontology can exchange data using the the mapping to oneM2M Base Ontology and the semantic functionalities of a oneM2M service platform.

- The fifth Technical Report is to describe how developer can quickly implement interworking with non-oneM2M device using the porwerfull meachnism defined in the IPE Interworking Proxy Entity. The basic scenario could to describe by example a simple interworking between a Zigbee device sensor to be monitored by CSE via IPE function

- The sixth Technical Report is to describe how developer can quickly implement Device Management of M2M devices, based on a simple use case. As example, it is foreseen a set of basic procedures using OMA LWM2M and/or OMA DM and/or TR-069.

- The seventh Technical report is to provide a simple use case in a similar way as described in TR-0025 but addressing other case as the light control. It is foressen to present a simple use case of smart agriculture farm, using MQTT Protocol binding and JSON serialization and based on oneM2M Rel.2. The scenario will describe an example of implementation of a basic farm management in a smart and convenient way. For instance, collecting indoor temperature and humidity, illumination and trigger certain devices such as fans, sidewindown screen to adjust the indoor temperature in order to guarantee the most suitable conditions for growing plants.

Sensors and actuators will be deployed and interconnected to and communicate to the infrastructure CSE using MQTT protocol binding. oneM2M common services functions including REG, data management, subscription and notification etc. will be implemented in the use case. In addition, since the difference in working principle between HTTP (CoAP) and MQTT, it is intended also cover the configuration details for MQTT broker in order to implement those functions required in the use case as well as notifications through MQTT.

- The eighth Technical report is to provide a guideline on implementation of 3GPP interworking functions in R2. Being aware of mobile network and its capabilities is one of the critical aspects of successful oneM2M implementation. This guideline may be very helpful for implementing communications to devices, particularly for operators.

- The nineth Technical Report is to describe how a developer can easily implement the SDT (Smart Device Template) based semantic functionnality of the release 2 described in TS-0023 (Home appliances Information Model). This guideline is of particular interest for monitoring and controlling a home appliance in a unified way, whatever local connectivity technology (e.g. ZigBee, ZWave, etc) is used by the appliance and whoever the manufacturer is.

6	Schedule and impacted specifications

Provide the schedule of tasks to be performed;

| New Specifications (if any) |
| --- |
| Document Type | Document Number* | Title | Schedule (TP No.) | Lead WG | Impacted WGs | Comments |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |  |
| TR | TR-0025 | Application developer guide: Light control example using HTTP binding | TP 25 | TP 26 | TP 27 | TP 29 | TST |  | Rapporteur: Laurent Velez |
| TR | TR-00xx | Application developer guide: Temperature monitoring example using CoAP binding | TP 25 | TP 28 | TP 30 | TP 32 | TST |  | Rapporteur: Shane He |
| TR | TR-00xx | Developer guide: Implementing security example | TP 25 | TP 28 | TP 30 | TP 32 | TST | SEC | Rapporteur: Francois Ennesser, & Laurent Velez |
| TR | TR-00xx | Developer guide: Implementing Semantic- the SAREF use case | TP 25 | TP 28 | TP 30 | TP 32 | TST | MAS | Rapporteur: TBD |
| TR | TR-00xx | Application developer guide: Interworking Proxy Entity example use case | TP 25 | TP 28 | TP 30 | TP 32 | TST | ARC | Rapporteur: Mahdi Ben Alaya & Laurent Velez |
| TR | TR-00xx | Developer guide: Device Management use case | TP 25 | TP 28 | TP 30 | TP 32 | TST | MAS | Rapporteur: Jiaxin Yin |
| TR | TR-00xx | Developer guide: smart farm example using MQTT binding | TP 25 | TP 28 | TP 30 | TP 32 | TST |  | Rapporteur: Ting Martin Miao |
| TR | TR-00xx | Developer guide: 3GPP interworking example | TP 25 | TP 28 | TP 30 | TP 32 | TST | ARC | Rapporteur: Jessie Lijing & Patricia Martigne & James Hu |
| TR | TR-00vv | Developer guide: SDT-based implementation | TP 27 | TP29 | TP30 | TP32 | TST | MAS | Patricia Martigne, Laurent Velez |

* Optional for first versions (i.e. before it will be assigned by the secretariat)

------------------------------------------------------------End of CHANGE 1 ----------------------------------