| CHANGE REQUEST |
| --- |
| Meeting:* | TST 26.1 |
| Source:* | KETI (Korea Electronics Technology Institute) |
| Date:* | 2017-01-06 |
| Contact:* | Ting Martin Miao, KETI, novamartin@keti.re.kr |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 V0.1.4 |
| Clauses/Sub Clauses* | 7.2.2.4 Group Management (GMG) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Several GMG testcases contain incorrect response message. We propose to clarify those GMG testcases.

- TP/oneM2M/CSE/GMG/BV/011

- TP/oneM2M/CSE/GMG/BV/016

- TP/oneM2M/CSE/GMG/BV/018

### -----------------------Start of change 1-------------------------------------------

## 7.2.2.4		Group Management (GMG)

##### TP/oneM2M/CSE/GMG/BV/011

| TP Id | TP/oneM2M/CSE/GMG/BV/011 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during the creation of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is SET_MIXED. |
| Reference | TS-0001 10.2.7.2, TS-0004 7.4.14.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS allowing a child resource type <group> and the AE having privileges to perform CREATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS having resourceType attribute RESOURCE_TYPE_1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to <group> and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS memberType attribute set to RESOURCE_TYPE_2 consistencyStrategy attribute set to SET_MIXED } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2001 (CREATED) Content set to <group> resource containing memberTypeValidated attribute set to TRUE memberType attribute set to MIXED } | IUT ( AE |

##### TP/oneM2M/CSE/GMG/BV/016

| TP Id | TP/oneM2M/CSE/GMG/BV/016 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during an UPDATE of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is SET_MIXED. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 memberType attribute set to RESOURCE_TYPE_1 memberTypeValidated attribute set to TRUE consistencyStrategy attribute set to SET_MIXED and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2004 (UPDATED) Content set to <group> resource containing memberTypeValidated attribute set to TRUE memberType attribute set to MIXED } | IUT ( AE |

##### TP/oneM2M/CSE/GMG/BV/018

| TP Id | TP/oneM2M/CSE/GMG/BV/018 |
| --- | --- |
| Test objective | Check that the IUT handles unsuccessful validation of the resource type during the creation of the <group> resource when memberType attribute is not ‘mixed’ and the consistencyStrategy attribute is ABANDON_GROUP. |
| Reference | TS-0001 10.2.7.4, TS-0004 7.4.14.2.4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a resource at TARGET_RESOURCE_ADDRESS of type <group> containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1 memberType attribute set to RESOURCE_TYPE_1 memberTypeValidated attribute set to TRUE consistencyStrategy attribute set to ABANDON_GROUP and the AE having privileges to perform UPDATE operation on the TARGET_RESOURCE_ADDRESS and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_1 having resourceType attribute RESOURCE_TYPE_1 and the IUT having a resource at MEMBER_RESOURCE_ADDRESS_2 having resourceType attribute RESOURCE_TYPE_2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives an valid UPDATE request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content set to <group> resource containing memberIDs attribute set to MEMBER_RESOURCE_ADDRESS_1, MEMBER_RESOURCE_ADDRESS_2 } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set 2002 (DELETED) } | IUT ( AE |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

TRUE??

TS-0004 7.4.13.2.1 CREATE

If the consistencyStrategy of the <group> resource is SET_ MIXED then set the memberType attribute of the <group> resource to "MIXED" and create the <group> resource and the memberTypeValidated attribute shall be set to TRUE.

True?

The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully. If a member validation for memberType of the <group> resource is unsuccessful, then the Hosting CSE shall perform the following:

- If the consistencyStrategy of the <group> resource is ABANDON_GROUP then the request shall be rejected with a Response Status Code indicating "GROUP_MEMBER_TYPE_INCONSISTENT" error.

- If the consistencyStrategy of the <group> resource is ABANDON_ MEMBER then remove the inconsistent members and update the <group> resource and the memberTypeValidated attribute shall be set to TRUE.

- If the consistencyStrategy of the <group> resource is SET_ MIXED then set the memberType attribute of the <group> resource to "MIXED" and update the <group> resource and the memberTypeValidated attribute shall be set to TRUE.