| Input Contribution |
| --- |
| Meeting ID* | TST#27 |
| Title:* | Monitoring_procedures_of_TR-0034 |
| Source:* | Shane He, shane.he@nokia.com |
| Uploaded Date:* | 2017-02-07 |
| Document(s) Impacted* | TR-0034 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to add context and figure of clause 7.1 of TR-0034 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 7	Procedures and call flows

## 7.1	Monitoring procedures

In this scenario, user can use the smartphone application to monitor the temperature data of applications embedded in Sensor#1 and Sensor#2. Furthermore, the actuator application embedded in Actuator#1 also can be managed by the smartphone application. To realize these functions, the deployment of the oneM2M standard in the present use case requires procedures that are classified as follows:

- Registration: the current procedure contains sensor and actuator applications registration, gateway, and smartphone application registration.

- Initial resource creation: the current procedure contains container resource creation.

- Discovery and retrieval: the current procedure contains discovery and retrieval of sensor applications using resource identities through a smartphone application .

- In some use cases, if the actuator application embedded in Actuator#1 is non server capable, which means it cannot be notified by the gateway (MN-CSE). oneM2M defines the <pollingChannel> resource which represents a channel that can be used for such situation [i.2]. The clause 7 also provides relevant procedures and call flows using <pollingChannel> resource:

- PollingChannel resource creation: The current procedure contains pollingChannel resource creation.

- Actuator switch on/off: the actuator application that is discovered by and connected to the smartphone application is able to be switched via polling channel.

# End of the text