| Input Contribution |
| --- |
| Meeting ID* | TST#27 |
| Title:* | Actuator_switch_call_flows_of_TR-0034 |
| Source:* | Shane He, shane.he@nokia.com |
| Uploaded Date:* | 2017-02-07 |
| Document(s) Impacted* | TR-0034 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to add context and figure of clause 7.2 of TR-0034 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### 7.2.4 	Actuator switch

In this example, if the temperature indicated by sensors is out of th range of normal. For example, there maybe a fire disaster or other possibilities. The Actuator is able to be controlled remotely through the smartphone application accessing the oneM2M service platform, in order to achieve some safety procedures.

Actuator#1 are controlled remotely by a human user through a smartphone application (ADN-AE4). A call flow for remote control is depicted in figure 7.2.4 and the steps are ordered as follows:

- The ADN-AE3 sends request to the gateway in order to retrieve requests, which is marked as REQ1.

- When the user updates the actuator state on the smartphone, the ADN-AE4 generates a request representing a new state under the targeted container of ADN-AE3 stored in the MN-CSE, which is marked as REQ2.

- The gateway (MN-CSE) internaly processes request and response to the ADN-AE3 with the REQ2 in content parameter.

- After processing, the ADN-AE3 sends request REQ3 to the gateway (MN-CSE) carrying the response “RESP2” in the content parameter.

- The gateway (MN-CSE) responds to the smartphone application (ADN-AE4), to indicate that the status of actuator is successfully updated.

Figure 7.2.4: Actuator remote control phase call flows

# End of the text