| Input Contribution |
| --- |
| Meeting ID* | TST 27 |
| Title:* | TR-0037-Smart Farm Example using MQTT Binding Function Call Flow – Automated Actuation Enhancement |
| Source:* | Ting Martin Miao, KETI, martin.miao@keti.re.kr |
| Uploaded Date:* | 2017-Feb-13 |
| Document(s) Impacted* | TR-0037 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes to define function call flows for subscribing an interested resources.

## -----------------------Start of change 1--------------------------------------------

## 7.4	Automated Actuation Enhancement

Actutors deployed in the farm control use case can be actuated by many ways, e.g. by subscription and notification mechanism or by periodically polling way. In this use case, we apply the subscription and notification mechanism to implement the automated actuation services and we also take the advantage of publish and forwarding mechanism in MQTT protocol.

In oneM2M architecture perspective, authenticated users have to subscribe to the target resource from which notification is expected to be send when certain notification criterias meet the pre-defined rules. In the farm control use case, the measured quantity from sensors deployed in the farm will be used as a stimulus to trigger certain notification events. Those measured quantities are normally stored in a container resource in a node which hosts an AE (ADN-AE). Therefore, subscription to the container resource is a normal way to monitor the measurement quantity as well as actuating purposes.

All those subscription request to tareget resource can only be done by the authenticated users such as farm administrators.

Figure 7.5- 1 Subscription Resource Creation Flows

## -----------------------End of change 1--------------------------------------------