| CHANGE REQUEST |
| --- |
| Meeting:* | TST 27 |
| Source:* | TTA |
| Date:* | 2017-02-14 |
| Contact:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Sookhyun Jeon, TTA, shjeon@tta.or.kr |
| Reason for Change/s:* | To add TDs for latest, oldest retrieve. |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0013-V.1.3.0 |
| Clauses/Sub Clauses* | 8.1.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: TST-2017-0047) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to add Test Descriptions for latest and oldest retrieve operation.

### -----------------------Start of change 1-------------------------------------------

### 8.1.5	ContentInstance Management

#### 8.1.5.7	<latest> ContentInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_60 |
| Objective: | AE retrieves a <latest> resource of a <container> and the Registrar CSE points a latest <contentInstance> among the existing contentInstances to the <latest> resource of the <container> |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.22.1 TS-0004 [2], clause 7.4.27.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a contentInstance resource <contentInstance> as child resource of <container> resource |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Retrieve Request for a <latest> |
| 2 | Mca | PRO Check Primitive | op = 2 (Retrieve) to = {CSEBaseName}/URI of <latest> resource fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}/URI of <latest> resource Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <latest> resource oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/< AE-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName}/URI of <latest> resource fr = AE-ID rqi = (token-string) pc = empty |
| 3 | Mca | PRO Check Primitive | rsc =2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of latest <contentInstance> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of latest <contentInstance> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 (OK) oneM2M-RSC: 2000(OK) oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of latest <contentInstance> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc 2000(OK) rqi = (token-string) same as received in request message pc = Serialized representation of latest <contentInstance> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.5.8 <oldest> ContentInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_61 |
| Objective: | AE retrieves a <oldest> resource of a <container> and the Registrar CSE points a oldest <contentInstance> among the existing contentInstances to the <oldest> resource of the <container> |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.23.1 TS-0004 [2], clause 7.4.28.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a contentInstance resource <contentInstance> as child resource of <container> resource |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a Retrieve Request for a <oldest> |
| 2 | Mca | PRO Check Primitive | op = 2 (Retrieve) to = {CSEBaseName}/URI of <oldest> resource fr = AE-ID rqi = (token-string) pc = empty |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}/URI of <oldest> resource Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/URI of <oldest> resource oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: empty |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/< AE-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName}/URI of <oldest> resource fr = AE-ID rqi = (token-string) pc = empty |
| 3 | Mca | PRO Check Primitive | rsc =2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of oldest <contentInstance> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of oldest <contentInstance> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 (OK) oneM2M-RSC: 2000(OK) oneM2M-RQI: (token-string) same as received in request message Content-format: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Payload: Serialized representation of oldest <contentInstance> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/resp/< AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc 2000(OK) rqi = (token-string) same as received in request message pc = Serialized representation of oldest <contentInstance> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### -----------------------End of change 1---------------------------------------------