| Input Contribution |
| --- |
| Meeting ID* | TST#27 |
| Title:* | Update on IN profile |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com |
| Date:* | 2017-02-13 |
| Input related to* | WI-0055 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0025 |
| Decision requested or recommendation:* | Incooperate the contribution to TS-0025 if agreed. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 7.6	IN Profile 5

### 7.6.1	Profile description

oneM2M provides serveral logical entity concepts called ‘Node’ to explain oneM2M Architecture in TS-0001. And from the descriptions about the node types indicates some examples that particular node could match with pyshical oneM2M devices (e.g. ADN -> constrainted oneM2M Device). But for the oneM2M device developers, may require more detail information to design and implement physical devices.

This IN Profile 1 defines set of common features which could be used for server device type of oneM2M services.

Editor’s Node: TBD. Has to be updated.

### 7.6.2	Profile usage examples

IN Profile 1 could be the common profile of oneM2M devices like service server etc. And also this profile could be used independently when developers want to implement oneM2M device with special functions.

Editor’s Node: TBD. Has to be updated.

### 7.6.3	Fundamental feature sets

Table 7.6.3-1: Fundamental feature set for IN Profile 1

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| GEN | GE/GEN/00001 | At least one | Support one of the bindings |
| GEN | GE/GEN/00002 | At least one | Support one of the serializations |
| GEN | CE/GEN/00001 | CE/GEN/00001/00001 | Support Unstructured resource identifier |
|  |  | CE/GEN/00001/00002 | Support Structured resource identifier |
| GEN | CE/GEN/00002 | CE/GEN/00002/00001 | Support blocking request |
| REG | CE/REG/00001 | CE/REG/00001/00001 | Support <CSEBase> resource. |
|  |  | CE/REG/00001/00002 | Support the cseType attribute of <CSEBase> |
|  |  | CE/REG/00001/00003 | Support the nodeLink attribute of <CSEBase> |
|  | CE/REG/00002 | CE/REG/00002/00001 | Support <AE> resource |
|  |  | CE/REG/00002/00002 | AE registration without pre-assigned AE-ID in the registration request. Possible cases are: The request includes AE-ID Stem as ‘C’. The request includes AE-ID Stem as ‘S’. The request does not include AE-ID Stem |
|  |  | CE/REG/00002/00003 | Support the labels attribute of <AE> resource |
|  |  | CE/REG/00002/00004 | Support the applicationName attribute of <AE> resource |
|  |  | CE/REG/00002/00005 | Support the pointOfAccess attribute of <AE> resource |
|  |  | CE/REG/00002/00006 | AE registration with pre-assigned AE-ID |
|  | CE/REG/00004 | CE/REG/00004/00001 | Support <remoteCSE> resource with attributes multiplicity equals 1[1] |
|  |  | CE/REG/00004/00002 | Support the labels attribute of <remoteCSE> resource |
|  |  | CE/REG/00004/00003 | Support the cseType attribute of <remoteCSE> resource |
|  |  | CE/REG/00004/00004 | Support the pointOfAccess attribute of <remoteCSE> resource |
|  |  | CE/REG/00004/00005 | Support the nodeLink attribute of <remoteCSE> resource |
| DMR | CE/DMR/00001 | CE/DMR/00001/00001 | Support <container> resource with attributes multiplicity equals 1[1] |
|  |  | CE/DMR/00001/00002 | Support the labels attribute of <container> resource |
|  |  | CE/DMR/00001/00003 | Support the creator attribute of <container> resource |
|  |  | CE/DMR/00001/00004 | Support the maxNrOfInstances attribute of <container> resource |
|  |  | CE/DMR/00001/00005 | Support the maxByteSize attribute of <container> resource |
|  |  | CE/DMR/00001/00006 | Support the maxInstanceAge attribute of <container> resource |
|  | CE/DMR/00002 | CE/DMR/00002/00001 | Support <contentInstance> resource with attributes multiplicity equals 1[1] |
|  |  | CE/DMR/00002/00002 | Support the labels attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00003 | Support the creator attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00004 | Support the contentInfo attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00005 | Support the contentRef attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00006 | Retrieve and Delete of latest <contentInstance> resource by <latest> virtual resource |
|  |  | CE/DMR/00002/00007 | Retrieve and Delete of oldest <contentInstance> resource by <oldest> virtual resource |
| DMG | CE/DMG/00001 | CE/DMG/00001/00001 | Support <node> resource with attributes multiplicity equals 1[1] |
|  |  | CE/DMG/00001/00002 | Support the labels attribute of <node> resource |
|  |  | CE/DMG/00001/00003 | Support the hostedCSELink attribute of <node> resource |
| SUB | CE/SUB/00001 | CE/SUB/00001/00001 | The Support of <subscription> resource with attributes multiplicity equals 1[1] |
|  |  | CE/SUB/00001/00002 | Support the labels attribute of <subscription> resource. |
|  |  | CE/SUB/00001/00003 | Support the creator attribute of <subscription> resource |
|  |  | CE/SUB/00001/00004 | Support the subscriberURI attribute of <subscription> resource |
|  | CE/SUB/00004 | CE/SUB/00004/00001 | Notify the address indicated in notificationURI with notification elements multiplicity equals 1[2] |
|  |  | CE/SUB/00004/00002 | Notify with notificationEvent/representation set in the notification |
|  |  | CE/SUB/00004/00003 | Notify with creator set in the notification |
| SEC | CE/SEC/00001 | CE/SEC/00001/00001 | Support <accessControlPolicy> resource with attributes multiplicity equals 1[1] |
|  |  | CE/SEC/00001/00002 | Support the labels attribute of <accessControlPolicy> resource |
|  | CE/SEC/00002 | CE/SEC/00002/00001 | Support accessControlPolicyIDs attribute for <resource> that the Implementation supports. |
|  |  | CE/SEC/00002/00002 | Support access control decision and enforcement making on the Hosting CSE |

### 7.6.4	Extendable feature sets

Editor’s Node: TBD. Has to be updated.

Table 7.6.3-1: Extendable feature set for IN Profile 1

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| DIS | CE/DIS/00001 | CE/DIS/00001/00001 | Support the Discovery request with filterUsage equals to “Discovery” |
|  |  | CE/DIS/00001/00002 | Support discovery with filterCriteria (createdBefore, createdAfter, modifiedSince, unmodifiedSince, stateTagSmaller, stateTagBigger, expireBefore, expireAfter, labels, resourceType, sizeAbove, sizeBelow, contentType, limit, attribute) |
|  |  | CE/DIS/00001/00003 | Support discovery with filterCriteria (level, offset) |
|  |  | CE/DIS/00001/00004 | Support discovery with content filter (contentFilterSyntax, contentFilterQuery of filterCriteria) |
|  |  | CE/DIS/00001/00005 | Support discovery with filterCriteria (filterOperation) |
| GMG |  | CE/GMG/00001/00001 | Support the <group> resource with attributes multiplicity equals 1[1] |
|  |  | CE/GMG/00001/00002 | Support the labels attribute of <group> resource |
|  |  | CE/GMG/00001/00003 | Support the creator attribute of <group> resource |
|  |  | CE/GMG/00001/00004 | Support the groupName attribute of <group> resource |
|  |  | CE/GMG/00002/00001 | Support the memberTypeValidated attribute of <group> resource |
|  |  | CE/GMG/00002/00002 | Support the validation of member’s resource type and set the memberTypeValidated as well as the procedure to update the group according to consistencyStrategy |
|  |  | CE/GMG/00002/00003 | Support the consistencyStrategy attribute of <group> resource |
|  |  | CE/GMG/00003/00001 | Fan out of request to all members and aggregate member responses |
|  |  | CE/GMG/00003/00002 | Create sub group resource in case multiple members belong to same member CSE |
|  |  | CE/GMG/00003/00003 | Create <subscription> resource via group without aggregating notifications |
|  |  | CE/GMG/00003/00004 | Create <subscription> resource via group and aggregate notifications |
|  |  | CE/GMG/00003/00005 | Support the membersAccessControlPolicyIDs attribute of <group> resource |
| DMG | CE/DMG/00002 | CE/DMG/00002/00001 | Support <mgmtObj> resource with attributes multiplicity equals 1[1] |
|  |  | CE/DMG/00002/00002 | Support the labels attribute of <mgmtObj> resource |
|  |  | CE/DMG/00002/00003 | Support the description attribute of <mgmtObj> resource |
|  |  | CE/DMG/00002/00004 | Support the mgmtLink attribute of <mgmtObj> resource |
|  | CE/DMG/00003 | CE/DMG/00003/00001 | Support the [software] specialization attributes multiplicity equals 1[1] |
|  |  | CE/DMG/00003/00002 | Support the activate attribute of [software] resource |
|  |  | CE/DMG/00003/00003 | Support the deactivate attribute of [software] resource |
|  |  | CE/DMG/00003/00004 | Support the activeStatus attribute of [software] resource |
|  | CE/DMG/00004 | CE/DMG/00004/00001 | Support the [firmware] specialization attributes multiplicity equals 1[1] |
|  | CE/DMG/00005 | CE/DMG/00005/00001 | Support the [deviceInfo] specialization attributes multiplicity equals 1[1] |
|  | CE/DMG/00006 | CE/DMG/00006/00001 | Support [deviceCapability] specialization attributes multiplicity equals 1[1] |
|  |  | CE/DMG/00006/00002 | Support the enable attribute of [deviceCapability] resource |
|  |  | CE/DMG/00006/00003 | Support the disable attribute of [deviceCapability] resource |
|  | CE/DMG/00007 | CE/DMG/00007/00001 | Support [reboot] specialization attributes multiplicity equals 1[1] |
|  | CE/DMG/00008 | CE/DMG/00008/00001 | Support [memory] specialization attributes multiplicity equals 1[1] |
|  | CE/DMG/00009 | CE/DMG/00009/00001 | Support the [battery] specialization attributes multiplicity equals 1[1] |
|  | CE/DMG/00010 | CE/DMG/00010/00001 | Support [eventLog] specialization attributes multiplicity equals 1[1] |
|  | CE/DMG/00011 | CE/DMG/00011/00001 | Support [areaNwkInfo] specialization attributes multiplicity equals 1[1] |
|  | CE/DMG/00012 | CE/DMG/00012/00001 | Support [areaNwkDeviceInfo] specialization attributes multiplicity equals 1[1] |
|  |  | CE/DMG/00012/00002 | Support the sleepInterval attribute of [areaNwkDeviceInfo] resource |
|  |  | CE/DMG/00012/00003 | Support the sleepDuration attribute of [areaNwkDeviceInfo] resource |
|  |  | CE/DMG/00012/00004 | Support the status attribute of [areaNwkDeviceInfo] resource |
|  | CE/DMG/00013 | CE/DMG/00013/00001 | Support the objectIDs attribute of <mgmtObj> resource |
|  |  | CE/DMG/00013/00002 | Support the objectPaths attribute of <mgmtObj> resource |
|  |  | CE/DMG/00013/00003 | Support the mgmtLink attribute of <mgmtObj> resource |