| CHANGE REQUEST |
| --- |
| Meeting:* | TST 27 |
| Source:* | KETI (Korea Electronics Technology Institute) |
| Date:* | 2017-02-14 |
| Contact:* | Ting Martin Miao, KETI, martin.miao@keti.re.kr |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0037 v0.0.2 |
| Clauses/Sub Clauses* | Section 5 Design of the Use Case |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Clarify the use case in terms of functions to be implemented in components deployed in the use case.

### ------------------------------Start of change 1-------------------------------------------

# 5	Design of the Use Case

## 5.1	Introduction

This user guide demonstrates how to implement a smart farm control use case that deploys different sensors to collect environment measurement data, and actuators to trigger some kind of IoT services by remotely human intervention using IoT applications. All devices involved in the smart farm control scenario leverage oneM2M common services functionalities.

The smart farm control use case is designed to implement functions as following:

- Remote environment measurement monitoring and remote actuators controlling using IoT applications by applying MQTT subscription and notification mechanism.

- Registration of sensors, actuators, and farm gateway application into the farm gateway as well as the farm gateway and IoT applications into a cloud server.

- Discovery of oneM2M resources representing sensors and actuators in farm gateway using IoT applications.

An overview of the smart farm control use case is depicted in Figure 5.1-1, where compound sensors with sensing data of temperature, humidity and CO2, illumination sensors, soil moisture and Photosynthetic Photon Flux Density (PPFD) sensors as well as actuators used to trigger machines deployed in the farm such as fans, air conditioner, sprinkler, roof cover controller and irrigation and nutrient management system etc. Those deployed sensors and actuators are connected to a farm gateway which is capable to communicate with a oneM2M cloud server. In addition, IoT applications that interface directly with the cloud server are responsible for monitoring crops growing environment and controlling farm machines remotely. A farm gateway application is responsible for communication with the farm gateway. The subscription and notification mechnisms are applied to implement the remote farm monitoring and controlling services.

Figure 5.1-1 Overview of smart farm control use case

## 5.2	Modelling Components

IoT devices involved in the use case are modelled to map to entity types defined in oneM2M TS-0001. The modelling of those IoT devices are as following:

- Sensors such as compound sensors,  illumination sensors, soil moisture and PPFD sensors each host an Application Dedicated Nodes with embedded application entity (ADN-AE) for collecting farm environment measurements and uploading the data into a farm gateway.

- Actuators such as fans, air conditioner, sprinkler, and roof cover controller each host an Application Dedicated Nodes with embedded application entity (ADN-AE).

- The farm gateway hosts a Middle Nodes with embedded Common Service Entity (MN-CSE) which provides both interface with sensors/actuators and interface with the cloud server.

- IoT cloud server hosts an oneM2M Infrastructure Node Common Service Entity (IN-CSE) which implements all the functionalities defined in oneM2M specifications such as registration, data management, subscription and notification etc.

- IoT applications each host an Application Dedicated Nodes with embedded application entity (ADN-AE) which interface directly with the cloud server to request interested resources exposed by the farm gateway.

- The gateway application hosts an application entity (MN-AE) that resides on a Middle Node with embedded Common Service Entity (MN-CSE), which interfaces with the farm gateway (MN-CSE).

### ------------------------------End of change 1-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?