| CHANGE REQUEST |
| --- |
| Meeting:* | TST#27 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2017-2-15 |
| Contact:* | Jiaxin Yin, yinjiaxin@huawei.com |
| Reason for Change/s:* |  |
| CR against: Release* | Release One |
| CR against: WI* | Active WI-0055 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0025 |
| Clauses/Sub Clauses* | 7.2.3, 7.2.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### -----------------------Start of change 1-------------------------------------------

# 5	Introduction of product profile

5.1	Introduction

Product profile is the specification with a collection of profiles of implementation that is claimed to comply to oneM2M standard. Differentiated by the different type of the implementation, different features may be supported. The profiling work is to collect features that is eligible to one certain type of implementation together. For the purpose of interoperability, vendors or service providers of the same type of implementation shall support the common set of features.

TS-0031 includes the abstracted features that are provided by oneM2M standards. The Features are grouped into Feature Sets and then to Functions according to the service the feature is deliver. All Features in product profile specification are defined in TS-0031.

Each Feature is associated with multiple Test Purposes for conformance testing. The Test Purposes are essential for the Feature that all implementations shall pass the corresponding Test Purpose if claimed to support the Feature.

For each profile in this specification, a description of the profile and an example is needed to help understanding the type of implementation so that companies who intends to implement oneM2M can choose one of the profiles out of this specification to assist the designing and developing of the product. The profile with specified Features further assists the testing and certification as each Feature is associated with multiple Test Purposes.

Each profile comprises a fundamental feature set and an extendable feature set. The fundamental feature set includes Features that shall be implemented if claimed to comply with the profile. The Features shall be validated during testing and certification. The extendable feature set includes Features that are recommended to be implemented. These Features are validated on a requirement basis. The implementation may choose to support these Features and require the Certification Body to test these Features.

5.2	Definition of Product Profiles

Each Profile has an unique profile identifier. Profiles shall be based on real market product that complies to oneM2M such as platform, gateway or device. One product shall comply to at least one profile. One product may also comply to multiple profiles. In this case, the product shall support all Features from the fundamental feature set from all the profiles. All corresponding Test Purposes of the Features shall be tested in order to be certified.

There may be multiple products in the market certified against one profile.

New Profiles may be generated by moving Features from the extendable feature set to fundamental feature set of the existing Profile. In this case, the new Profile is the super set of the original profile. All services deployed against the original Profile can be deployed against the new Profile as well. The original Profile may be upgraded to the new Profile (the original Profile is deleted and superseded by the new Profile) if oneM2M agrees and all companies with products certified against the orginal agrees to upgrade their product to comply with the new Profile.

New Profiles may be generated by updating Features of the Profile. Features may be modified between releases of oneM2M. As a result, Test Purposes related to the testing of the Feature may be added or changed. Therefore resulting in new Profiles. The orginal Profile may be upgraded following the same principle.

Stale Profiles may be removed. No new product claims to comply with the Profile and the Profile is superseded by other Profiles.

5.3	Addition of Features to Profile

Addition of Feature to Profile may be adding new Feature or moving Features from extendable feature set to fundamental feature set. The Feature shall be defined in TS-0031 and have a Feature ID. The Feature may be added to an existing Profile to form a new Profile or be merged into an existing Profile. If the Feature is to be merged into an existing Profile, it shall be required to check if companies that have products comply to the Profile agrees to upgrade their product.

Features added to a Profile shall be testable. There shall be Test Purposes corresponding to the Feature defined.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?