| CHANGE REQUEST |
| --- |
| Meeting:* | TST#27 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-11-23 |
| Contact:* | Jiaxin Yin, yinjiaxin@huawei.com |
| Reason for Change/s:* | The profile for MN |
| CR against: Release* | Release One |
| CR against: WI* | Active WI-0055 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0025 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The profile for MN.

### -----------------------Start of change 1-------------------------------------------

## 7.x	Gateway as MN

### 7.x.1	Profile description

The profile defines gateways that may support multiple different area network technologies and connect devices from the corresponding area networks. The devices may be oneM2M defined ADNs,  ASNs or NoDNs which are not defined by oneM2M. The gateway hosts resources to enforce common services that devices in the area network may utilize the enable local services without the dependency of the platform and the wide area network.

### 7.x.2	Profile usage examples

Home gateways deployed in the home for smart home:

Sensors, actuators and home appliances are connected with the home gateway. Applications can be connected through the platfrom to access the smart home service as well as applications can be directly connected with the gateway to do the same thing.

Head unit in connected vehicles:

Sensors and actuators in the car are connected with the head unit. The sensed data and control command are reported to delivered through the head unit. Applications may access the head unit and monitor the car state via the platform. Applications may also access the head unit once connected directly with the head unit via area network such as Wifi or Bluetooth.

### 7.x.3	Fundamental feature sets

Table 7.x.3-1: Fundamental feature sets for gateway as MN

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| GEN | CE/GEN/00001 | CE/GEN/00001/00001 | Unstructured resource id |
|  |  | CE/GEN/00001/00002 | Structured resource id |
|  | CE/GEN/00002 | CE/GEN/00002/00001 | Support blocking request |
| REG | CE/REG/00001 | CE/REG/00001/00001 | Support <CSEBase> resource with attributes multiplicity equals 1[1]. |
|  |  | CE/REG/00001/00002 | Support the cseType attribute of <CSEBase> resource |
|  |  | CE/REG/00001/00003 | Support the nodeLink attribute of <CSEBase> resource. This is dependent on the feature set for <node> resource. |
|  | CE/REG/00002 | CE/REG/00002/00001 | Support <AE> resource with attributes multiplicity equals 1[1] |
|  |  | CE/REG/00002/00002 | AE registration without pre-assigned AE-ID in the registration request. Possible cases are: The request includes AE-ID Stem as ‘C’. The request includes AE-ID Stem as ‘S’. The request does not include AE-ID Stem |
|  |  | CE/REG/00002/00003 | Support the labels attribute of <AE> resource |
|  |  | CE/REG/00002/00004 | Support the applicationName attribute of <AE> resource |
|  |  | CE/REG/00002/00005 | Support the pointOfAccess attribute of <AE> resource |
|  |  | CE/REG/00002/00006 | AE registration with pre-assigned AE-ID |
|  | CE/REG/00004 | CE/REG/00004/00001 | Support <remoteCSE> resource with attributes multiplicity equals 1[1] |
|  |  | CE/REG/00004/00002 | Support the labels attribute of <remoteCSE> resource |
|  |  | CE/REG/00004/00003 | Support the cseType attribute of <remoteCSE> resource |
|  |  | CE/REG/00004/00004 | Support the pointOfAccess attribute of <remoteCSE> resource |
|  |  | CE/REG/00004/00005 | Support the nodeLink attribute of <remoteCSE> resource |
|  | CE/REG/00005 | CE/REG/00005/00001 | The Creation with <remoteCSE> resource for CSE registration with mandatory attributes[2] for Create and locally create <remoteCSE> that represents the Regstree CSE |
|  |  | CE/REG/00005/00002 | Create the <remoteCSE> with resourceName attribute |
|  |  | CE/REG/00005/00003 | Create the <remoteCSE> with expirationTime attribute |
|  |  | CE/REG/00005/00004 | Create the <remoteCSE> with labels attribute |
|  |  | CE/REG/00005/00005 | Create the <remoteCSE> with cseType attribute |
|  |  | CE/REG/00005/00006 | Create the <remoteCSE> with pointOfAccess attribute |
|  |  | CE/REG/00005/00007 | Create the <remoteCSE> with nodeLink attribute |
|  |  | CE/REG/00005/00008 | Update the <remoteCSE> with labels |
|  |  | CE/REG/00005/00009 | Update the <remoteCSE> with expirationTime |
|  |  | CE/REG/00005/00010 | Update the <remoteCSE> with pointOfAccess attribute |
|  |  | CE/REG/00005/00011 | Update the <remoteCSE> with requestReachability |
|  |  | CE/REG/00005/00012 | Update the <remoteCSE> with nodeLink attribute |
|  |  | CE/REG/00005/00013 | Delete the <remoteCSE> resource on the Registrar, also delete the <remoteCSE> resource on the Registree |
|  |  | CE/REG/00005/00014 | Retrieve the <remoteCSE> resource |
| DMR | CE/DMR/00001 | CE/DMR/00001/00001 | Support <container> resource with attributes multiplicity equals 1[1] |
|  |  | CE/DMR/00001/00002 | Support the labels attribute of <container> resource |
|  |  | CE/DMR/00001/00003 | Support the creator attribute of <container> resource |
|  |  | CE/DMR/00001/00004 | Support the maxNrOfInstances attribute of <container> resource |
|  |  | CE/DMR/00001/00005 | Support the maxByteSize attribute of <container> resource |
|  |  | CE/DMR/00001/00006 | Support the maxInstanceAge attribute of <container> resource |
|  | CE/DMR/00002 | CE/DMR/00002/00001 | Support <contentInstance> resource with attributes multiplicity equals 1[1] |
|  |  | CE/DMR/00002/00002 | Support the labels attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00003 | Support the creator attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00004 | Support the contentInfo attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00005 | Support the contentRef attribute of <contentInstance> resource |
|  |  | CE/DMR/00002/00006 | Retrieve and Delete of latest <contentInstance> resource by <latest> virtual resource |
|  |  | CE/DMR/00002/00007 | Retrieve and Delete of oldest <contentInstance> resource by <oldest> virtual resource |
| SUB | CE/SUB/00001 | CE/SUB/00001/00001 | The Support of <subscription> resource with attributes multiplicity equals 1[1] |
|  |  | CE/SUB/00001/00002 | Support the labels attribute of <subscription> resource. |
|  |  | CE/SUB/00001/00003 | Support the creator attribute of <subscription> resource |
|  |  | CE/SUB/00001/00004 | Support the subscriberURI attribute of <subscription> resource |
|  | CE/SUB/00004 | CE/SUB/00004/00001 | Notify the address indicated in notificationURI with notification elements multiplicity equals 1[2] |
|  |  | CE/SUB/00004/00002 | Notify with notificationEvent/representation set in the notification |
|  |  | CE/SUB/00004/00003 | Notify with creator set in the notification |
| SEC | CE/SEC/00001 | CE/SEC/00001/00001 | Support <accessControlPolicy> resource with attributes multiplicity equals 1[1] |
|  |  | CE/SEC/00001/00002 | Support the labels attribute of <accessControlPolicy> resource |
|  | CE/SEC/00002 | CE/SEC/00002/00001 | Support accessControlPolicyIDs attribute for <resource> that the Implementation supports. |
|  |  | CE/SEC/00002/00002 | Support access control decision and enforcement making on the Hosting CSE |

### 7.x.4	Extendable feature sets

Table 7.x.4-1: Extendable feature set for gateway as MN

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| DIS | CE/DIS/00001 | CE/DIS/00001/00001 | Support the Discovery request with filterUsage equals to “Discovery” |
|  |  | CE/DIS/00001/00002 | Support discovery with filterCriteria (createdBefore, createdAfter, modifiedSince, unmodifiedSince, stateTagSmaller, stateTagBigger, expireBefore, expireAfter, labels, resourceType, sizeAbove, sizeBelow, contentType, limit, attribute) |
|  |  | CE/DIS/00001/00003 | Support discovery with filterCriteria (level, offset) |
|  |  | CE/DIS/00001/00004 | Support discovery with content filter (contentFilterSyntax, contentFilterQuery of filterCriteria) |
|  |  | CE/DIS/00001/00005 | Support discovery with filterCriteria (filterOperation) |
| GMG | CE/GMG/00001 | CE/GMG/00001/00001 | Support the <group> resource with attributes multiplicity equals 1[1] |
|  |  | CE/GMG/00001/00002 | Support the labels attribute of <group> resource |
|  |  | CE/GMG/00001/00003 | Support the creator attribute of <group> resource |
|  |  | CE/GMG/00001/00004 | Support the groupName attribute of <group> resource |
|  | CE/GMG/00002 | CE/GMG/00002/00001 | Support the memberTypeValidated attribute of <group> resource |
|  |  | CE/GMG/00002/00002 | Support the validation of member’s resource type and set the memberTypeValidated as well as the procedure to update the group according to consistencyStrategy |
|  |  | CE/GMG/00002/00003 | Support the consistencyStrategy attribute of <group> resource |
|  | CE/GMG/00003 | CE/GMG/00003/00001 | Fan out of request to all members and aggregate member responses |
|  |  | CE/GMG/00003/00002 | Create sub group resource in case multiple members belong to same member CSE |
|  |  | CE/GMG/00003/00003 | Create <subscription> resource via group without aggregating notifications |
|  |  | CE/GMG/00003/00004 | Create <subscription> resource via group and aggregate notifications |
|  |  | CE/GMG/00003/00005 | Support the membersAccessControlPolicyIDs attribute of <group> resource |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?