| CHANGE REQUEST |
| --- |
| Meeting:* | TST 27 |
| Source:* | Convida |
| Date:* | 2017-02-15 |
| Contact:* | Bob Flynn, Flynn.Bob@convidawireless.com |
| Reason for Change/s:* | To add TDs for CSE Registration. |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V.0.1.6 |
| Clauses/Sub Clauses* | 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

| CSE registration | CSE registration operation in receiver role, only using mandatory attributes. | ETSI | Covered in this contribution |
| --- | --- | --- | --- |
|  | CSE registration operation in receiver role, using optional attributes. | ETSI | Covered in this contribution. See comments below |
| CSE deregistration | CSE deregistration operation in receiver role. | ETSI | Covered in this contribution |
| <remoteCSE> resource management | Retrieve operation in receiver role. | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, only with mandatory attributes | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘accessControlPolicyIDs’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘expirationTime’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘labels’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘announceTo’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘announcedAttribute’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘pointOfAccess’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘M2M-Ext-ID’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘Trigger-Recipient-ID’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘requestReachability’ | ETSI | Basic DMR test cases??? |
|  | Update operation in receiver role, using optional attribute ‘nodeLink’ | ETSI | Basic DMR test cases??? |

This contribution proposes to add Test Descriptions for CSE Registration.

In the introduction section, I renumber “OLD” requirement IDs to align with new values in our spreadsheet.

|  | REQ-0001-10142 | Basic CREATE <remoteCSE> - check if covered |
| --- | --- | --- |
|  | REQ-0001-10200 | allow “unknown” CSE that is “Authenticated” |
|  | REQ-0001-10201 | REQ-0001-10138, REQ-0001-10139, REQ-0001-10140 |
|  | REQ-0001-10202 | Repeat common create operations. Is this covered in existing TPs? |
|  | REQ-0001-10143 | Test needed to see if originator creates local <remoteCSE> |
|  | REQ-0001-10144 | I added another sentence to the requirement. Uses a “MAY” statement. Should it be made into a “shall” for CSE consistency? ARC CR? Must perform “proper” request message. |
|  | REQ-0001-10145 | If REQ-0001-10144 is done, then this must be done as well. However, information to be updated is not specified, therefore there is no compliance check that can fail, because any update or no update is valid. TS-0004 lists possible attributes to update. Spec change could require this and test could verify that existing optional data is updated in the local resource. |
| TS-0001_remoteCSE_002 | REQ-0001-10012 | Moved this to a more appropriate location. A couple lines down. How can we verify that a CSE-ID in the from field is actually a CSE-ID? |
|  | REQ-0001-10203 | I am not sure what this is for and how it relates to oneM2M. This is an external interface. |
|  | REQ-0001-10204 | Verify that the response from the receiver is proper <remoteCSE>. DMR? |
|  | REQ-0001-10205 | Originator create a local <remoteCSE> with information about the CSE that was just registered to. Verify that M attributes are created. |
|  | REQ-0001-10206 | If a retrieve is performed on the remote <CSEbase> the remote CSE should have <ACP> that allow this retrieve. This is an IMPLIED requirement. If a retrieve is performed, optional values should be updated. Test setup should specify optional attributes so that we can check that they are used. Should use this: REQ-0001-10013 |
| TS-0001_remoteCSE_003 | REQ-0001-10013 | Can be a basic DMR test case |
| TS-0001_remoteCSE_004 | REQ-0001-10014 | Can be a basic DMR test case |
| TS-0001_remoteCSE_005 | REQ-0001-10015 | Can be a basic DMR test case |
|  | REQ-0001-10207 | I am not sure what this is for and how it relates to oneM2M. This is an external interface. REQ-0001-10203 |
|  | REQ-0001-10173 | Repeat common DELETE operations. Is this covered in existing TPs? |
|  | REQ-0001-10174 | Repeat common DELETE operations. Is this covered in existing TPs? |
|  | REQ-0001-10175 | Repeat common DELETE operations. Is this covered in existing TPs? |
|  | REQ-0001-10176 | The Originator, upon receipt of the DELETE response, shall delete a <remoteCSE> resource locally under its <CSEBase> resource |
|  | REQ-0001-10208 | If the Receiver rejects the DELETE request and responds with an error in the DELETE response, the Originator cannot perform the action described in the Step 004 |
|  | REQ-0001-10209 | The originator CSE does not have RETRIEVE permission at CSEBase |

##### 10.1.1.2.1	CSE Registration procedure

The procedure for CSE Registration follows the procedure described in clause 10.1.1.1, but with some deviations. Below is the detailed description on how to perform the CSE Registration and which part of the procedure deviates from the one described in clause 10.1.1.1.

The Registration procedure requires the creation of two resources (a <remoteCSE> on the Receiver CSE and a <remoteCSE> on the Originator CSE) rather than one resource. The Registration procedure is always initiated by a CSE in the field domain except in the inter-domain case described in clause 6.5.

Originator: The Originator shall be the registering CSE.

Receiver: The Receiver shall create the <remoteCSE> resource.

Figure 10.1.1.2.1-1: Procedure for CREATEing a <remoteCSE> Resource

All the parameters of the request and steps that are not indicated do not deviate from clause 10.1.1.1.

Step 001: The Originator shall send mandatory parameters and may send optional parameters in Request message for CREATE operation as specified in clause 8.1.2

Step 002: The Receiver shall:

- The registrar CSE shall allow unknown remote CSE to attempt to ‘CREATE’ when it was authenticated by credential provided by the entity. See TS-0003[2] further detail about authentication for the CSE.

- Perform sub-steps 2)-10), from step 002 from clause 10.1.1.1 are applicable.

NOTE:	Optionally, if the M2M Service Provider supports inter-domain communication, the Receiver could perform this step if the attribute CSEBase (part of the Content parameter of the request) contains the public domain of the CSE. The Receiver could construct the domain as described in clause 6.4 and 6.5. The Receiver could add an AAA or AAAA record in DNS with the public domain name of the Originator CSE and the IP address of the IN-CSE associated with the Originator.

Step 003: See clause 10.1.1.1.

Step 004: The Originator, upon receipt of the successful CREATE response message, shall create a <remoteCSE> resource locally under its <CSEBase> resource. This resource is representing the Receiver CSE. The Originator shall provide the appropriate values to all mandatory parameters as described in clause 9.6.4.

Step 005: The Originator may issue a RETRIEVE Request towards the Receiver (same To as for the CREATE request message) to obtain the optional attributes of the <remoteCSE> resource created at the Originator in step 004 (e.g. labels, accessControlPolicyIDs attributes). The RETRIEVE procedure is described in clause 10.1.2.

See clauses 8.1.2 for the information to be included in the Request message.

Step 006: The Receiver verifies that the Originator has the appropriate privileges to access the information.

Step 007: The Receiver sends a RETRIEVE response message, according to the procedure described in clause 10.1.2.

See clauses 8.1.3 and 8.1.4 for the information to be included in the Response message.

Step 008: The Originator shall update the created <remoteCSE> resource for the Receiver with the information obtained in step 007.

General Exceptions:

All exceptions from clause 10.1.1.1 are applicable; in addition the following exception may occur:

- The Originator does not have the privileges to retrieve the attributes of the Receiver CSE. The Receiver responds with an error.

##### 10.1.4.2.1	CSE Deregistration procedure

The procedure for CSE Deregistration follows the procedure described in clause 10.1.4.1, but with some exceptions. Below is the detailed description on how to perform the CSE Deregistration and which part of the procedure deviates from the one described in clause 10.1.4.1.

The Deregistration procedure accompanies the deletion of two resources (a <remoteCSE> on the Hosting CSE and a <remoteCSE> on the Originator CSE) rather than one resource. The Deregistration procedure can be initiated by either Registree CSE or Registrar CSE.

Figure 10.1.4.2.1-1: Procedure for DELETING a <remoteCSE> Resource

Step 001: See clause 10.1.4.1.

Step 002: See clause 10.1.4.1.

Step 003: See clause 10.1.4.1.

Step 004: The Originator, upon receipt of the DELETE response, shall delete a <remoteCSE> resource locally under its <CSEBase> resource.

General Exceptions:

All exceptions from 10.1.4.1 are applicable; in addition the following exception may occur:

- If the Receiver rejects the DELETE request and responds with an error in the DELETE response, the Originator cannot perform the action described in the Step 004.

### 10.2.2	<remoteCSE> Resource Procedures

#### 10.2.2.1	Create <remoteCSE>

This procedure shall be used for creating a <remoteCSE> resource. It is part of the registration procedure for remote CSEs on the Registrar CSE (which is also the Hosting CSE), as described in clause 10.1.1.2.1.

Table 10.2.2.1-1: <remoteCSE> CREATE

| <remoteCSE> CREATE |
| --- |
| Associated Reference Point | Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: From: Originator CSE-ID Content: The resource content shall provide the information as defined in clause 9.6.4 |
| Processing at Originator before sending Request | According to clause 10.1.1.2.1 |
| Processing at Receiver | According to clause 10.1.1.2.1 If the IN-CSE is the receiver and if the M2M SP policies do allow access to the CSEs across multiple domains, then the IN shall create the appropriate entry in the M2M SP's DNS for successfully registered CSE |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <remoteCSE> resource, according to clause 10.1.1.2.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.2.1. the Originator upon receipt of successful CREATE response message, shall create <remoteCSE> resource locally and thereafter, it may issue a Retrieve request to its Registrar CSE’s <CSEBase> resource to update the optional attributes of locally created <remoteCSE> resource. |
| Exceptions | According to clause 10.1.1.2.1 |

#### 10.2.2.2	Retrieve <remoteCSE>

This procedure shall be used for retrieving the representation of the <remoteCSE> resource with its attributes.

Table 10.2.2.2-1: <remoteCSE> RETRIEVE

| <remoteCSE> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: attributes of the <remoteCSE> resource as the Originator requested |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.2.3	Update <remoteCSE>

This procedure shall be used for updating the attributes and the actual data of an <remoteCSE> resource.

Table 10.2.2.3-1: <remoteCSE> UPDATE

| <remoteCSE> UPDATE |
| --- |
| Associated Reference Point | Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: attributes of the <remoteCSE> resource as defined in clause 9.6.4 which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.2.4	Delete <remoteCSE>

This procedure shall be used for deleting the <remoteCSE> resource with all related information.

Table 10.2.2.4-1: <remoteCSE> DELETE

| <remoteCSE> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.4 |
| Processing at Receiver | According to clause 10.1.4 If the IN-CSE is the receiver and it has created an entry in the DNS to allow access to the CSE across multiple M2M domains, then it shall delete the entry from the DNS |
| Information in Response message | According to clause 10.1.4 |
| Processing at Originator after receiving Response | According to clause 10.1.4 |
| Exceptions | According to clause 10.1.4 |

In the introduction section, I renumber “OLD” requirement IDs to align with new values in our spreadsheet.

| TS-0004_remoteCSE_001 | REQ-0004-07041 | Moved comment to a more specific sentence for this requirement. This requires 3 test purposes: -Do not allow an <AE> to create a <remoteCSE>. -Do not allow a <CSE> to create a <remoteCSE> if it does not have proper credentials. Repond with SECURITY_ASSOCIATION_REQUIRED -Respond to a CREATE <remoteCSE> primitive with CREATED – see if this is covered in DMR. |
| --- | --- | --- |
| TS-0004_remoteCSE_002 | REQ-0004-07042 | – see if this is covered in DMR |
| TS-0004_remoteCSE_003 | REQ-0004-07043 | – see if this is covered in DMR |
| TS-0004_remoteCSE_004 | REQ-0004-07044 | Moved comment to a more specific sentence for this requirement. -Do not allow an <AE> to DELETE a <remoteCSE>. -Originator - Upon receiving a DELETE response, delete the local <remoteCSE> -Reciever - Respond to a DELETE <remoteCSE> primitive with DELETED – see if this is covered in DMR. |

#### <remoteCSE> resource specific procedure on CRUD operations

##### Introduction

The entire CSE registration procedure including <CSE> resource creation procedure below is defined in clause 10.1.1.2.1 of oneM2M TS-0001 [6] ("CSE registration procedure").

##### Create

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exception:

An AE shall not originate a Create <remoteCSE> resource request.

The Originator, upon receipt of successful CREATE response message, shall create a <remoteCSE> resource locally.

The Originator may issue RETRIEVE request to its registrar <CSEBase>, to fetch the additional information about the registrar CSE and add this information to its local <remoteCSE> resource. The Originator may choose which optional attributes to include in its <remoteCSE> resource.

Receiver:

Same as the generic procedures in clause 7.2.2.2 except replacement of Recv-6.3 step with following:

- The Hosting CSE shall check if the credential provided by the Originator is valid.

- If the check is failed, then the Hosting CSE shall return response primitive with a Response Status Code indicating "SECURITY_ASSOCIATION_REQUIRED" error.

##### Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Update

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exception:

An AE shall not originate a Update <remoteCSE> resource request.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Delete

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exceptions:

- An AE shall not originate a Delete <remoteCSE> resource request.

- The Originator, upon receipt of successful DELETE response message, shall delete the corresponding <remoteCSE> resource locally.

Receiver:

No change from the generic procedures in clause 7.2.2.2

### -----------------------Start of change 1-------------------------------------------

TP/oneM2M/CSE/REG/BV/0XX1

| TP Id | TP/oneM2M/CSE/REG/BV/0XX1 |
| --- | --- |
| Test objective | Check that the IUT accepts a CSE registration from another CSE |
| Reference | TS-0001 10.1.1.2.1 - case C, 9.6.19 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the CSE having privileges to perform CREATE remoteCSE resource on the IUT CSEBase } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from CSE containing Resource Type set to 16 (remoteCSE) and From set to CSE-ID and Content containing remoteCSE resource representation } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( CSE |

TP/oneM2M/CSE/REG/BV/0XX2

| TP Id | TP/oneM2M/CSE/REG/BV/0XX2 |
| --- | --- |
| Test objective | Check that the IUT creates a local <remoteCSE> after receiveing a created response to a CREATE <remoteCSE> request on a registrar CSE |
| Reference | TS-0001 10.1.1.2.1 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the CSE and the CSE having privileges to perform RETRIEVE operation on the IUT CSEBase } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to IUT_CSE_BASE_RESOURCE_ADDRESS and From set to CSE_ID and ResultContent set to 3 (attributes+child resources) } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing CSEBase resource containing childResource containing remoteCSE resource representation } | IUT ( CSE |

TP/oneM2M/CSE/REG/BV/0XX3

| TP Id | TP/oneM2M/CSE/REG/BV/0XX3 |
| --- | --- |
| Test objective | Check that the IUT updates a local <remoteCSE> after receiving a retrieve response to a RETRIEVE <CSEBase> request on a registrar CSE |
| Reference | TS-0001 10.1.1.2.1 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the CSE and the IUT having retrieved remoteCSE resource on the CSE containing label set to VALUE and the IUT having privileges to perform UPDATE operation on the CSE and the CSE having privileges to perform RETRIEVE operation on the IUT CSEBase } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to IUT_CSE_BASE_RESOURCE_ADDRESS and From set to CSE_ID and ResultContent set to 3 (attributes+child resources) } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing CSEBase resource containing childResource containing remoteCSE resource containing label set to VALUE } | IUT ( CSE |

TP/oneM2M/CSE/REG/BV/0XX4

| TP Id | TP/oneM2M/CSE/REG/BV/0XX4 |
| --- | --- |
| Test objective | Check that the IUT does not update a local <remoteCSE> after receiving an unsuccessful retrieve response to a RETRIEVE <CSEBase> request on a registrar CSE |
| Reference | TS-0001 10.1.1.2.1 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the CSE and the IUT having not retrieved successfully remoteCSE resource on the CSE containing label set to VALUE and the IUT not having privileges to perform UPDATE operation on the CSE and the CSE having privileges to perform RETRIEVE operation on the IUT CSEBase } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to IUT_CSE_BASE_RESOURCE_ADDRESS and From set to CSE_ID and ResultContent set to 3 (attributes+child resources) } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing CSEBase resource containing childResource containing remoteCSE resource containing label set to NULL | IUT ( CSE |

TP/oneM2M/CSE/REG/BV/0XX5

| TP Id | TP/oneM2M/CSE/REG/BV/0XX5 |
| --- | --- |
| Test objective | Check that the IUT deletes the local <remoteCSE> after receiving a deleted response to a DELETE <remoteCSE> request on a registrar CSE |
| Reference | TS-0001 10.1.1.2.1 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the CSE and the IUT having a <remoteCSE> resource and the IUT having deleted the remoteCSE resource on the CSE and the IUT having privileges to perform DELETE operation on the CSE and the CSE having privileges to perform RETRIEVE operation on the IUT CSEBase } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to IUT_CSE_BASE_RESOURCE_ADDRESS and From set to CSE_ID and ResultContent set to 3 (attributes+child resources) } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing CSEBase resource containing childResource containing no remoteCSE resource representation } | IUT |

TP/oneM2M/CSE/REG/BV/0XX6

| TP Id | TP/oneM2M/CSE/REG/BV/0XX6 |
| --- | --- |
| Test objective | Check that the IUT does not delete the local <remoteCSE> after receiving a error response to a DELETE <remoteCSE> request on a registrar CSE |
| Reference | TS-0001 10.1.1.2.2 - case C, 9.6.19 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the CSE and the IUT having a <remoteCSE> resource and the IUT having not deleted successfully the remoteCSE resource on the CSE and the IUT not having privileges to perform DELETE operation on the CSE and the CSE having privileges to perform RETRIEVE operation on the IUT CSEBase } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to IUT_CSE_BASE_RESOURCE_ADDRESS and From set to CSE_ID and ResultContent set to 3 (attributes+child resources) } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing CSEBase resource containing childResource containing remoteCSE resource representation } | IUT |

### -----------------------End of change 1---------------------------------------------

# Comments

How is it “unknown” if we can authenticate it?

Should this be changed to a shall not - > ARC SPEC CR.

REQ-0001-10142

REQ-0001-10200

Check latest specs because these sub-steps (9 & 10) do not exist in our current annotated version. This is fixed in V2_12_0.

REQ-0001-10201

REQ-0001-10202

REQ-0001-10143

REQ-0001-10144

REQ-0001-10145

REQ-0001-10209

REQ-0001-10173

REQ-0001-10174

REQ-0001-10175

REQ-0001-10176

REQ-0001-10208

REQ-0001-10012

REQ-0001-10203

REQ-0001-10204

REQ-0001-10205

REQ-0001-10206

REQ-0001-10013

REQ-0001-10014

REQ-0001-10015

REQ-0001-10207

REQ-0004-07041

REQ-0004-07042

REQ-0004-07043

REQ-0004-07044

IUT is a receiver CSE (IN or MN).

REQ-0001-10142

REQ-0001-10201

REQ-0001-10202

IUT is a originator CSE (MN)

REQ-0001-10143

REQ-0001-10205

IUT is a originator CSE (MN)

REQ-0001-10145

REQ-0001-10206

IUT is a originator CSE (MN)

REQ-0001-10209

I didn’t see anything like this in other tests.

IUT is a originator CSE (MN)

REQ-0001-10176

IUT is a originator CSE (MN)

REQ-0001-10208