| Input Contribution |
| --- |
| Meeting ID* | TST 28 |
| Title:* | TS-0018_New_TPs_for_ AE registration supporting attributes (labels, AppName and , pointOfAccess ) (IN-PROFILE) |
| Source:* | R. Trapero, AT4 wireless, rtmiralles@at4wireless.com Antonio Castillo Verdugo, AT4 wireless, acverdugo@at4wireless.com |
| Uploaded Date:* | 2017-03-09 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some new test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) for IN-PROFILE |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some additional TPs for groups CSE/REG of the TS-0018 – Test Suite Structure and Test Purposes covering  the labels, applicationName and pointOfAccess attributes of <AE> resource.

Proposal

================ Start of  1st  Part: Test Purposes ==================

#### Registration (REG)

| TP Id | TP/oneM2M/CSE/REG/BV/XXX |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration with the optional attribute OPTIONAL_ATTRIBUTE provided |
| Reference | TS-0001 10.1.1.2.2, 9.6.5-2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE, PICS_IN_PROFILE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having a CSEBase resource containing a ServiceSubscribedProfile resource containing a serviceSubscribedNode resource containing ruleLinks attribute pointing to a serviceSubscribedAppRule resource containing applicableCredIDs attribute set to None and allowedApp-IDs attribute indicating APP-ID and allowedAEs attribute indicating C-AE-ID-STEM } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to 2 (AE) and From set to empty and Content containing AE resource containing OPTIONAL_ATTRIBUTE attribute } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE | RESOURCE_TYPE |
| --- | --- | --- | --- |
| TP/oneM2M/CSE/REG /BV/0XX_01 | TS-0001 9.6.5-2 | labels | AE |
| TP/oneM2M/CSE/REG/BV/0XX_02 | TS-0001 9.6.5-2 | AppName | AE |
| TP/oneM2M/CSE/REG/BV/0XX_03 | TS-0001 9.6.5-2 | pointOfAccess | AE |