| Input Contribution |
| --- |
| Meeting ID* | TST 28 |
| Title:* | TS-0018_New_TPs_for_ResultContent_attribute |
| Source:* | Miguel A. Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org Laurent Velez, ETSI, Laurent.Velez@etsi.org |
| Uploaded Date:* | 2017-03-22 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some new test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) for IN-PROFILE |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some additional TPs for groups CSE/DMR and CSE/DMR/CRE of the TS-0018 – Test Suite Structure and Test Purposes covering ResultContent attribute handling for several resource types during CREATE and RETRIEVE operations.

Proposal

================ Start of  1st  Part: Test Purposes ==================

## 7.2.2	Group CSE

TP/oneM2M/CSE/DMR/BV/006

| TP Id | TP/oneM2M/CSE/DMR/BV/006 |
| --- | --- |
| Test objective | Check that the IUT returns successfully only child resources of TARGET_RESOURCE_ADDRESS resource when Result Content is set to 8 (child resources) |
| Reference | TS-0001 8.1.2 & TS-0004 6.3.3.2.7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type RESOURCE_TYPE containing child resource representation and the AE having privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to 8 (child resources) } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing CHILD_RESOURCE_TYPE resource representation } | IUT  AE |

| TP Id | RESOURCE_TYPE |
| --- | --- |
| TP/oneM2M/CSE/DMR/BV/006_01 | 3 (container) |
| TP/oneM2M/CSE/DMR/BV/006_02 | 9 (group) |
| TP/oneM2M/CSE/DMR/BV/006_03 | 1 (accessControlPolicy) |
| TP/oneM2M/CSE/DMR/BV/006_04 | 18 (schedule) |
| TP/oneM2M/CSE/DMR/BV/006_05 | 15 (pollingChannel) |
| TP/oneM2M/CSE/DMR/BV/006_06 | 23 (subscription) |

| TP Id | TP/oneM2M/CSE/DMR/CRE/BV/0XX |
| --- | --- |
| Test objective | Check that the IUT rejects a CREATE request when the ResultContent is set to RESULT_CONTENT |
| Reference | TS-0001 8.1.2 & TS-0004 7.3.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to AE_RESOURCE_ADDRESS and From set to AE_IDENTIFIER and Result Content set to RESULT_CONTENT } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) and no Content } | IUT  AE |

| TP ID | Reference | RESULT_CONTENT |
| --- | --- | --- |
| TP/oneM2M/CSE/DMR/CRE/BV/0XX_01 | TS-0004 6.3.4.2.7 | 4 (attributes and child resources) |
| TP/oneM2M/CSE/DMR/CRE/BV/0XX_02 |  | 5 (attributes and child resources references) |
| TP/oneM2M/CSE/DMR/CRE/BV/0XX_03 |  | 6 (child resrouces references) |
| TP/oneM2M/CSE/DMR/CRE/BV/0XX_04 |  | 8 (child resources) |

================ End of  1st  Part: Test Purposes ==================