| Input Contribution |
| --- |
| Meeting ID* | TST#28 |
| Title:* | TP for CE/REG/00002 |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd., Yinjiaxin@huawei.com |
| Date:* | 2017-03-21 |
| Input related to* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0018 v0.1.7 |
| Decision requested or recommendation:* | Incorporate the text if agreed. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

#### 7.2.2.1	Registration

TP/oneM2M/CSE/REG/RET/BV/00x

| TP Id | TP/oneM2M/CSE/REG/RET/BV/00x |
| --- | --- |
| Test objective | Check that the IUT accepts an retrieval request of <AE> resource with attributes multiplicity equals to 1. The IUT could be MN-CSE, IN-CSE or ASN-CSE. |
| Reference | TS-0001 10.2.1.2, TS-0001 9.6.5, TS-0004 7.4.5.2.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform RETRIEVE operation on the <AE> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to ResourceID of AE resoure and From set to AE_ID } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing <AE> resource representation containing ATTRIBUTE } | IUT ( AE |

| TP Id | Reference | ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/REG/BV/00x _01 | TS-0001 9.6.5 | labels |
| TP/oneM2M/CSE/REG/BV/00x _02 | TS-0001 9.6.5 | appName |
| TP/oneM2M/CSE/REG/BV/00x _03 | TS-0001 9.6.5 | pointOfAccess |
| TP/oneM2M/CSE/REG/BV/00x _04 | TS-0001 9.6.5 | nodeLink |
| TP/oneM2M/CSE/REG/BV/00x _05 | TS-0001 9.6.5 | contentSerialization |

TP/oneM2M/CSE/REG/CRE/BV/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/00x |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <AE> resource with attributes multiplicity equals to 1 and provided preprovisioned AE_ID of CSE relative format. It’s assumed that the checking in Step 003 if TS-0001 10.1.1.2.2 is successful due to implementation specific procedure. Case d of TS-0001 10.1.1.2.2 applies to this test purpose. The IUT could be ASN-CSE, MN-CSE or IN-CSE. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the AE_ID_stem already preconfigured at the IUT } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to AE_ID_Stem and resource type set to 2(AE) request identifier set to REQUEST_ID representation of AE resource containing appID set to APP_ID and requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (OK) and Content containing <AE> resource representation containing AE-ID attribute set to AE_ID_Stem requestReachability attribute set to REQUEST_REACHABILITY and resourceID attribute set to AE_ID_Stem resourceType attribute set to AE resourceName attribute set to VALUE1 parentID attribute set to ResourceID_of_CSEBase expirationTime attribute set to VALUE2 creationTime attribute set to VALUE3 lastModifiedTime attribute set to VALUE3 App-ID attribute set to APP_ID AE-ID attribute set to CSE_relative_AE_ID requestReachability attribute set to REQUEST_REACHABILITY } | IUT ( AE |

VALUE1: resourceNameassigned by the IUT and guarenteed to be unique amang all other resouceNames of child resource of the CSEBase

VALUE2: time assigned by the IUT that is larger than VALUE3

VALUE3: time the IUT creates the AE resource

TP/oneM2M/CSE/REG/CRE/BV/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/00x |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <AE> resource with attributes multiplicity equals to 1 and provided preprovisioned SP_relative_AE_ID. It’s assumed that the checking in Step 003 if TS-0001 10.1.1.2.2 is successful due to implementation specific procedure. Case b of TS-0001 10.1.1.2.2 applies to this test purpose. The IUT could be ASN-CSE or MN-CSE. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the AE_ID_stem already preconfigured at the IUT } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to SP_relative_AE_ID and resource type set to 2(AE) request identifier set to REQUEST_ID representation of AE resource containing appID set to APP_ID and requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then{ the IUT sends a valid UPDATE Request to IN-CSE containing to set to ResourceID_of_CSEBase of IN-CSE and from set to CSE_ID of IUT and content containing the representation of <AEAnnc> containing expirationTime set to EXPIRATION_TIME link attribute set to the SP_relative_AE_ID labels attribute set to CREDENTIAL_ID } | IUT ( IN-CSE |
|  | then{ the IUT receives a valid Response containing Response Status Code set to 2001 (OK) and Content containing <AEAnnc> resource representation containing resourceType attribute set to 10002 (AEAnnc) resourceName attribute set to VALUE1 parentID attribute set to ResourceID_of_CSEBase of IN_CSE expirationTime attribute set to VALUE2 creationTime attribute set to VALUE3 lastModifiedTime attribute set to VALUE4 link attribute set to SP_relative_AE_ID labels attribute set to CREDENTIAL_ID } | IUT <- IN-CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (OK) and Content containing <AE> resource representation containing resourceID attribute set to AE_ID_Stem requestReachability attribute set to REQUEST_REACHABILITY and resourceType attribute set to 2 (AE) resourceName attribute set to VALUE5 parentID attribute set to ResourceID_of_CSEBase expirationTime attribute set to VALUE6 creationTime attribute set to VALUE7 lastModifiedTime attribute set to VALUE7 App-ID attribute set to APP_ID AE-ID attribute set to SP_relative_AE_ID requestReachability attribute set to REQUEST_REACHABILITY } | IUT ( AE |

VALUE1: resourceNameassigned by the IUT and guarenteed to be unique amang all other resouceNames of child resource of the CSEBase

VALUE2: time assigned by the IUT that is larger than VALUE4 but no larger than EXPIRATION_TIME

VALUE3: time the IUT creates the AE resource

VALUE4: time the <AEAnnc> resource is modified

VALUE5: resourceNameassigned by the IUT and guarenteed to be unique amang all other resouceNames of child resource of the CSEBase

VALUE6: time assigned by the IUT that is larger than VALUE7

VALUE7: the creationTime of the <AE> resource

TP/oneM2M/CSE/REG/CRE/BV/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/00x |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <AE> resource with attributes multiplicity equals to 1 and asking an CSE relative AE_ID by indicating AE_ID_Stem starting with ‘C’. It’s assumed that the checking in Step 003 if TS-0001 10.1.1.2.2 is successful due to implementation specific procedure. Case c of TS-0001 10.1.1.2.2 applies to this test purpose. The IUT could be ASN-CSE, MN-CSE or IN-CSE. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to string with character ‘C’ and resource type set to 2(AE) request identifier set to REQUEST_ID representation of AE resource containing appID set to APP_ID and requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (OK) and Content containing <AE> resource representation containing resourceID attribute set to AE_ID_Stem requestReachability attribute set to REQUEST_REACHABILITY and resourceType attribute set to AE resourceName attribute set to VALUE1 parentID attribute set to ResourceID_of_CSEBase expirationTime attribute set to VALUE2 creationTime attribute set to VALUE3 lastModifiedTime attribute set to VALUE3 App-ID attribute set to APP_ID AE-ID attribute set to CSE_relative_AE_ID requestReachability attribute set to REQUEST_REACHABILITY } | IUT ( AE |

VALUE1: resourceNameassigned by the IUT and guarenteed to be unique amang all other resouceNames of child resource of the CSEBase

VALUE2: time assigned by the IUT that is larger than VALUE3

VALUE3: time the IUT creates the AE resource

TP/oneM2M/CSE/REG/CRE/BV/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/00x |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <AE> resource with attributes multiplicity equals to 1 and provided character ‘S’ in AE_ID_Stem ask for a SP_relative_AE_ID. It’s assumed that the checking in Step 003 if TS-0001 10.1.1.2.2 is successful due to implementation specific procedure. Case a of TS-0001 10.1.1.2.2 applies to this test purpose. The IUT could be ASN-CSE or MN-CSE. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to character ‘S’ and resource type set to 2(AE) request identifier set to REQUEST_ID representation of AE resource containing appID set to APP_ID and requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then{ the IUT sends a valid CREATE Request to IN-CSE containing to set to ResourceID_of_CSEBase of IN-CSE and from set to CSE_ID of IUT and content containing the representation of <AEAnnc> containing AE-ID attribute set to character ‘S’ APP-ID attribute set to APP_ID expirationTime set to EXPIRATION_TIME link attribute set to the SP_relative_AE_ID labels attribute set to CREDENTIAL_ID } | IUT ( IN-CSE |
|  | then{ the IUT receives a valid Response containing Response Status Code set to 2001 (OK) and Content containing <AEAnnc> resource representation containing resourceType attribute set to 10002 (AEAnnc) resourceName attribute set to VALUE1 parentID attribute set to ResourceID_of_CSEBase of IN_CSE expirationTime attribute set to VALUE2 creationTime attribute set to VALUE3 lastModifiedTime attribute set to VALUE4 AE-ID set to SP_relative_AE_ID APP-ID set to APP_ID link attribute set to SP_relative_AE_ID labels attribute set to CREDENTIAL_ID } | IUT <- IN-CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (OK) and Content containing <AE> resource representation containing resourceID attribute set to AE_ID_Stem requestReachability attribute set to REQUEST_REACHABILITY and resourceType attribute set to 2 (AE) resourceName attribute set to VALUE5 parentID attribute set to ResourceID_of_CSEBase expirationTime attribute set to VALUE6 creationTime attribute set to VALUE7 lastModifiedTime attribute set to VALUE7 App-ID attribute set to APP_ID AE-ID attribute set to SP_relative_AE_ID requestReachability attribute set to REQUEST_REACHABILITY } | IUT ( AE |

Editor’s Note: what’s the content of link attribute of <AEAnnc> to be created need to be clarified.

TP/oneM2M/CSE/REG/CRE/BV/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/00x |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <AE> resource with attributes multiplicity equals to 1 without preference of format of AE_ID |
| Reference |  |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |

Editor’s Note: the case need to be added after the publication of updated R2 of TS-0001 where the case will be added.

TP/oneM2M/CSE/REG/CRE/BV/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BV/00x |
| --- | --- |
| Test objective | Check that the IUT accepts an create request of <AE> resource with attributes multiplicity equals to 1 and provided preprovisioned SP_relative_ AE_ID. It’s assumed that the checking in Step 003 if TS-0001 10.1.1.2.2 is successful due to implementation specific procedure. Case b of TS-0001 10.1.1.2.2 applies to this test purpose. The IUT could be IN-CSE. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the AE_ID_stem already preconfigured at the IUT } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to AE_ID_Stem and resource type set to 2(AE) request identifier set to REQUEST_ID representation of AE resource containing appID set to APP_ID and requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (OK) and Content containing <AE> resource representation containing resourceID attribute set to AE_ID_Stem requestReachability attribute set to REQUEST_REACHABILITY and resourceID attribute set to SP_relative_AE_ID resourceType attribute set to AE resourceName attribute set to VALUE1 parentID attribute set to ResourceID_of_CSEBase expirationTime attribute set to VALUE2 creationTime attribute set to VALUE3 lastModifiedTime attribute set to VALUE3 App-ID attribute set to APP_ID AE-ID attribute set to SP_relative_AE_ID requestReachability attribute set to REQUEST_REACHABILITY } | IUT ( AE |

VALUE1: resourceNameassigned by the IUT and guarenteed to be unique amang all other resouceNames of child resource of the CSEBase

VALUE2: time assigned by the IUT that is larger than VALUE3

VALUE3: time the IUT creates the AE resource

TP/oneM2M/CSE/REG/CRE/BI/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BI/00x |
| --- | --- |
| Test objective | Check that the IUT rejects an create request of <AE> resource that doesn’t include the requestReachability attribute. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to AE_ID_Stem and resource type set to 2(AE) request identifier set to REQUEST_ID representation of AE resource containing APP-ID attribute set to APP_ID } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD Request) } | IUT ( AE |

TP/oneM2M/CSE/REG/CRE/BI/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BI/00x |
| --- | --- |
| Test objective | Check that the IUT rejects an create request of <AE> resource that doesn’t include the APP-ID attribute. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to AE_ID_Stem and resource type set to 2(AE) request identifier set to REQUEST_ID representation of AE resource containing requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD Request) } | IUT ( AE |

TP/oneM2M/CSE/REG/CRE/BI/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BI/00x |
| --- | --- |
| Test objective | Check that the IUT rejects an create request of <AE> resource that doesn’t include the resourceType parameter. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to AE_ID_Stem and request identifier set to REQUEST_ID representation of AE resource containing APP-ID set to APP_ID requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD Request) } | IUT ( AE |

Editor’s Note: Need to figure a way to address all invalid behaviours for common parameter and attributes.

TP/oneM2M/CSE/REG/CRE/BI/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BI/00x |
| --- | --- |
| Test objective | Check that the IUT rejects an create request of <AE> resource with AE-ID of the wrong format |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to AE_ID_Stem of wrong format and request identifier set to REQUEST_ID and resource type set to 2(AE) representation of AE resource containing APP-ID set to APP_ID requestReachability set to REQUEST_REACHABILITY } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD Request) } | IUT ( AE |

TP/oneM2M/CSE/REG/CRE/BI/00x

| TP Id | TP/oneM2M/CSE/REG/CRE/BI/00x |
| --- | --- |
| Test objective | Check that the IUT rejects an create request of <AE> resource that contains attributes with the wrong format. |
| Reference | TS-0001 10.1.1.2.2, TS-0004 7.4.5.2.1 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a CREATE Request from AE containing to set to ResourceID_of_CSEBase and from set to AE_ID_Stem and request identifier set to REQUEST_ID and resource type set to 2(AE) representation of AE resource containing APP-ID set to APP_ID of wrong format or requestReachability set to REQUEST_REACHABILITY of wrong format } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4000 (BAD Request) } | IUT ( AE |

# Comments

Normal retrieval of AE

Create AE with configured CSE relative AE-ID-Stem

Create AE to ASN or MN with SP relative AEID

Create AE to ASN, MN or IN with AE_ID_stem starting with C

Create AE to ASN or MN with AE_ID_Stem  starting with ‘S’

Creating AE without any preference of AE-ID

Create AE on IN-CSE with AE-ID-stem just a ‘S’