| Input Contribution |
| --- |
| Meeting ID* | TST 28 |
| Title:* | TS-0028 Security Test Purposes ESPrim (Rel2) |
| Source:* | Easy Global Market |
| Uploaded Date:* | 2017-03-28 |
| Document(s) Impacted* | TS-0028 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes some additional TPs for the TS-0028 – Security Test Suite Structure and Test Purposes, Release 2.

Proposal

================ Start of  1st  Part: Test Purposes ==================

| TP Id | TP/oneM2M/CSE/SEC/BV/001 |
| --- | --- |
| Test objective | Check that the IUT sends a new ESPrimRandObject when the old one is expired |
| Reference | TS-0003 8.4.2 – step B.2C.2, TS-0004 7.5.1.2.11 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with AE and the AE obtained e2eSecInfo attribute from IUT with a Suid set to support ESPrim and sharedReceivedESPrimRandObject with esprimRandExpiry attribute expired } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY request from AE containing To set to CSE_ID and From set to AE_ID and Content containing securityInfo element containing securityInfoType attribute set to 3 } | IUT  AE |
|  | then { the IUT sends a valid NOTIFY Response containing Content containing securityInfo containing securityInfoType set to 4 and esprimRandObject set to a generated ESPrim Object } | IUT  AE |

| TP Id | TP/oneM2M/CSE/SEC/BV/002 |
| --- | --- |
| Test objective | Check that the IUT can retrieve the list of security features available on the CSE |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with AE and the IUT having created an attribute e2eSecInfo } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_ATTRIBUTE_ADDRESS and From set to AE_ID and no Content attribute } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing CSEBase resource containing e2eSecInfo attribute containing no sharedReceiverESPrimRandObject parameter } | IUT  AE |

Note: TARGET_ATTRIBUTE_ADDRESS = remoteCSE#e2eSecInfo

| TP Id | TP/oneM2M/CSE/SEC/BV/003 |
| --- | --- |
| Test objective | Check that the IUT responds with an error when there is no e2eSecInfo attribute |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE containing To set to TARGET_ATTRIBUTE_ADDRESS and From set to AE_ID and no Content attribute } | IUT  AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4004 (NOT_FOUND) } | IUT  AE |

Note: TARGET_ATTRIBUTE_ADDRESS = remoteCSE#e2eSecInfo

| TP Id | TP/oneM2M/CSE/SEC/BV/004 |
| --- | --- |
| Test objective | Check that the IUT responds with a valid ESPrim object |
| Reference | TS-0003 8.4.2 – step C10, TS-0004 7.6.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a sessionESPrimKey with AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from AE containing To set to CSE_ID and From set to AE_ID and Content containing securityInfo element containing securityInfoType attribute set to 5 (ESPrim Object) and valid esprimObject attribute } | IUT  AE |
|  | then { the IUT sends a valid NOTIFY Response containing Response Status Code set to 2000 (OK) and Content containing securityInfo element containing securityInfoType attribute set to 5 and valid esprimObject attribute } | IUT  AE |

| TP Id | TP/oneM2M/CSE/SEC/BV/005 |
| --- | --- |
| Test objective | Check that the IUT responds with a valid ESPrim object, but with expired session values |
| Reference | TS-0003 8.4.2 – step C11, TS-0004 7.6.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a sessionESPrimKey with AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY request from AE containing To set to CSE_ID and From set to AE_ID and Content containing securityInfo element containing securityInfoType attribute set to 5 (ESPrim Object) and valid esprimObject attribute | IUT  AE |
|  | then { the IUT sends a valid NOTIFY Response containing Response Status Code set to 2000 (OK) and Content containing securityInfo element containing securityInfoType attribute set to 5 and valid esprimObject attribute containing JWE Protected Header containing expired ATTRIBUTE } | IUT  AE |

| TP Id | Reference | ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/SEC/BV/005_01 | TS-0003 8.4.3.2 | pairwiseESPrimKeyID |
| TP/oneM2M/CSE/SEC/BV/005_02 | TS-0003 8.4.3.2 | originatorESPrimRandObject |
| TP/oneM2M/CSE/SEC/BV/005_03 | TS-0003 8.4.3.2 | receiverESPrimRandObject |

================ End of  1st  Part: Test Purposes ==================