| CHANGE REQUEST |
| --- |
| Meeting:* | TST 28.1 |
| Source:* | Ting Martin Miao, KETI, martin.miao@keti.re.kr |
| Date:* | 2017-04-03 |
| Contact:* | Same as Source |
| Reason for Change/s:* | Correct HTTP Host Header |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0034 |
| Clauses/Sub Clauses* | 8.3.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Correct HTTP Host Header.

### -----------------------Start of change 1-------------------------------------------

### 8.3.3  Long Polling

As mentioned in clause 7.2.4, for using long polling procedures, ADN-AE3 creates <pollingChannel> resource on MN-CSE. The following example shows <pollingChannel> resource create request and response using HTTP with JSON serialization.

HTTP Request:

POST /~/mn-cse/gateway/adn-ae3?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Cadn-ae3
Content-Type: application/vnd.onem2m-res+json;ty=15

X-M2M-RI: mncse-12345

{

"m2m:pch":

{

"rn":"actuator01"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-12345

Content-Location: /mn-cse/pch-78901234

Content-Type: application/vnd.onem2m-res+json

ADN-AE3 also generates a container and a content instance resource under the container of ADN-AE3, according to the similar procedure in 8.3.1. It is assumed that a subscription to this container resource has been created using the <pollingChannel> as a notificationURI in the subscraption.

Then user can subscribe or make a change of the actuator state on the gateway. It is assumed that the user already subscribed this resource, so when the user makes a change to the actuator state via the smartphone user interface, the smartphone application performs a new content instance creation procedure carrying the new state in request.

If the contentInstance create request body is represented in JSON, the following is a HTTP request message example:

HTTP Request:

POST /~/mn-cse/gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Cadn-ae4
Content-Type: application/vnd.onem2m-res+json;ty=4

X-M2M-RI: mncse-11123

{

"m2m:cin":

{

"cnf": "text/plains:0",

"con": "ON"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-11123

Content-Location: /mn-cse/cin-789356234

Then the gateway will generate a notification based on the new content instance creation procedure. Usually the actuator (ADN-AE3) sends request periodically to the gateway in order to retrieve this notification though long polling procedure.

If the request body is represented in JSON, the following is a HTTP request message example:

HTTP Request:

GET /~/mn-cse/gateway/adn-ae3/actuator01/pcu HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Cadn-ae3

X-M2M-RI: mncse-11223

HTTP Response:

200 OK

X-M2M-RI: mncse-11223

{

"m2m:sgn":

{

"nev":{

"rep":

{

"cin":

{

"cnf": "text/plain:0"	,

"con": "ON"

}

}

},

"sur":"/mn-cse/sub-856463728"

}

}

After retrieved the notification, the states of actuator (ADN-AE3) can be updated automatically. Then the ADN-AE3 sends request to the gateway to indicate the previous notification had been successfully performed.

### ----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?