| CHANGE REQUEST |
| --- |
| Meeting:* | TST 28.1 |
| Source:* | Ting Martin Miao, KETI, martin.miao@keti.re.kr |
| Date:* | 2017-04-03 |
| Contact:* | Same as Source |
| Reason for Change/s:* | Correct HTTP Host Header |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0025v2.0.0 |
| Clauses/Sub Clauses* | 8.7 Implementation Procedures |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Correct HTTP Host Header.

### -----------------------Start of change 1-------------------------------------------

## 8.7	Implementation Procedures

### 8.7.1 	Introduction

The implementation procedures in the current use case are mapped into HTTP bindings with both XML and JSON serializations of oneM2M primitives according to the standard APIs describing the reference points Mca and Mcc, as defined in oneM2M TS-0001 [i.2], oneM2M TS-0004 [i.3], the HTTP binding TS-0009 [i.4].

In addition, short names for the representation of the resources and attributes are used in the implementation procedures.

### 8.7.2 	MN-CSE registration

The implementation starts with the registration of MN-CSE with IN-CSE as shown in the following procedure.

The following example shows the MN-CSE registration request and response using XML serialization

HTTP Request:

POST /~/in-cse/server?rcn=0 HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /mn-cse
Content-Type: application/xml;ty=16

X-M2M-RI: incse-88643

<?xml version="1.0" encoding="UTF-8"?>

<m2m:csr xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="home_gateway">

<csi>mn-cse</csi>

<cb>mn.provider.com/mn-cse</cb>

<rr>true</rr>

<poa>http://mn.provider.com:8080</poa>

<cst>2</cst>

<acpi>/in-cse/acp-666957710</acpi>

</m2m:csr>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse-88643

Content-Location: /in-cse/csr-299409504

The following example shows the MN-CSE registration request and response using HTTP with JSON serialization.:

HTTP Request:

POST /~/in-cse/server?rcn=0 HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /mn-cse
Content-Type: application/json;ty=16

X-M2M-RI: incse-88643

{

"m2m:csr":

{

"rn": "home_gateway",

"csi": "mn-cse",

"cb": "mn.provider.com/mn-cse",

"rr": true,

"poa": ["http://mn.provider.com:8080"],

"cst": 2,

"acpi": ["/in-cse/acp-666957710"]

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse-88643

Content-Location: /in-cse/csr-299409504

### 8.7.3 	Access control policy creation

When an access control policy resource is created, a list of one or more allowed request originators must be specified in the acor field and the allowed operations in the acop field.

The value of acop is set to 63 which indicates that the specified originator is granted privileges to conduct CREATE, RETRIEVE, UPDATE, DELETE, DISCOVERY,and NOTIFY operations.

The creation of access control policy resource gateway_acp in MN-CSE is implemented in the following procedure.

The following example shows an access control policy create request and response using HTTP with XML serialization.

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Cgateway_ae
Content-Type: application/xml;ty=1

X-M2M-RI: mncse-62948

<m2m:acp xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="gateway_acp">

<pv>

<acr>

<acor>Cgateway_ae Clight_ae1 Clight_ae2 /in-cse/Csmartphone_ae</acor>

<acop>63</acop>

</acr>

</pv>

<pvs>

<acr>

<acor>Cgateway_ae </acor>

<acop>51</acop>

</acr>

</pvs>

</m2m:acp>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-62948

Content-Location: /mn-cse/acp-805496226

The following example shows an access control policy create request and response using HTTP with XML serialization.

HTTP Request:

POST /~/mn-cse/home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Cgateway_ae
Content-Type: application/json;ty=1

X-M2M-RI: mncse-62948

{

"m2m:acp":

{

"rn": "gateway_acp",

"pv":

{

"acr":[{

"acor":

[

"Cgateway_ae",

"Clight_ae1",

"Clight_ae2",

"/in-cse/Csmartphone_ae"

],

"acop":63

}]

},

"pvs":

{

"acr":[{

"acor":

[

"Cgateway_ae"

],

"acop":51

}]

}

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-62948

Content-Location: /mn-cse/acp-805496226

The access control policy resource is used to grant applications the access rights to conduct specific operations and access to specific resources. The list of applications could be obtained with a discovery procedure using filter criteria conditions. For more details about the discovery procedure, please go to clause  8.7.9. Here it is required that the list of applications has been discovered before creating the access control policy resource.

### 8.7.4 	Application entities registration

#### 8.7.4.1	Light application ADN-AE1

The registration of ADN-AE1 with MN-CSE is shown in the following procedure. Note that the access control policy identifier (unstructured SP-relative resourceID) which is assigned to ADN-AE1 is /mn-cse/acp-805496226.

The following example shows an ADN-AE registration request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/xml;ty=2

X-M2M-RI: mncse-92345

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light_ae1">

<api>A01.com.company.lightApp1</api>

<rr>true</rr>

<poa>http://192.168.0.10:9090</poa>

<acpi>/mn-cse/acp-805496226</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-92345

Content-Location: /mn-cse/ae-CAE340304071

The following example shows an ADN-AE registration request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/json;ty=2

X-M2M-RI: mncse-92345

{

"m2m:ae":

{

"rn": "light_ae1",

"api": "A01.com.company.lightApp1",

"rr": true,

"poa": ["http://192.168.0.10:9090"],

"acpi": ["/mn-cse/acp-805496226"]

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-92345

Content-Location: /mn-cse/ae-CAE340304071

#### 8.7.4.2	Light application ADN-AE2

The registration of ADN-AE2 with MN-CSE is shown in the following procedure. Note that the access control policy identifier (unstructured SP-relative resourceID) which is assigned to ADN-AE2 is /mn-cse/acp-805496226.

The following example shows an ADN-AE registration request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/xml;ty=2

X-M2M-RI: mncse-18346

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light_ae2">

<api>A01.com.company.lightApp2</api>

<rr>true</rr>

<poa>http://192.168.0.20:9090</poa>

<acpi>/mn-cse/acp-805496226</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-18346

Content-Location: /mn-cse/ae-CAE340304042

The following example shows an ADN-AE registration request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/json;ty=2

X-M2M-RI: mncse-18346

{

"m2m:ae":

{

"rn": "light_ae2",

"api": "A01.com.company.lightApp2",

"rr": true,

"poa": ["http://192.168.0.20:9090"],

"acpi": ["/mn-cse/acp-805496226"]

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-18346

Content-Location: /mn-cse/ae-CAE340304042

#### 8.7.4.3	Home gateway application MN-AE

The registration of MN-AE with MN-CSE is shown in the following procedure. Note that the access control policy identifier (unstructured SP-relative resourceID) which is assigned to MN-AE is /mn-cse/acp-805496226.

The following example shows an MN-AE registration request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/xml;ty=2

X-M2M-RI: mncse-19347

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="gateway_ae">

<api>A01.com.company.gatewayApp</api>

<rr>false</rr>

<acpi>/mn-cse/acp-805496226</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-19347

Content-Location: /mn-cse/ae-CAE340303271

The following example shows an MN-AE registration request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/json;ty=2

X-M2M-RI: mncse-19347

{

"m2m:ae":

{

"rn": "gateway_ae",

"api": "A01.com.company.gatewayApp",

"rr": false,

"acpi": ["/mn-cse/acp-805496226"]

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-19347

Content-Location: /mn-cse/ae-CAE340303271

#### 8.7.4.4	Smartphone application IN-AE

The registration of IN-AE with IN-CSE is shown in the following procedure. Note that the access control policy identifier (unstructured SP-relative resourceID) which is assigned to IN-AE is /in-cse/acp-666957710.

The following example shows an IN-AE registration request and response using HTTP with XML serialization.

HTTP Request:

POST /server?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/xml;ty=2

X-M2M-RI: incse-16346

<?xml version="1.0" encoding="UTF-8"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="smartphone_ae">

<api>A01.com.company.lightControlApp</api>

<rr>false</rr>

<acpi>/in-cse/acp-666957710</acpi>

</m2m:ae>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse-16346

Content-Location: /in-cse/ae-CAE340304178

The following example shows an IN-AE registration request and response using HTTP with JSON serialization.

HTTP Request:

POST /server?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: C
Content-Type: application/json;ty=2

X-M2M-RI: incse-16346

{

"m2m:ae":

{

"rn": "smartphone_ae",

"api": "A01.com.company.lightControlApp",

"rr": false,

"acpi": ["/in-cse/acp-666957710"]

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: incse-16346

Content-Location: /in-cse/ae-CAE340304178

### 8.7.5 	Containers creation

#### 8.7.5.1	Create a container of ADN-AE1

The creation of a container resource for ADN-AE1 is shown in the following procedure.

The following example shows a container create request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway/light_ae1?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/xml;ty=3

X-M2M-RI: mncse/13345

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light">

</m2m:cnt>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-13345

Content-Location: /mn-cse/cnt-582759912

The following example shows a container create request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway/light_ae1?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/json;ty=3

X-M2M-RI: mncse-13345

{

"m2m:cnt":

{

"rn": "light"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-13345

Content-Location: /mn-cse/cnt-582759912

#### 8.7.5.2 	Create a container of ADN-AE2

The creation of a container resource for ADN-AE2 is shown in the following procedure.

The following example shows a container create request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway/light_ae2?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae2
Content-Type: application/xml;ty=3

X-M2M-RI: mncse-62345

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light">

</m2m:cnt>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-62345

Content-Location: /mn-cse/cnt-582769893

The following example shows a container create request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway/light_ae2?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae2
Content-Type: application/json;ty=3

X-M2M-RI: mncse-62345

{

"m2m:cnt":

{

"rn": "light"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-62345

Content-Location: /mn-cse/cnt-582769893

### 8.7.6 	ContentInstances creation

#### 8.7.6.1	Create a content instance of ADN-AE1

The creation of a content instance resource under the light container of ADN-AE1 with initial content OFF is shown in the following procedure.

The following example shows a contentInstance create request and response using HTTP with XML serialization.:

HTTP Request:

POST /home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/xml;ty=4

X-M2M-RI: mncse-24345

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<cnf>text/plain:0</cnf>

<con>OFF</con>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-24345

Content-Location: /mn-cse/cin-394798749

Content-Type: application/xml

The following example shows a contentInstance create request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/json;ty=4

X-M2M-RI: mncse-24345

{

"m2m:cin":

{

"cnf": "text/plains:0",

"con": "OFF"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-24345

Content-Location: /mn-cse/cin-394798749

Content-Type: application/json

#### 8.7.6.2	Create a content instance of ADN-AE2

The creation of a content instance resource under the light container of ADN-AE2 with initial content OFF is shown in the following procedure.

The following example shows a contentInstance create request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/xml;ty=4

X-M2M-RI: mncse-22345

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<cnf>text/plain:0</cnf>

<con>OFF</con>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-22345

Content-Location: /mn-cse/cin-256599578

The following example shows a contentInstance create request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/json;ty=4

X-M2M-RI: mncse-22345

{

"m2m:cin":

{

"cnf": "text/plains:0",

"con": "OFF"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-22345

Content-Location: /mn-cse/cin-256599578

### 8.7.7 	Group creation

The creation of a group resource by the MN-AE is shown in the following procedure. The group resource is created with two initial member ids of the light container resources..

The following example shows a group create request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway/gateway_ae?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Cgateway_ae
Content-Type: application/xml;ty=9

X-M2M-RI: mncse-76905

<?xml version="1.0" encoding="UTF-8"?>

<m2m:grp xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="containers_grp">

<mt>3</mt>

<mid>/mn-cse/cnt-582759912 /mn-cse/cnt-582769893</mid>

<mnm>10</mnm>

</m2m:grp>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-76905

Content-Location: /mn-cse/grp-977978327

The following example shows a group create request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway/gateway_ae?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Cgateway_ae
Content-Type: application/json;ty=9

X-M2M-RI: mncse-76905

{

"m2m:grp":

{

"rn":"containers_grp",

"mt": 3,

"mid":["/mn-cse/cnt-582759912", "/mn-cse/cnt-582769893"],

"mnm": 10

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-76905

Content-Location: /mn-cse/grp-977978327

### 8.7.8 	Subscriptions creation

#### 8.7.8.1	Subscription to the content instance of ADN-AE1

When a subscription resource is created, the notification content type (short for nct) parameter is set to a value 1 to indicate that all attributes of the subscribed resource will be notified to the subscriber.

ADN-AE1 creates a subscription resource including the notification URI set to the resource identifier of ADN-AE1 so that the ADN-AE1 will get notified whenever a content instance child resource is created in the container .  The corresponding subscription create request is shown in the following procedure.

The following example shows a subscription create request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/xml;ty=23

X-M2M-RI: mncse-67891

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sub xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="lightstate_sub1">

<enc>

<net>3</net>

</enc>

<nu>Clight_ae1</nu>

<nct>1</nct>

</m2m:sub>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-67891

Content-Location: /mn-cse/sub-856593979

The following example shows a subscription create request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae1
Content-Type: application/json;ty=23

X-M2M-RI: mncse-67891

{

"m2m:sub":

{

"rn": "lightstate_sub1",

"enc":

{

"net":[3]

},

"nu":["Clight_ae1"],

"nct":1

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-67891

Content-Location: /mn-cse/sub-856593979

#### 8.7.8.2	Subscription to the content instance of ADN-AE2

When a subscription resource is created, the notification content type (short for nct) parameter is set to a value 1 to indicate that all attributes of the subscribed resource will be notified to the subscriber.

ADN-AE1 creates a subscription resource including the notification URI set to the resource identifier of ADN-AE1 so that the ADN-AE1 will get notified whenever a content instance child resource is created in the container .  The corresponding subscription create request is shown in the following procedure.

When a subscription resource is created, the notification content type (short for nct) parameter is set to value 1 to indicate that all attributes of the subscribed resource will be notified to the subscriber.

ADN-AE2 creates a subscription resource including the notification URI set to the resource identifier of ADN-AE2 so that the ADN-AE2 will get notified whenever a content instance child resource is created in the container.  The corresponding subscription create request is shown in the following procedures.

The following example shows a subscription create request and response using HTTP with XML serialization.

HTTP Request:

POST /home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae2
Content-Type: application/xml;ty=23

X-M2M-RI: mncse-29387

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sub xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="lightstate_sub2">

<enc>

<net>3</net>

</enc>

<nu>Clight_ae2</nu>

<nct>1</nct>

</m2m:sub>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-29387

Content-Location: /mn-cse/sub-856463728

The following example shows a subscription create request and response using HTTP with JSON serialization.

HTTP Request:

POST /home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: Clight_ae2
Content-Type: application/json;ty=23

X-M2M-RI: mncse-29387

{

"m2m:sub":

{

"rn": "lightstate_sub2",

"enc":

{

"net":[3]

},

"nu":["Clight_ae2"],

"nct":1

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-29387

Content-Location: /mn-cse/sub-856463728

### 8.7.9 	Discovery

#### 8.7.9.1	Introduction

The discovery functionality in oneM2M is implemented using a RETRIEVE operation along with one or multiple filter criteria parameters.

In order to enable the retrieve operation for resource discovery, parameter filterUsage (short for fu) is included in the RETRIEVE request as a query string.

In addition, parameter resource type (short for rty) is used as a filterCriteria condition for the discovery of single light and group light members. The parameter discovery result type (short for drt) is set to 2 to indicate that the format of elements of URIList is unstructured. The detailed discovery procedures are presented in clauses 8.7.9.2 and 8.7.9.3.

#### 8.7.9.2	Discovery of single light registered with MN-CSE

The discovery of containers for each light registered with the MN-CSE by the smartphone AE is shown in the  following procedure.

If the discovery response is preferred to be returned with a XML representation, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=3&drt=2 HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-99882
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-99882

X-M2M-CNST: 2

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:uril xmlns:m2m="http://www.onem2m.org/xml/protocols">

/mn-cse/cnt-582759912

/mn-cse/cnt-582769893

</m2m:uril>

If the discovery response is preferred to be returned with a JSON representation, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=3&drt=2 HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-99882
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-99882

X-M2M-CNST: 2

Content-Type: application/json

{

"m2m:uril":

[

"/mn-cse/cnt-582759912",

"/mn-cse/cnt-582769893"

]

}

The smartphone application retrieves a list of URIs representing containers registered with MN-CSE from the response message, e.g. /mn-cse/cnt-582759912 which is the URI of container created in ADN-AE1. The retrieved URIs of the discovered containers are then used for the group member update operation.

#### 8.7.9.3	Discovery of groups located in MN-CSE

The discovery of groups located in MN-CSE by the smartphone AE is shown in the following procedures.

If the discovery response is preferred to be returned with a XML representation, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=9&drt=2 HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-15001
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-15001

X-M2M-CNST: 2

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:uril xmlns:m2m="http://www.onem2m.org/xml/protocols">

/mn-cse/grp-977978327

</m2m:uril>

If the discovery response is preferred to be returned with a JSON representation, the HTTP request message is sent as following example:

HTTP Request:

GET /~/mn-cse/home_gateway?fu=1&rty=9&drt=2 HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-15001
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-15001

X-M2M-CNST: 2Content-Type: application/json

{

"m2m:uril":

[

"/mn-cse/grp-977978327"

]

}

The smartphone application retrieves a list of URIs representing group resources located in MN-CSE from the response message, e.g. /mn-cse/grp-977978327 which is the URI of the group resource. The retrieved URIs of the discovered group resource are then used for the group member update operation.

### 8.7.10 	Latest content instances retrieval

#### 8.7.10.1	Introduction

The smartphone application can retrieve the latest light states via sending a RETRIEVE request targeting a container’s la (short for latest) virtual resource.

The smartphone application can also retrieve a group of latest light states via sending a RETRIEVE request targeting the group fanOutPoint virtual resource.

#### 8.7.10.2	Retrieve the latest content instance of ADN-AE1

The latest content instance of the light container resource for ADN-AE1 can be retrieved by the following procedure.

If the response is preferred to be returned with a XML representation, the following is a HTTP request message example:

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae1/light/la HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-11223
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-11223

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin

xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="cin-394798749">

<ty>4</ty>

<ri>cin-394798749</ri>

<pi>cnt-181049109</pi>

<ct>20150925T045938</ct>

<lt>20150925T045938</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

If the response is preferred to be returned with a JSON representation, the following is a HTTP request message example:

GET /~/mn-cse/home_gateway/light_ae1/light/lat HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-11223
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-11223

Content-Type: application/json

{

"m2m:cin":

{

"ty":4,

"ri":"cin-394798749",

"pi":"cnt-181049109",

"rn":"cin-394798749",

"ct":"20150925T045938",

"lt":"20150925T045938",

"et":"20151107T154802",

"st":0,

"cnf":"text/plain:0",

"cs":3,

"con":"OFF"

}

}

#### 8.7.10.3	Retrieve the latest content instance of ADN-AE2

The latest content instance of the light container resource for ADN-AE2 can be retrieved by the following procedures.

If the response is preferred to be represented in XML, the following is a HTTP request message example:

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae2/light/la HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-22336
Accept: application/xml

HTTP Response:

200 OK
X-M2M-RSC: 2000

X-M2M-RI: mncse-22336

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin

xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="cin-256599578">

<ty>4</ty>

<ri>cin-256599578</ri>

<pi>cnt-790965889</pi>

<ct>20150925T050515</ct>

<lt>20150925T050515</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

If the response is preferred be returned in representation of JSON, the following is a HTTP request message example:

GET /~/mn-HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-22336
Accept: application/json

HTTP Response:

200 OK
X-M2M-RSC: 2000

X-M2M-RI: mncse-22336

Content-Type: application/json

{

"m2m:cin":

{

"ty":4,

"ri": "cin-256599578",

"pi": "cnt-790965889",

"rn": "cin-256599578",

"ct": "20150925T050515",

"lt": "20150925T050515",

"et": "20151107T154802",

"st": 0,

"cnf": "text/plain:0",

"vcs": 3,

"con": "OFF"

}

}

#### 8.7.10.4	Retrieve a group of latest content instances for all light states

A group of latest content instances can be retrieved via sending a RETRIEVE request targeting the group fanOutPoint virtual resource and appending  latest as shown in the following procedures.

If the response is preferred to be returned with a XML representation, the following is a HTTP request message example:

HTTP Request:

GET /~/mn-cse/home_gateway/gateway_ae/containers_grp/fopt/la HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-55667
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-55667

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:agr

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<m2m:rsp>

<rsc>2000</rsc>

<rqi>mncse-55667</rqi>

<pc>

<m2m:cin rn="cin-394798749">

<ty>4</ty>

<ri>cin-394798749</ri>

<pi>cnt-181049109</pi>

<ct>20150925T045938</ct>

<lt>20150925T045938</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

</pc>

<to>/in-cse/Csmartphone_ae</to>

<fr>/mn-cse/cnt-582759912/la</fr>

</m2m:rsp>

<m2m:rsp>

<rsc>2000</rsc>

<rqi>mncse-55667</rqi>

<pc>

<m2m:cin rn="cin-256599578">

<ty>4</ty>

<ri>cin-256599578</ri>

<pi>cnt-790965889</pi>

<ct>20150925T050515</ct>

<lt>20150925T050515</lt>

<et>20151107T154802</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>3</cs>

<con>OFF</con>

</m2m:cin>

</pc>

<to>/in-cse/Csmartphone_ae</to>

<fr>/mn-cse/cnt-582769893/la</fr>

</m2m:rsp>

</m2m:agr>

If the response is preferred to be returned with a JSON representation, the following is a HTTP request message example:

HTTP Request:

GET /~/mn-cse/home_gateway/containers_grp/fopt/la HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-55667
Accept: application/json

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-55667

Content-Type: application/json

{

"m2m:agr":

{

"m2m:rsp":[

{

"rsc": 2000,

"rqi": "mncse-55667",

"pc":

{

"m2m:cin":

{

"ty":4,

"ri": "cin-394798749",

"pi": "cnt-181049109",

"rn": "cin-394798749",

"ct": "20150925T045938",

"lt": "20150925T045938",

"et": "20151107T154802",

"st": 0,

"cnf":"text/plain:0",

"cs": 3,

"con": "OFF"

}

},

"to":"/in-cse/Csmartphone_ae",

"fr":"/mn-cse/cnt-582759912/la"

},

{

"rsc":2000,

"rqi": "mncse-55667",

"pc":

{

"m2m:cin":

{

"ty":4,

"ri":"cin-256599578",

"pi":"cnt-790965889",

"rn":"cin-256599578",

"ct":"20150925T050515",

"lt":"20150925T050515",

"et":"20151107T154802",

"st":0,

"cnf":"text/plain:0",

"cs":3,

"con":"OFF"

}

},

"to":"/in-cse/Csmartphone_ae",

"fr":"/mn-cse/cnt-582769893/la"

}

]}

}

### 8.7.11 	Light state modification

#### 8.7.11.1	Introduction

Once the smartphone application is registered with the IN-CSE, it can be granted access to resources including containers located in the MN-CSE so that smartphone application users can send light control commands for modifying the light states.

When the user makes a change to the light state via the smartphone user interface, the smartphone application performs a new content instance creation procedure carrying the new state.

The modification of a single light state is implemented by creating a new content instance resource for the specific container with access control policy acp1 (gateway_acp) while the modification of all light states is implemented by creating a new content instance resource for each member of group (containers_grp) with access control policy acp1 (gateway_acp). The implementation of the latter case is to target the  <fopt> virtual resource of containers_grp resource with a content instance create request so that the content of all members of the group is updated together.

#### 8.7.11.2	Create a content instance under container of ADN-AE1

If the contentInstance create request body is represented in XML, the following is a HTTP request message example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/xml;ty=4

X-M2M-RI: mncse-11123

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<cnf>text/plain:0</cnf>

<con>ON</con>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-11123

Content-Location: /mn-cse/cin-789356234

If the contentInstance create request body is represented in JSON, the following is a HTTP request message example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae1/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/json;ty=4

X-M2M-RI: mncse-11123

{

"m2m:cin":

{

"cnf": "text/plains:0",

"con": "ON"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-11123

Content-Location: /mn-cse/cin-789356234

#### 8.7.11.3	Create a content instance under container of ADN-AE2

If the contentInstance create request body is represented in XML, the following is an HTTP request message the example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/xml;ty=4

X-M2M-RI: mncse-12222

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<cnf>text/plain:0</cnf>

<con>ON</con>

</m2m:cin>

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse/12222

Content-Location: /mn-cse-cin-237896783

If the contentInstance create request body is represented in JSON, the following is a HTTP request message example:

HTTP Request:

POST /~/mn-cse/home_gateway/light_ae2/light?rcn=0 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/json;ty=4

X-M2M-RI: mncse-12222

{

"m2m:cin":

{

"cnf": "text/plains:0",

"con": "ON"

}

}

HTTP Response:

201 Created

X-M2M-RSC: 2001

X-M2M-RI: mncse-12222

Content-Location: /mn-cse/cin-237896783

#### 8.7.11.4	Update  the state of all lights using group fanout

If the fanOutPoint request body is represented in XML, the following is a HTTP request message example:

HTTP Request:

POST /~/mn-cse/home_gateway/gateway_ae/containers_grp/fopt HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/xml

X-M2M-RI: mncse-33344

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin xmlns:m2m="http://www.onem2m.org/xml/protocols">

<cnf>text/plain:0</cnf>

<con>ON</con>

</m2m:cin>

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-33344

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:agr

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<m2m:rsp>

<rsc>2001</rsc>

<rqi>mncse-33344</rqi>

<pc>

<m2m:cin rn="cin-479874939">

<ty>4</ty>

<ri>cin-479874939</ri>

<pi>cnt-181049109</pi>

<ct>20151025T045938</ct>

<lt>20151025T045938</lt>

<et>20151207T154802</et>

<st>0</st>

<cs>2</cs>

</m2m:cin>

</pc>

<to>/in-cse/Csmartphone_ae</to>

<fr>/mn-cse/cnt-582759912</fr>

</m2m:rsp>

<m2m:rsp>

<rsc>2001</rsc>

<rqi>mncse-33344</rqi>

<pc>

<m2m:cin rn="cin-659957825">

<ty>4</ty>

<ri>cin-659957825</ri>

<pi>cnt-790965889</pi>

<ct>20151025T045938</ct>

<lt>20151025T045938</lt>

<et>20151207T154802</et>

<st>0</st>

<cs>2</cs>

</m2m:cin>

</pc>

<to>/in-cse/Csmartphone_ae</to>

<fr>/mn-cse/cnt-582769893</fr>

</m2m:rsp>

</m2m:agr>

If the fanOutPoint request body is represented in JSON, the following is a HTTP request message example:

HTTP Request:

POST /~/mn-cse/home_HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae
Content-Type: application/json

X-M2M-RI: mncse-33344

{

"m2m:cin":

{

"cnf": "text/plains:0",

"con": "ON"

}

}

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-33344

Content-Type: application/json

{

"m2m:agr":

{

"m2m:rsp":

[{

"rsc": 2001,

"rqi":"mncse-33344",

"pc":

{

"m2m:cin":

{

"ty": 4,

"ri": "cin-479874939",

"pi": "cnt-181049109",

"rn": "cin-479874939",

"ct": "20151025T045938",

"lt": "20151025T045938",

"et": "20151207T154802",

"st": 0,

"cs": 2

}

},

"to": "/in-cse/Csmartphone_ae",

"fr": "/mn-cse/cnt-582759912"

},

{

"rsc": 2001,

"rqi": "mncse-33344",

"pc":

{

"m2m:cin":

{

"ty": 4,

"ri": "cin-659957825",

"pi": "cnt-790965889",

"rn": "cin-659957825",

"ct": "20151025T050515",

"lt": "20151025T050515",

"et": "20151207T154802",

"st": 0,

"cs": 2

}

},

"to": "/in-cse/Csmartphone_ae ",

"fr": "/mn-cse/cnt-582769893"

}

]}

}

### 8.7.12 	Notifications

#### 8.7.12.1	Introduction

Each time a content instance is created under a container of an ADN-AE, then a notification containing the whole created content instance is posted to the targeted subscriber i.e. ADN-AE1 or ADN-AE2, that can actuate the light with the new state received in the notification.

#### 8.7.12.2	Post a notification to ADN-AE1

If the notification request body is represented in XML, the following is a HTTP request message example:

HTTP Request:

POST / HTTP/1.1

Host: 192.168.0.10:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif-12345

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sgn

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<nev>

<rep>

<m2m:cin>

<cnf>text/plain:0</cnf>

<con>ON</con>

</m2m:cin>

</rep>

</nev>

<sur>

/mn-cse/sub-856593979

</sur>

</m2m:sgn>

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: notif-12345

If the notification request body is represented in JSON, the following is a HTTP request message:

HTTP Request:

POST / HTTP/1.1

Host: 192.168.0.10:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif-12345

Content-Type: application/json

{

"m2m:sgn":

{

"nev":{

"rep":

{

"cin":

{

"cnf": "text/plain:0"	,

"con": "ON"

},

"rss":201

}

},

"sur":"/mn-cse/sub-856593979"

}

}

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: notif-12345

#### 8.7.12.3	Post a notification to ADN-AE2

If the notification request body is represented in XML, the following is a HTTP request message example:

HTTP Request:

POST /  HTTP/1.1

Host: 192.168.0.20:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif-12346

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:sgn

xmlns:m2m="http://www.onem2m.org/xml/protocols">

<nev>

<rep>

<cin>

<cnf>text/plain:0</cnf>

<con>ON</con>

</cin>

<rss>201</rss>

</rep>

</nev>

<sur>

/mn-cse/sub-856463728

</sur>

</m2m:sgn>

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI:  notif-12346

If the notification request body is represented in JSON, the following is a HTTP request message example:

HTTP Request:

POST /  HTTP/1.1

Host: 192.168.0.20:9090

X-M2M-Origin: /mn-cse

X-M2M-RI: notif-12346

Content-Type: application/json

{

"m2m:sgn":

{

"nev":{

"rep":

{

"cin":

{

"cnf": "text/plain:0"	,

"con": "ON"

},

"rss":201

}

},

"sur":"/mn-cse/sub-856463728"

}

}

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI:  notif-12346

Annex A: 
Reading Resources

## Annex A.1 Introduction

The information of resources created during each call flow of current use case can be retrieved via smartphone application IN-AE initiates a RETRIEVE request to the target resources as following.

## Annex A.2 CSE resources

### Annex A.2.1 IN-CSE

HTTP Request:

GET /~/in-cse/server HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: incse-12345
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: incse-12345

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cb xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="server">

<ty>5</ty>

<ri>/in-cse</ri>

<ct>20150925T045938</ct>

<lt>20150925T045938</lt>

<acpi>/in-cse/acp-666957710</acpi>

<cst>1</cst>

<csi>in-cse</csi>

<srt>1 2 3 4 5 9 14 15 16 17 23</srt>

<poa>http://in.provider.com:8080/</poa>

</m2m:cb>

### Annext A.2.2 MN-CSE

HTTP Request:

GET /~/in-cse/server/home_gateway HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: incse-12346
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: incse-12346

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:csr xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="home_gateway">

<ty>16</ty>

<ri>csr-299409504</ri>

<pi>/in-cse</pi>

<ct>20150925T045938</ct>

<lt>20150925T045938</lt>

<et>20171005T105550</et>

<acpi>/in-cse/acp-666957710</acpi>

<poa>http://mn.provider.com:8080/</poa>

<cb>mn.provider.com/mn-cse</cb>

<csi>/mn-cse</csi>

<rr>true</rr>

</m2m:csr>

## Annex A.3 Gateway device application MN-AE

HTTP Request:

GET /~/mn-cse/home_gateway/gateway_ae HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-12347
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12347

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="gateway_ae">

<ty>2</ty>

<ri>ae-CAE340303271</ri>

<pi>/mn-cse</pi>

<ct>20150925T052438</ct>

<lt>20150925T052438</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226</acpi>

<api>A01.com.company.gatewayApp</api>

<aei>CAE340303271</aei>

<rr>false</rr>

</m2m:ae>

## Annex A.4. Light device applications

### Annex A.4.1 ADN-AE1

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae1 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12347
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12347

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light_ae1">

<ty>2</ty>

<ri>ae-CAE340304071</ri>

<pi>/mn-cse</pi>

<ct>20150925T052455</ct>

<lt>20150925T052455</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226</acpi>

<api>A01.com.company.lightApp1</api>

<aei>CAE340304071</aei>

<rr>true</rr>

</m2m:ae>

### Annex A.4.2 ADN-AE2

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae2 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12348
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12348

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light_ae2">

<ty>2</ty>

<ri>ae-CAE340304042</ri>

<pi>/mn-cse</pi>

<ct>20150925T052542</ct>

<lt>20150925T052542</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226</acpi>

<api>A01.com.company.lightApp2</api>

<aei>CAE340304042</aei>

<rr>true</rr>

</m2m:ae>

## Annex A.5 Smartphone application IN-AE

HTTP Request:

GET /~/in-cse/server/smartphone_ae HTTP/1.1
Host: in.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: incse-12349
Accept: application/xml

Resonse status:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: incse-12349

Content-Type: application/xml

Resonse message:

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:ae xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="smartphone_ae">

<ty>2</ty>

<ri>ae-CAE340304178</ri>

<pi>/in-cse</pi>

<ct>20150925T052622</ct>

<lt>20150925T052622</lt>

<et>20171005T105550</et>

<acpi>/in-cse/acp-666957710</acpi>

<api>A01.com.company.lightControlApp</api>

<aei>CAE340304178</aei>

<rr>false</rr>

</m2m:ae>

## Annex A.6 Access control policy

HTTP Request:

GET /~/mn-cse/home_gateway/gateway_acp HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12350
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12350

Content-Type: application/xml

<m2m:acp xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="gateway_acp">

<ty>1</ty>

<ri>acp-805496226</ri>

<pi>/mn-cse</pi>

<ct>20150925T050238</ct>

<lt>20150925T050238</lt>

<et>20171005T105550</et>

<pv>

<acr>

<acor>/in-cse/home_gateway /mn-cse/Cgateway_ae /mn-cse/Clight_ae1 /mn-cse/Clight_ae2 /in-cse/Csmartphone_ae</acor>

<acop>63</acop>

</acr>

</pv>

<pvs>

<acr>

<acor>/in-cse/home_gateway /mn-cse/Cgateway_ae /mn-cse/Clight_ae1 /mn-cse/Clight_ae2 /in-cse/Csmartphone_ae</acor>

<acop>51</acop>

</acr>

</pvs>

</m2m:acp>

## Annex A.7 Containers

### Annex A.7.1 Container under ADN-AE1

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae1/light HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12351
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12351

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light">

<ty>3</ty>

<ri>cnt-582759912</ri>

<pi>/mn-cse/ae-CAE340304071</pi>

<ct>20150925T052955</ct>

<lt>20150925T052955</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226</acpi>

<st>0</st>

<cni>1</cni>

<cbs>3</cbs>

</m2m:cnt>

### Annex A.7.2 Container under ADN-AE2

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae2/light HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12352
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12352

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:cnt xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="light">

<ty>3</ty>

<ri>cnt-582769893</ri>

<pi>/mn-cse/ae-CAE340304042</pi>

<ct>20150925T053135</ct>

<lt>20150925T053135</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226</acpi>

<st>0</st>

<cni>1</cni>

<cbs>3</cbs>

</m2m:cnt>

## Annex A.8 ContentInstances

### Annex A.8.1 Latest contentInstance in ADN-AE1

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae1/light/la HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12353
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12353

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin

xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="cin-394798749">

<ty>4</ty>

<ri>cin-394798749</ri>

<pi>/mn-cse/cnt-582759912</pi>

<ct>20150925T053225</ct>

<lt>20150925T053225</lt>

<et>20171005T105550</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>2</cs>

<con>ON</con>

</m2m:cin>

### Annex A.8.2 Latest contentInstance in ADN-AE2

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae2/light/la HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12354
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12354

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:cin

xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="cin-256599578">

<ty>4</ty>

<ri>cin-256599578</ri>

<pi>/mn-cse/cnt-582769893</pi>

<ct>20150925T053425</ct>

<lt>20150925T053425</lt>

<et>20171005T105550</et>

<st>0</st>

<cnf>text/plain:0</cnf>

<cs>2</cs>

<con>ON</con>

</m2m:cin>

## Annex A.9 Subscriptions

### Annex A.9.1 Subscription to container in ADN-AE1

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae1/light/lightstate_sub1 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12355
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12355

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:sub xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="lightstate_sub1">

<ty>23</ty>

<ri>sub-856593979</ri>

<pi>/mn-cse/cnt-582759912</pi>

<ct>20150926T052955</ct>

<lt>20150926T052955</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226</acpi>

<enc>

<net>3</net>

</enc>

<nu>/mn-cse/ae-CAE340304071</nu>

<nct>1</nct>

</m2m:sub>

### Annex A.9.2 Subscription to container in ADN-AE2

HTTP Request:

GET /~/mn-cse/home_gateway/light_ae2/light/lightstate_sub2 HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /mn-cse/Cgateway_ae

X-M2M-RI: mncse-12356
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12356rs

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8" standalone="yes"?>

<m2m:sub xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="lightstate_sub2">

<ty>23</ty>

<ri>sub-856463728</ri>

<pi>/mn-cse/cnt-582759912</pi>

<ct>20150926T053055</ct>

<lt>20150926T053055</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226</acpi>

<enc>

<net>3</net>

</enc>

<nu>/mn-cse/ae-CAE340304042</nu>

<nct>1</nct>

</m2m:sub>

## Annex A.10 Groups

### Annex A.10.1 Group1

HTTP Request:

GET /~/mn-cse/home_gateway/gateway_ae/containers_grp HTTP/1.1
Host: mn.provider.com:8080
X-M2M-Origin: /in-cse/Csmartphone_ae

X-M2M-RI: mncse-12357
Accept: application/xml

HTTP Response:

200 OK

X-M2M-RSC: 2000

X-M2M-RI: mncse-12357

Content-Type: application/xml

<?xml version="1.0" encoding="UTF-8"?>

<m2m:grp xmlns:m2m="http://www.onem2m.org/xml/protocols" rn="containers_grp">

<ty>9</ty>

<ri>grp-977978327</ri>

<pi>/mn-cse/ae-CAE340303271</pi>

<ct>20151004T045954</ct>

<lt>20151004T045954</lt>

<et>20171005T105550</et>

<acpi>/mn-cse/acp-805496226 /mn-cse/acp-805496226</acpi>

<mt>3</mt>

<cnm>2</cnm>

<mnm>10</mnm>

<mid>/mn-cse/cnt-582759912 /mn-cse/cnt-582769893</mid>

<mtv>true</mtv>

<csy>1</csy>

<fopt>/mn-cse/grp-977978327/fopt</fopt>

</m2m:grp>

### ----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

This is erroneous. Please prepare a CR to remove the “rss” attribute!!