| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#30 |
| Source:* | Maciej Goluch, ORANGE, maciej.goluch@orange.com, Pawel Srzemecki, ORANGE |
| Date:* | 2017-07-07 |
| Reason for Change/s:* | Improve pseudocode for implementation example |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0054> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0039 ‘Developer guide: Interworking Proxy using SDT’ |
| Clauses * | 9 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This document improve the pseudocode example of  SDT and IPE implementation to make both simpler to understand. It helps to understand how to connect external non-oneM2M devices to oneM2M network.

### -----------------------Start of change 1 -------------------------

### 9.3.3 Implementation of abstract SDT Device example: deviceLight

This section presents a “pseudo code” implementation of abstract SDT Device based on deviceLight example. Please note that this pseudo-code is similar to Java but should be considering just an example, it isn’t attend to be compilable.

/**

*

* Stores information about name and domain of the device

*

*/

class Device{

string name;

string domain;

public Device(string name, string domain){

name = name;

domain = domain;

}

}

/**
* DeviceLight class is an implementation of deviceLight model, it inherits from Device * class, and has 8 fields relevant for 8 ModuleClasses of deviceLight model.
* DeviceLight has a contructor which creates objects for ModuleClasses and defines 
* Name and Domain.
*/

class DeviceLight extends Device{

FaultDetection faultDetection;

BinarySwitch binarySwitch;

RunMode runMode;

Colour colour;

ColourSaturation colourSaturation;

Brightness brightness;

public DeviceLight(string name, string domain){

super(name, domain);

}

}

/**

* Module consists of 3 fields which are relevant to DataPoints parameters in SDT.

*/

class Module{

boolean optional;

string name;

string domain;

public Module(string name, string domain, boolean optional){

this.name = name;

this.optional = optional;

this.domain = domain;

}

}

/**

* BinarySwitch class is considered as an example of ModuleClass implementation,

* it inherits from Module. It has fields relevant for Datapoints and Actions

* which are defined in SDT data model. Constructor of BinarySwitch creates powerState

* Datapoint. BinarySwitch class has also setToggle function which allows to set toogle

* action which is not mandatory.

*/

class BinarySwitch extends Module {

BooleanDataPoint powerState;

Toggle toggle;

public BinarySwitch(string moduleName, string moduleDomain, BooleanDataPoint powerStateArgument){

super(moduleName, moduleDomain, false);

powerState = powerStateArgument;

powerState.optional = false;

powerState.readable = true;

powerState.writeable = true;

powerState.documentation = "The current status of the binarySwitch. "True"

indicates turned-on, and "False" indicates turned-off";

}

void setToggle(Toggle toggleArgument){

toggle = toggleArgument;

toggle.optional = true;

}

}

/**

* Colour extends Module and has 3 fields relevant to Colour ModuleClass Datapoints.

* In the constructor of Colour class there are DataPoints assingments with their

* parameters. There's also abstract setColour method which allows to set

* all colours (R,G,B) at once.

*/

class Colour extends Module {

IntegerDataPoint red;

IntegerDataPoint green;

IntegerDataPoint blue;

public Colour(string moduleName, string moduleDomain, IntegerDataPoint redArgument, IntegerDataPoint greenArgument, IntegerDataPoint blueArgument){

super(moduleName, moduleDomain, true);

red = redArgument;

green = greenArgument;

blude = blueArgument;

red.optional = false;

red.readable = true;

red.writeable = true;

red.documentation = "";

green.optional = false;

green.readable = true;

green.writeable = true;

green.documentation = "";

blue.optional = false;

blue.readable = true;

blue.writeable = true;

blue.documentation = "";

}

/**

* This method allows to set all colours (R,G,B) in a single call.

* Since it is an abstract method it has to be implemented by developer according to

* specific technology which the device uses.

*/

public abstract setColour(int R, int G, int B);

}

/**

* Toggle class consists of 3 fields which are relevant to SDT Action parameters and

* toggle() method which determines Toggle Action.

*/

class Toggle {

boolean optional = true;

string documentation;

string name;

public abstract void toggle(){}

public Toggle(boolean optional, string documentation, string name){

this.optional = optional;

this.documentation = documentation;

this.name = name;

}

}

/**

* DataPoint class constis of 6 fields relevant to DataPoint SDT parameters.

* In the constructor there's name and type assingments. The rest of paremeters are

* assingments in classes which inherits from DataPoint class.

*/

class DataPoint{

string name;

string type;

boolean optional;

bool readable;

bool writeable;

string documentation;

public DataPoint(string nameArgument, string typeArgument){

name = nameArgument;

type = typeArgument;

}

}

/**

* IntegerDataPoint class consists of two abstract methods getValue() and setValue()

* which are implemented in HueLight class in 9.3.4 clause.

* Notice there is DataPoint constructor called in IntegerDataPoint constructor.

*/

public abstract class IntegerDataPoint extends DataPoint{

public IntegerDataPoint(string name){

super(name, "Integer");

}

abstract int getValue(){};

abstract void setValue(int value){};

}

/**

* BooleanDataPoint class consists of two abstract methods getValue() and setValue()

* which are implemented in HueLight class in 9.3.4 clause.

* Notice there is DataPoint constructor called in BooleanDataPoint constructor.

*/

public abstract class BooleanDataPoint extends DataPoint{

public BooleanDataPoint(string name){

super(name, "Boolean");

}

abstract boolean getValue();

abstract void setValue(boolean value);

}

- 9.3.4 Instance of SDT Device example: Hue Light

This section presents a “pseudo code” implementation of IPE for particular device: Hue Light. Please note that this pseudo-code is similar to Java but should be considering just an example, it isn’t attend to be compilable.

/**

* HueLight class inherits from DeviceLight class. In the contructor of this class

* DataPoints are created with all needed abstract methods implementation

* specific for technology (Hue Light in this use case) the device uses. It means that

* each DataPoint (e.g. powerState in BinarySwitch) has implementation of each abstract * method which consists of Hue API calls to control Hue Light.

*/

class HueLight extends DeviceLight{

public HueLight(string name, string domain){

super(name, domain);

}

BinarySwitch = new BinarySwitch("binarySwitch", domain, 
new BooleanDataPoint("powerState"){

boolean getValue(){

HttpRequest httpRequest;

httpRequest.setURL("http://<bridge_ip_address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setMethod("GET");

bool state = parseOnOff(httpRequest.sendHTTPRequest());

return state;

}

void setValue(boolean value){

HTTPRequest httpRequest;

httpRequest.setURL("http://<bridge_ip_address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setBody("{\"on\":" + value + "}");

httpRequest.setMethod(“PUT”);

httpRequest.sendHTTPRequest();

}

});

Colour = new Colour("colour", domain, new IntegerDataPoint("red"){

int getValue(){

HttpRequest httpRequest;

httpRequest.setURL(http://<bridge ip address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setMethod("GET");

int red = parseRed(parseColor(httpRequest.sendHTTPRequest()));

return red;

}

void setValue(int value){

HSVColour hsv = new HSVColour();

hsv.convertFromRGB(value, 0, 0);

HTTPRequest httpRequest;

httpRequest.setURL("http://<bridge ip address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setBody("{\"on\":true, \"sat\":" + hsv.getSat() + ", \"bri\":" + hsv.getBri() + ",\"hue\":" + hsv.getHue() +"}"});

httpRequest.setMethod(“PUT”)

httpRequest.sendHTTPRequest();

}

}, new IntegerDataPoint("green"){

int getValue(){

HttpRequest httpRequest;

httpRequest.setURL(http://<bridge ip address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setMethod("GET");

int green = parseGreen(parseColor(httpRequest.sendHTTPRequest()));

return green;

}

void setValue(int value){

HSVColour hsv = new HSVColour();

hsv.convertFromRGB(0, value, 0);

HTTPRequest httpRequest;

httpRequest.setURL("http://<bridge ip address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setBody("{\"on\":true, \"sat\":" + hsv.getSat() + ", \"bri\":" + hsv.getBri() + ",\"hue\":" + hsv.getHue() +"}"});

httpRequest.setMethod(“PUT”)

httpRequest.sendHTTPRequest();

}

}, new IntegerDataPoint("blue"){

int getValue(){

HttpRequest httpRequest;

httpRequest.setURL(http://<bridge ip address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setMethod("GET");

int blue = parseBlue(parseColor(httpRequest.sendHTTPRequest()));

return blue;

}

void setValue(int value){

HSVColour hsv = new HSVColour();

hsv.convertFromRGB(0, 0, value);

HTTPRequest httpRequest;

httpRequest.setURL("http://<bridge ip address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setBody("{\"on\":true, \"sat\":" + hsv.getSat() + ", \"bri\":" + hsv.getBri() + ",\"hue\":" + hsv.getHue() +"}"});

httpRequest.setMethod(“PUT”)

httpRequest.sendHTTPRequest();

}

}){

void setColour(int R, int G, int B){

HSVColour hsv = new HSVColour();

hsv.convertFromRGB(R, G, B);

HTTPRequest httpRequest;

httpRequest.setURL("http://<bridge ip address>/api/1028d66426293e821ecfd9ef1a0731df/lights/1/state");

httpRequest.setBody("{\"on\":true, \"sat\":" + hsv.getSat() + ", \"bri\":" + hsv.getBri() + ",\"hue\":" + hsv.getHue() +"}"});

httpRequest.setMethod(“PUT”)

httpRequest.sendHTTPRequest();

}

};

}

/**

* SDT Colour model uses RGB colour values and Hue Light device uses HSV model.

* HSVColour class allows to convert RGB to HSV with its convertFromRGB methods.

* This class and method isn’t a part of SDT data model.

*/

class HSVColour{

int hue;

int sat;

int value;

void convertFromRGB(int R, int G, int B){

//Algorithm that converts RGB values to HSV values should be implemented here

}

}

### -----------------------End of change 1---------------------------------------------