| Input Contribution |
| --- |
| Meeting ID* | TST #30 |
| Title:* | ADN TPs for resource identifier. |
| Source:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Heejin Joung, TTA, heejin.joung.84@tta.or.kr |
| Date:* | 2017-07-08 |
| Input related to* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0018 |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution provides ADN TPs for resource identifier.

## ----------------------- Start of change 1 -----------------------

#### General Capability (GEN)

##### AE/GEN/00001/00001

Support CSE-relative Unstructured resource identifier

###### CREATE OPERATION

TP/oneM2M/AE/GEN/CRE/001

| TP Id | TP/oneM2M/AE/GEN/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT sends the creation of a <container> resource using unstructured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use NON_HIERARCHICAL_RESOURCE_ADDRESS and the IUT having privileges to perform CREATE operation on resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a container CREATE Request } | NA |
|  | then { the IUT sends a valid Container CREATE Request to CSE containing To set to NON_HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID } | CSE ( IUT |

| TP Id | NON_HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/CRE/001_CSR | UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/CRE/001_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/CRE/001_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Unstructured-CSE-Relative-Resource-ID |

###### UPDATE OPERATION

TP/oneM2M/AE/GEN/UPD/001

| TP Id | TP/oneM2M/AE/GEN/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT sends the update of a <container> resource using unstructured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use NON_HIERARCHICAL_RESOURCE_ADDRESS and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS and the IUT having privileges to perform UPDATE operation on resource CONTAINER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send an UPDATE Request on the CONTAINER_RESOURCE_ADDRESS containing Content containing Container resource containing valid labels attribute } | NA |
|  | then { the IUT sends a valid UPDATE request to CSE containing To set to NON_HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID and Content containing Container resource containing valid labels attribute } | IUT ( CSE |

| TP Id | NON_HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/UPD/001_CSR | UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/UPD/001_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/UPD/001_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Unstructured-CSE-Relative-Resource-ID |

###### RETRIEVE OPERATION

TP/oneM2M/AE/GEN/RET/001

| TP Id | TP/oneM2M/AE/GEN/RET/001 |
| --- | --- |
| Test objective | Check that the IUT sends the retrieval of a <container> resource using unstructured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use NON_HIERARCHICAL_RESOURCE_ADDRESS and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS and the IUT having privileges to perform RETRIEVE operation on container resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a RETRIEVE Request on the CONTAINER_RESOURCE_ADDRESS } | NA |
|  | then { the IUT sends a valid RETRIEVE request to CSE containing To set to NON_HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID } | IUT ( CSE |

| TP Id | NON_HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/RET/001_CSR | UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/RET/001_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/RET/001_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Unstructured-CSE-Relative-Resource-ID |

###### DELETE OPERATION

TP/oneM2M/AE/GEN/DEL/001

| TP Id | TP/oneM2M/AE/GEN/DEL/001 |
| --- | --- |
| Test objective | Check that the IUT sends the deletion of a <container> resource using unstructured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use NON_HIERARCHICAL_RESOURCE_ADDRESS and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS and the IUT having privileges to perform DELETE operation on container resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a DELETE Request on the CONTAINER_RESOURCE_ADDRESS } | NA |
|  | then { the IUT sends a valid DELETE request to CSE containing To set to NON_HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID } | IUT ( CSE |

| TP Id | NON_HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/DEL/001_CSR | UNSTRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/DEL/001_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/DEL/001_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Unstructured-CSE-Relative-Resource-ID |

##### AE/GEN/00001/00002

Support SP-relative Unstructured resource identifier

TP/oneM2M/AE/GEN/CRE/001_SPR

TP/oneM2M/AE/GEN/UPD/001_SPR

TP/oneM2M/AE/GEN/RET/001_SPR

TP/oneM2M/AE/GEN/DEL/001_SPR

##### AE/GEN/00001/00003

Support Absolute Unstructured resource identifier

TP/oneM2M/AE/GEN/CRE/001_ABS

TP/oneM2M/AE/GEN/UPD/001_ABS

TP/oneM2M/AE/GEN/RET/001_ABS

TP/oneM2M/AE/GEN/DEL/001_ABS

##### AE/GEN/00001/00004

Support CSE-relative Structured resource identifier

###### CREATE OPERATION

TP/oneM2M/AE/GEN/CRE/002

| TP Id | TP/oneM2M/AE/GEN/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT sends the creation of a <container> resource using structured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_STRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use HIERARCHICAL_RESOURCE_ADDRESS and the IUT having privileges to perform CREATE operation on resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a container CREATE Request } | NA |
|  | then { the IUT sends a valid Container CREATE Request to CSE containing To set to HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID } | CSE ( IUT |

| TP Id | HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/CRE/002_CSR | STRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/CRE/002_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/CRE/002_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Structured-CSE-Relative-Resource-ID |

###### UPDATE OPERATION

TP/oneM2M/AE/GEN/UPD/002

| TP Id | TP/oneM2M/AE/GEN/UPD/002 |
| --- | --- |
| Test objective | Check that the IUT sends the update of a <container> resource using structured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_STRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use HIERARCHICAL_RESOURCE_ADDRESS and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS and the IUT having privileges to perform UPDATE operation on resource CONTAINER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send an UPDATE Request on the CONTAINER_RESOURCE_ADDRESS containing Content containing Container resource containing valid labels attribute } | NA |
|  | then { the IUT sends a valid UPDATE request to CSE containing To set to HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID and Content containing Container resource containing valid labels attribute } | IUT ( CSE |

| TP Id | HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/UPD/002_CSR | STRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/UPD/002_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/UPD/002_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Structured-CSE-Relative-Resource-ID |

###### RETRIEVE OPERATION

TP/oneM2M/AE/GEN/RET/002

| TP Id | TP/oneM2M/AE/GEN/RET/002 |
| --- | --- |
| Test objective | Check that the IUT sends the retrieval of a <container> resource using structured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_STRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use HIERARCHICAL_RESOURCE_ADDRESS and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS and the IUT having privileges to perform RETRIEVE operation on container resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a RETRIEVE Request on the CONTAINER_RESOURCE_ADDRESS } | NA |
|  | then { the IUT sends a valid RETRIEVE request to CSE containing To set to HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID } | IUT ( CSE |

| TP Id | HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/RET/002_CSR | STRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/RET/002_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/RET/002_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Structured-CSE-Relative-Resource-ID |

###### DELETE OPERATION

TP/oneM2M/AE/GEN/DEL/002

| TP Id | TP/oneM2M/AE/GEN/DEL/002 |
| --- | --- |
| Test objective | Check that the IUT sends the deletion of a <container> resource using structured resource identifier |
| Reference | TS-0001 9.3.1-1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, PICS_STRUCTURED_CSE_RELATIVE_RESOURCE_ID_FORMAT |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT being configured to use HIERARCHICAL_RESOURCE_ADDRESS and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS and the IUT having privileges to perform DELETE operation on container resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a DELETE Request on the CONTAINER_RESOURCE_ADDRESS } | NA |
|  | then { the IUT sends a valid DELETE request to CSE containing To set to HIERARCHICAL_RESOURCE_ADDRESS and From set to AE_ID } | IUT ( CSE |

| TP Id | HIERARCHICAL_RESOURCE_ADDRESS |
| --- | --- |
| TP/oneM2M/AE/GEN/DEL/002_CSR | STRUCTURED_CSE_RELATIVE_RESOURCE_ID |
| TP/oneM2M/AE/GEN/DEL/002_SPR | SP_RELATIVE_RESOURCE_ID* |
| TP/oneM2M/AE/GEN/DEL/002_ABS | ABSOLUTE_RESOURCE_ID* |
| * These addresses are constructed with the Structured-CSE-Relative-Resource-ID |

##### AE/GEN/00001/00005

Support SP-relative Structured resource identifier

TP/oneM2M/AE/GEN/CRE/002_SPR

TP/oneM2M/AE/GEN/UPD/002_SPR

TP/oneM2M/AE/GEN/RET/002_SPR

TP/oneM2M/AE/GEN/DEL/002_SPR

##### AE/GEN/00001/00006

Support Absolute Structured resource identifier

TP/oneM2M/AE/GEN/CRE/002_ABS

TP/oneM2M/AE/GEN/UPD/002_ABS

TP/oneM2M/AE/GEN/RET/002_ABS

TP/oneM2M/AE/GEN/DEL/002_ABS

## ----------------------- End of change 1 -----------------------