| Input Contribution |
| --- |
| Meeting ID* | TST 30 |
| Title:* | New Test Purposes of <remoteCSE> for MN-CSE |
| Source:* | Ting Martin Miao, KETI, martin.miao@keti.re.kr |
| Date:* | 2017-07-08 |
| Input related to* | <remoteCSE> resource CRUD operations with MN-CSE as an originator |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0018 v0.3.0 |
| Decision requested or recommendation:* | Add missing <remoteCSE> relevant test purposes that initated by a MN-CSE. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

Features listed as below don’t have any related test purposes for the moment:

- 7.2.3.2.27	CE/REG/00005/00001 - The Creation with <remoteCSE> resource for CSE registration with mandatory attributes[2] for Create and locally create <remoteCSE> that represents the Regstree CSE

- 7.2.3.2.28	CE/REG/00005/00002 - Create the <remoteCSE> with resourceName attribute

- 7.2.3.2.29	CE/REG/00005/00003 - Create the <remoteCSE> with expirationTime attribute

- 7.2.3.2.30	CE/REG/00005/00004 - Create the <remoteCSE> with labels attribute

- 7.2.3.2.31	CE/REG/00005/00005 - Create the <remoteCSE> with cseType attribute

- 7.2.3.2.32	CE/REG/00005/00006 - Create the <remoteCSE> with pointOfAccess attribute

- 7.2.3.2.33	CE/REG/00005/00007 - Create the <remoteCSE> with nodeLink attribute

- 7.2.3.2.34	CE/REG/00005/00008 - Update the <remoteCSE> with labels

- 7.2.3.2.35	CE/REG/00005/00009 - Update the <remoteCSE> with expirationTime

- 7.2.3.2.36	CE/REG/00005/00010 - Update the <remoteCSE> with pointOfAccess attribute

- 7.2.3.2.37	CE/REG/00005/00011 - Update the <remoteCSE> with requestReachability

- 7.2.3.2.38	CE/REG/00005/00012 - Update the <remoteCSE> with nodeLink attribute

- 7.2.3.2.39	CE/REG/00005/00013 - Delete the <remoteCSE> resource on the Registrar, also delete the <remoteCSE> resource on the Registree

- 7.2.3.2.40	CE/REG/00005/00014 - Retrieve the <remoteCSE> resource

This input contribution proposes a group of test purposes mapping to those features, and the test purposes are written for a MN-CSE which is the IUT and acts as an originator of a request.

Requirements from TS-0001 and TS-0004 which relate to the <remoteCSE> features are attached as below.

#### -----------------------------Start of Requirement TS-0001------------------------------------------------

#### 10.1.1.2	Registration related CREATE procedure

##### 10.1.1.2.0	General

This clause describes the CREATE procedure for <remoteCSE> and <AE> resource type.

##### 10.1.1.2.1	CSE Registration procedure

The procedure for CSE Registration follows the procedure described in clause 10.1.1.1, but with some deviations. Below is the detailed description on how to perform the CSE Registration and which part of the procedure deviates from the one described in clause 10.1.1.1.

The Registration procedure requires the creation of two resources (a <remoteCSE> on the Receiver CSE and a <remoteCSE> on the Originator CSE) rather than one resource. The Registration procedure is always initiated by a CSE in the field domain except in the inter-domain case described in clause 6.5.

Originator: The Originator shall be the registering CSE.

Receiver: The Receiver shall create the <remoteCSE> resource.

Figure 10.1.1.2.1-1: Procedure for CREATEing a <remoteCSE> Resource

All the parameters of the request and steps that are not indicated do not deviate from clause 10.1.1.1.

Step 001: The Originator shall send mandatory parameters and may send optional parameters in Request message for CREATE operation as specified in clause 8.1.2

Step 002: The Receiver shall:

- The registrar CSE shall allow unknown remote CSE to attempt to ‘CREATE’ when it was authenticated by credential provided by the entity. See TS-0003[2] further detail about authentication for the CSE.

- Perform sub-steps 2)-10), from step 002 from clause 10.1.1.1 are applicable.

NOTE:	Optionally, if the M2M Service Provider supports inter-domain communication, the Receiver could perform this step if the attribute CSEBase (part of the Content parameter of the request) contains the public domain of the CSE. The Receiver could construct the domain as described in clause 6.4 and 6.5. The Receiver could add an AAA or AAAA record in DNS with the public domain name of the Originator CSE and the IP address of the IN-CSE associated with the Originator.

Step 003: See clause 10.1.1.1.

Step 004: The Originator, upon receipt of the successful CREATE response message, shall create a <remoteCSE> resource locally under its <CSEBase> resource. This resource is representing the Receiver CSE. The Originator shall provide the appropriate values to all mandatory parameters as described in clause 9.6.4.

Step 005: The Originator may issue a RETRIEVE Request towards the Receiver (same To as for the CREATE request message) to obtain the optional attributes of the <remoteCSE> resource created at the Originator in step 004 (e.g. labels, accessControlPolicyIDs attributes). The RETRIEVE procedure is described in clause 10.1.2.

See clauses 8.1.2 for the information to be included in the Request message.

Step 006: The Receiver verifies that the Originator has the appropriate privileges to access the information.

Step 007: The Receiver sends a RETRIEVE response message, according to the procedure described in clause 10.1.2.

See clauses 8.1.3 and 8.1.4 for the information to be included in the Response message.

Step 008: The Originator shall update the created <remoteCSE> resource for the Receiver with the information obtained in step 007.

General Exceptions:

All exceptions from clause 10.1.1.1 are applicable; in addition the following exception may occur:

- The Originator does not have the privileges to retrieve the attributes of the Receiver CSE. The Receiver responds with an error.

#### -----------------------------End of Requirement TS-0001------------------------------------------------

#### -----------------------------Start of Requirement TS-0004------------------------------------------------

### Resource Type <remoteCSE>

#### Introduction

A <remoteCSE> resource shall represent a remote CSE that is registered to the Registrar CSE. <remoteCSE> resources shall be located directly under the <CSEBase> of the registrar <CSEBase>.

In addition each registered CSE shall have a <remoteCSE> resource representing its registrar CSEBase. This is created directly under in the registered CSE's <CSEBase>.

The detailed description can be found in clause 9.6.4 in Architecture TS.

Table 7.4.5.1-1: Data type definition of <remoteCSE> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| remoteCSE | CDT-remoteCSE-v1_12_0.xsd |  |

Table 7.4.5.1-2: Universal/Common Attributes of <remoteCSE> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |

Table 7.4.5.1-3: Resource Specific Attributes of <remoteCSE> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| cseType | O | NP | m2m:cseTypeID | No default |
| pointOfAccess | O | O | m2m:poaList | No default |
| CSEBase | M | NP | xs:anyURI | No default |
| CSE-ID | M | NP | m2m:ID | No default |
| M2M-Ext-ID | O | O | m2m:externalID | No default |
| Trigger-Recipient-ID | O | O | m2m:triggerRecipientID | No default |
| requestReachability | M | O | xs:boolean | No default |
| nodeLink | O | O | xs:anyURI | No default |

Table 7.4.5.1-4: Child resources of <remoteCSE> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <container> | [variable] | 0..n | Clause 7.4.7 |
| <containerAnnc> | [variable] | 0..n | Clause 7.4.7 |
| <group> | [variable] | 0..n | Clause 7.4.14 |
| <groupAnnc> | [variable] | 0..n | Clause 7.4.14 |
| <accessControlPolicy> | [variable] | 0..n | Clause 7.4.3 |
| <accessControlPolicyAnnc> | [variable] | 0..n | Clause 7.4.3 |
| <subscription> | [variable] | 0..n | Clause 7.4.9 |
| <pollingChannel> | [variable] | 0..1 | Clause 7.4.22 |
| <schedule> | [variable] | 0..1 | Clause 7.4.10 |
| <nodeAnnc> | [variable] | 0..n | Clause 7.4.19 |
| <remoteCSEAnnc> | [variable] | 0..n | Clause 7.4.5 |
| <AEAnnc> | [variable] | 0..n | Clause 7.4.6 |
| <locationPolicyAnnc> | [variable] | 0..n | Clause 7.4.11 |

#### <remoteCSE> resource specific procedure on CRUD operations

##### Introduction

The entire CSE registration procedure including <CSE> resource creation procedure below is defined in clause 10.1.1.2.1 of oneM2M TS-0001 [6] ("CSE registration procedure").

##### Create

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exception:

An AE shall not originate a Create <remoteCSE> resource request.

The Originator, upon receipt of successful CREATE response message, shall create a <remoteCSE> resource locally.

The Originator may issue RETRIEVE request to its registrar <CSEBase>, to fetch the additional information about the registrar CSE and add this information to its local <remoteCSE> resource. The Originator may choose which optional attributes to include in its <remoteCSE> resource.

Receiver:

Same as the generic procedures in clause 7.2.2.2 except replacement of Recv-6.3 step with following:

- The Hosting CSE shall check if the credential provided by the Originator is valid.

- If the check is failed, then the Hosting CSE shall return response primitive with a Response Status Code indicating "SECURITY_ASSOCIATION_REQUIRED" error.

##### Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Update

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exception:

An AE shall not originate a Update <remoteCSE> resource request.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Delete

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exceptions:

- An AE shall not originate a Delete <remoteCSE> resource request.

- The Originator, upon receipt of successful DELETE response message, shall delete the corresponding <remoteCSE> resource locally.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

#### -----------------------------End of Requirement TS-0004------------------------------------------------

#### -------------------------------Start of Change 1------------------------------------------------------------------

# 7	Test Purposes (TP)

## 7.2 	Test Purposes for oneM2M Service Primitives

### Group CSE (CE)

#### Registration (REG)

##### CE/REG/00005/00001

The Creation with <remoteCSE> resource for CSE registration with mandatory attributes [2] for Create and locally create <remoteCSE> that represents the Regstree CSE.

TP/oneM2M/CSE/REG/CRE/XXZ

| TP Id | TP/oneM2M/CSE/REG/CRE/XXZ |
| --- | --- |
| Test objective | Check that IUT is triggered to send a CSE registration request with attributes multiplicity equals to 1 |
| Reference | TS-0001 10.1.1.2.1, TS-0004 7.4.5.2.2 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having privileges to perform CREATE operation on the resource CSEBASE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a CREATE Request on CSEBASE_RESOURCE_ADDRESS } | NA |
|  | then { the IUT sends a valid CREATE Request containing To set to CSEBASE_RESOURCE_ADDRESS and From set to CSE_ID and Resource Type set to 16 (remoteCSE) and Content containing remoteCSE resource representation } | IUT ( CSE |

TP/oneM2M/CSE/REG/CRE/XXK

| TP Id | TP/oneM2M/CSE/REG/CRE/XXK |
| --- | --- |
| Test objective | Check that IUT is accepted with a CSE registration request with attributes multiplicity equals to 1 |
| Reference | TS-0001 10.1.1.2.1, TS-0004 7.4.5.2.2 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having privileges to perform CREATE operation on the resource CSEBASE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid CREATE Request containing To set to CSEBASE_RESOURCE_ADDRESS and From set to CSE_ID and Resource Type set to 16 (remoteCSE) and Content containing remoteCSE resource representation } | IUT ( CSE |
|  | then { the IUT receives a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing remoteCSE resource representation and the IUT creates a <remoteCSE> locally to represent the CSE CSEBASE_RESOURCE_ADDRESS } | IUT ( CSE |

<REQ-0001-10142>

Register MN-CSE with optional attributes to CSE (IN-CSE or MN-CSE)

| TP Id | TP/oneM2M/CSE/REG/CRE/XXX |
| --- | --- |
| Test objective | Check that IUT is triggered to send a CSE registration request with OPTIONAL_ATTRIBUTE attribute |
| Reference | TS-0001 10.1.1.2.1, TS-0004 7.4.5.2.2 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having privileges to perform CREATE operation on the resource CSEBASE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a CREATE Request on CSEBASE_RESOURCE_ADDRESS containing Content containing remoteCSE resource representation containing valid attribute OPTIONAL_ATTRIBUTE } | NA |
|  | then { the IUT sends a valid CREATE Request containing To set to CSEBASE_RESOURCE_ADDRESS and From set to CSE_ID and Resource Type set to 16 (remoteCSE) and Content containing remoteCSE resource representation containing valid attribute OPTIONAL_ATTRIBUTE } | IUT ( CSE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/REG/CRE/XXX_RN | TS-0001 9.6.4-2 | resourceName |
| TP/oneM2M/CSE/REG/CRE/XXX_ET | TS-0001 9.6.4-2 | expirationTime |
| TP/oneM2M/CSE/REG/CRE/XXX_LBL | TS-0001 9.6.4-2 | labels |
| TP/oneM2M/CSE/REG/CRE/XXX_POA | TS-0001 9.6.4-2 | pointOfAccess |
| TP/oneM2M/CSE/REG/CRE/XXX_NL | TS-0001 9.6.4-2 | nodeLink |

| TP Id | TP/oneM2M/CSE/REG/CRE/XXD |
| --- | --- |
| Test objective | Check that IUT is triggered to send a CSE registration request with cseType attribute set to ‘MN_CSE’ |
| Reference | TS-0001 10.1.1.2.1, TS-0004 7.4.5.2.2 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having privileges to perform CREATE operation on the resource CSEBASE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a CREATE Request on CSEBASE_RESOURCE_ADDRESS containing Content containing remoteCSE resource representation containing cseType attribute set to 2 (MN_CSE) } | NA |
|  | then { the IUT sends a valid CREATE Request containing To set to CSEBASE_RESOURCE_ADDRESS and From set to CSE_ID and Resource Type set to 16 (remoteCSE) and Content containing remoteCSE resource representation containing cseType attribute set to 2 (MN_CSE) } | IUT ( CSE |

##### CE/REG/00005/00002

Create the <remoteCSE> with resourceName attribute

TP/oneM2M/CSE/REG/CRE/XXX_RN

TP/oneM2M/CSE/REG/CRE/XXR_RN

##### CE/REG/00005/00003

Create the <remoteCSE> with expirationTime attribute

TP/oneM2M/CSE/REG/CRE/XXX_ET

TP/oneM2M/CSE/REG/CRE/XXR_ET

##### CE/REG/00005/00004

Create the <remoteCSE> with labels attribute

TP/oneM2M/CSE/REG/CRE/XXX_LBL

TP/oneM2M/CSE/REG/CRE/XXR_LBL

##### CE/REG/00005/00005

Create the <remoteCSE> with cseType attribute

TP/oneM2M/CSE/REG/CRE/XXM

TP/oneM2M/CSE/REG/CRE/XXD

| TP Id | TP/oneM2M/CSE/REG/CRE/XXM |
| --- | --- |
| Test objective | Check that IUT is accepted with a CSE registration request with cseType attribute set to ‘MN_CSE’ |
| Reference | TS-0001 10.1.1.2.1, TS-0004 7.4.5.2.2 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having privileges to perform CREATE operation on the resource CSEBASE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid CREATE Request containing To set to CSEBASE_RESOURCE_ADDRESS and From set to CSE_ID and Resource Type set to 16 (remoteCSE) and Content containing remoteCSE resource representation containing cseType attribute set to 2 (MN_CSE) } | IUT ( CSE |
|  | then { the IUT receives a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing remoteCSE resource representation containing cseType attribute set to 2 (MN_CSE) } | IUT ( CSE |

| TP Id | TP/oneM2M/CSE/REG/CRE/XXR |
| --- | --- |
| Test objective | Check that IUT is accepted with a CSE registration request with OPTIONAL_ATTRIBUTE attribute |
| Reference | TS-0001 10.1.1.2.1, TS-0004 7.4.5.2.2 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having privileges to perform CREATE operation on the resource CSEBASE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid CREATE Request containing To set to CSEBASE_RESOURCE_ADDRESS and From set to CSE_ID and Resource Type set to 16 (remoteCSE) and Content containing remoteCSE resource representation containing valid attribute OPTIONAL_ATTRIBUTE } | IUT ( CSE |
|  | then { the IUT receives a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing remoteCSE resource representation containing valid attribute OPTIONAL_ATTRIBUTE and the IUT creates a <remoteCSE> locally to represent the CSE CSEBASE_RESOURCE_ADDRESS } | IUT ( CSE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/REG/CRE/XXR_RN | TS-0001 9.6.4-2 | resourceName |
| TP/oneM2M/CSE/REG/CRE/XXR_ET | TS-0001 9.6.4-2 | expirationTime |
| TP/oneM2M/CSE/REG/CRE/XXR_LBL | TS-0001 9.6.4-2 | labels |
| TP/oneM2M/CSE/REG/CRE/XXR_POA | TS-0001 9.6.4-2 | pointOfAccess |
| TP/oneM2M/CSE/REG/CRE/XXR_NL | TS-0001 9.6.4-2 | nodeLink |

##### CE/REG/00005/00006

Create the <remoteCSE> with pointOfAccess attribute

TP/oneM2M/CSE/REG/CRE/XXX_POA

TP/oneM2M/CSE/REG/CRE/XXR_POA

##### CE/REG/00005/00007

Create the <remoteCSE> with nodeLink attribute

TP/oneM2M/CSE/REG/CRE/XXX_NL

TP/oneM2M/CSE/REG/CRE/XXR_NL

##### CE/REG/00005/00008

Update the <remoteCSE> with labels attribute

TP/oneM2M/CSE/REG/UPD/XXX_LBL

TP/oneM2M/CSE/REG/UPD/XXY_LBL

| TP Id | TP/oneM2M/CSE/REG/UPD/XXX |
| --- | --- |
| Test objective | Check that IUT is triggered to send a <remoteCSE> update request with OPTIONAL_ATTRIBUTE attribute |
| Reference | TS-0001 10.2.2.3, TS-0004 7.4.5.2.4 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a resource TARGET_REMOTE_CSE_ADDRESS containing a RW OPTIONAL_ATTRIBUTE attribute set to VALUE_1 and the IUT having privileges to perform UPDATE operation on the resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send an UPDATE Request on resource TARGET_REMOTE_CSE_ADDRESS containing Content containing remoteCSE resource representation containing valid attribute OPTIONAL_ATTRIBUTE } | NA |
|  | then { the IUT sends a valid UPDATE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and Content containing remoteCSE resource representation containing valid attribute OPTIONAL_ATTRIBUTE set to VALUE_2 } | IUT ( CSE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/REG/UPD/XXX_ET | TS-0001 9.6.4-2 | expirationTime |
| TP/oneM2M/CSE/REG/UPD/XXX_LBL | TS-0001 9.6.4-2 | labels |
| TP/oneM2M/CSE/REG/UPD/XXX_POA | TS-0001 9.6.4-2 | pointOfAccess |
| TP/oneM2M/CSE/REG/UPD/XXX_NL | TS-0001 9.6.4-2 | nodeLink |
| TP/oneM2M/CSE/REG/UPD/XXX_RR | TS-0001 9.6.4-2 | RequestReachability |

##### CE/REG/00005/00009

Update the <remoteCSE> with expirationTime attribute

TP/oneM2M/CSE/REG/UPD/XXX_ET

TP/oneM2M/CSE/REG/UPD/XXY_ET

##### CE/REG/00005/00010

Update the <remoteCSE> with pointOfAccess attribute

TP/oneM2M/CSE/REG/UPD/XXX_POA

TP/oneM2M/CSE/REG/UPD/XXY_POA

##### CE/REG/00005/00011

Update the <remoteCSE> with requestReachability attribute

TP/oneM2M/CSE/REG/UPD/XXX_RR

TP/oneM2M/CSE/REG/UPD/XXY_RR

##### CE/REG/00005/00012

Update the <remoteCSE> with nodeLink attribute

TP/oneM2M/CSE/REG/UPD/XXX_NL

TP/oneM2M/CSE/REG/UPD/XXY_NL

| TP Id | TP/oneM2M/CSE/REG/UPD/XXY |
| --- | --- |
| Test objective | Check that IUT is accepted with a <remoteCSE> update request with OPTIONAL_ATTRIBUTE attribute |
| Reference | TS-0001 10.2.2.3, TS-0004 7.4.5.2.4 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a resource TARGET_REMOTE_CSE_ADDRESS containing a RW OPTIONAL_ATTRIBUTE attribute set to VALUE_1 and the IUT having privileges to perform CREATE operation on the resource CSEBASE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid UPDATE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and Content containing remoteCSE resource representation containing valid OPTIONAL_ATTRIBUTE attribute set to VALUE_2 } | IUT ( CSE |
|  | then { the IUT receives a valid Response containing Response Status Code set to 2004 (UPDATED) and Content containing remoteCSE resource representation containing valid OPTIONAL_ATTRIBUTE attribute set to VALUE_2 } | IUT ( CSE |

| TP Id | Reference | OPTIONAL_ATTRIBUTE |
| --- | --- | --- |
| TP/oneM2M/CSE/REG/UPD/XXY_ET | TS-0001 9.6.4-2 | expirationTime |
| TP/oneM2M/CSE/REG/UPD/XXY_LBL | TS-0001 9.6.4-2 | labels |
| TP/oneM2M/CSE/REG/UPD/XXY_POA | TS-0001 9.6.4-2 | pointOfAccess |
| TP/oneM2M/CSE/REG/UPD/XXY_NL | TS-0001 9.6.4-2 | nodeLink |
| TP/oneM2M/CSE/REG/UPD/XXY_RR | TS-0001 9.6.4-2 | RequestReachability |

##### CE/REG/00005/00013

Delete the <remoteCSE> resource on the Registrar, also delete the <remoteCSE> resource on

the Registree.

TP/oneM2M/CSE/REG/DEL/XXX

| TP Id | TP/oneM2M/CSE/REG/DEL/XXX |
| --- | --- |
| Test objective | Check that IUT is triggered to send a <remoteCSE> delete request on TARGET_REMOTE_CSE_ADDRESS |
| Reference | TS-0001 10.2.2.4, TS-0004 7.4.5.2.5 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a resource TARGET_REMOTE_CSE_ADDRESS and the IUT having privileges to perform DELETE operation on the resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a DELETE Request on resource TARGET_REMOTE_CSE_ADDRESSS } | NA |
|  | then { the IUT sends a valid DELETE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and no Content } | IUT ( CSE |

TP/oneM2M/CSE/REG/DEL/XXY

| TP Id | TP/oneM2M/CSE/REG/DEL/XXY |
| --- | --- |
| Test objective | Check that IUT is accepted with a <remoteCSE> delete request on TARGET_REMOTE_CSE_ADDRESS, and then deletes the <remoteCSE> locally |
| Reference | TS-0001 10.2.2.4, TS-0004 7.4.5.2.5 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a resource TARGET_REMOTE_CSE_ADDRESS and the IUT having privileges to perform DELETE operation on the resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid DELETE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and no Content } | IUT ( CSE |
|  | then { the IUT receives a valid Response containing Response Status Code set to 2002 (DELETED) and the IUT deletes the local <remoteCSE> that represented the hosting CSE of resource TARGET_REMOTE_CSE_ADDRESS } | IUT ( CSE |

##### CE/REG/00005/00014

Retrieve the <remoteCSE> resource.

TP/oneM2M/CSE/REG/RET/XXX

| TP Id | TP/oneM2M/CSE/REG/RET/XXX |
| --- | --- |
| Test objective | Check that IUT is triggered to send a <remoteCSE> retrieve request on TARGET_REMOTE_CSE_ADDRESS |
| Reference | TS-0001 10.2.2.2, TS-0004 7.4.5.2.3 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a resource TARGET_REMOTE_CSE_ADDRESS and the IUT having privileges to perform DELETE operation on the resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a DELETE Request on resource TARGET_REMOTE_CSE_ADDRESS } | NA |
|  | then { the IUT sends a valid DELETE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and no Content } | IUT ( CSE |

TP/oneM2M/CSE/REG/RET/XXY

| TP Id | TP/oneM2M/CSE/REG/RET/XXY |
| --- | --- |
| Test objective | Check that IUT is accepted with a <remoteCSE> retrieve request |
| Reference | TS-0001 10.2.2.2, TS-0004 7.4.5.2.3 |
| Config Id | CF04 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having created a resource TARGET_REMOTE_CSE_ADDRESS and the IUT having privileges to perform DELETE operation on the resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid DELETE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and no Content } | IUT ( CSE |
|  | then { the IUT receives a valid Response containing Response Status Code set to 2000 (OK) and Content containing remoteCSE resource representation } | IUT ( CSE |

#### --------------------------End of Change 1-----------------------------------------------------------------------

# Comments

See TS-0001_remoteCSE_002

REQ-0001-10142

REQ-0001-10143

REQ-0001-10144

Spec: there is no 8.1.4

REQ-0001-10145

TS-0004_remoteCSE_upd_001

TS-0004_remoteCSE_cr_001

TS-0004_remoteCSE_upd_002

TS-0004_remoteCSE_cr_002

TS-0004_remoteCSE_upd_003

TS-0004_remoteCSE_cr_003

TS-0004_remoteCSE_cr_004

TS-0004_remoteCSE_upd_004

TS-0004_remoteCSE_001

TS-0004_remoteCSE_002

TS-0004_remoteCSE_003

TS-0004_remoteCSE_004

The Originator shall send mandatory parameters and may send optional parameters in Request message for CREATE operation as specified in clause 8.1.2

This TP is separated from permutation of TP/oneM2M/CSE/REG/CRE/XXR

to test only the cseType set to MN-CSE

- An AE shall not originate a Delete <remoteCSE> resource request.

The Originator, upon receipt of successful DELETE response message, shall delete the corresponding <remoteCSE> resource locally