| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#30 |
| Source:* | Bob Flynn, Convida , Flynn.Bob@convidawireless.com |
| Date:* | 2017-07-09 |
| Reason for Change/s:* | To provide TPs for CSEBase requirements |
| CR against: Release* | 1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The last column can be used to update the requirements tracking spreadsheet.

This list is continued from TST-2017-0150R04-TDs_for_CSEBase

The following additional requirements are mapped to existing test purposes

I changed the old requirement name to new requirement names in change 0.

| TS-0001_CSEBase_006 | REQ-0001-09040 | 9.6.3-1 | <remoteCSE> at CSEBase | TP/oneM2M/CSE/REG/CRE/BV/0xx In TST-2017-0141 |
| --- | --- | --- | --- | --- |
| TS-0001_CSEBase_007 | REQ-0001-09041 | 9.6.3-1 | <node> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_18 |
| TS-0001_CSEBase_008 | REQ-0001-09042 | 9.6.3-1 | <AE> at CSEBase | TP/oneM2M/CSE/REG/CRE/BV/009 In TST-2017-0141 |
| TS-0001_CSEBase_009 | REQ-0001-09043 | 9.6.3-1 | <container> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_01 |
| TS-0001_CSEBase_010 | REQ-0001-09044 | 9.6.3-1 | <group> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_04 |
| TS-0001_CSEBase_011 | REQ-0001-09045 | 9.6.3-1 | <accessControlPolicy> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_06 |
| TS-0001_CSEBase_012 | REQ-0001-09046 | 9.6.3-1 | <subscription> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_12 |
| TS-0001_CSEBase_013 | REQ-0001-09047 | 9.6.3-1 | <mgmtCmd> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_19 |
| TS-0001_CSEBase_014 | REQ-0001-09048 | 9.6.3-1 | <locationPolicy> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_20 |
| TS-0001_CSEBase_015 | REQ-0001-09049 | 9.6.3-1 | <statsConfig> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_21 |
| TS-0001_CSEBase_016 | REQ-0001-09050 | 9.6.3-1 | <statsCollect> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_22 |
| TS-0001_CSEBase_017 | REQ-0001-09051 | 9.6.3-1 | <request> at CSEBase | TP/oneM2M/CSE/DMR/RET/013_REQ |
| TS-0001_CSEBase_018 | REQ-0001-09052 | 9.6.3-1 | <delivery> at CSEBase | TP/oneM2M/CSE/DMR/RET/013_DLV TP/oneM2M/CSE/DMR/RET/015_DLV |
| TS-0001_CSEBase_019 | REQ-0001-09053 | 9.6.3-1 | <schedule> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_08 |
| TS-0001_CSEBase_020 | REQ-0001-09054 | 9.6.3-1 | <m2mServiceSubscriptionProfile> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_23 |
| TS-0001_CSEBase_021 | REQ-0001-09055 | 9.6.3-1 | <serviceSubscribedAppRule> at CSEBase | TP/oneM2M/CSE/DMR/CRE/BV/001_24 |
| TS-0001_CSEBase_022 | REQ-0001-09056 | 9.6.3-3 | cseType M for IN, optional otherwise. RO | TP/oneM2M/CSE/REG/RET/BV/005 |
| TS-0001_CSEBase_023 | REQ-0001-09057 | 9.6.3-3 | CSE-ID RO (M) | TP/oneM2M/CSE/REG/RET/BV/001 |
| TS-0001_CSEBase_024 | REQ-0001-09058 | 9.6.3-3 | supportedResourceTypes. RO (M) | TP/oneM2M/CSE/REG/RET/BV/xxx1 |
| TS-0001_CSEBase_025 | REQ-0001-09059 | 9.6.3-3 | pointOfAccess. RO (M) | TP/oneM2M/CSE/REG/RET/BV/xxx1 |
| TS-0001_CSEBase_026 | REQ-0001-09060 | 9.6.3-3 | nodeLink. RO (O) | TP/oneM2M/CSE/REG/RET/002_NL |
| TS-0001_CSEBase_027 | REQ-0001-09061 | 9.6.3-3 | notificationCongestionPolicy. RO (O) |  |
| TS-0001_CSEBase_001 | REQ-0001-10016 | 10.2.3.1 | Do not allow creation of CSEBase | TP/oneM2M/CSE/REG/CRE/024 |
| TS-0001_CSEBase_002 | REQ-0001-10017 | 10.2.3.2 | Retrieve CseBase | TP/oneM2M/CSE/REG/RET/001 |
| TS-0001_CSEBase_004 | REQ-0001-10018 | 10.2.3.3 | Do not allow update CSEBase | TP/oneM2M/CSE/REG/UPD/001 |
| TS-0001_CSEBase_005 | REQ-0001-10019 | 10.2.3.4 | Do not allow delete CSEBase | TP/oneM2M/CSE/REG/DEL/001 |

### -----------------------Start of change 0-------------------------------------------

### <CSEBase> Resource Procedures

#### 10.2.3.1	Create <CSEBase>

The Create procedure shall be not apply to <CSEBase>. <CSEBase> can be created via management operation not defined in this version of the specification.

#### 10.2.3.2	Retrieve <CSEBase>

This procedure shall be used for retrieving the representation of the <CSEBase> resource with its attributes.

Table 10.2.3.2-1: <CSEBase> RETRIEVE

| <CSEBase> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clauses 10.1.2 and 10.1.1.2.1 |
| Processing at Receiver | According to clauses 10.1.2 and 10.1.1.2.1 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: attributes of the <CSEBase> resource as requested by the Originator |
| Processing at Originator after receiving Response | According to clauses 10.1.2 and 10.1.1.2.1 When this procedure is used during CSE Registration, a <remoteCSE> resource is created using the retrieved resource |
| Exceptions | According to clauses 10.1.2 and 10.1.1.2.1 |

#### 10.2.3.3	Update <CSEBase>

The Update procedure shall not apply to <CSEBase>. <CSEBase> can be updated via management operation not defined in this version of the specification.

#### 10.2.3.4	Delete <CSEBase>

The Delete procedure shall not apply to <CSEBase>. <CSEBase> can be deleted via management operation not defined in this version of the specification.

### -----------------------End of change 0-------------------------------------------

### -----------------------Start of change 1-------------------------------------------

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### -----------------------End of change 2---------------------------------------------

# Comments

Should be mandatory if sub/not is supported.  CR to this effect.

This applies to our ‘unofficial’ annotated spreadsheet.

REQ-0001-10016

REQ-0001-10017

REQ-0001-10018

REQ-0001-10019