| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST#30 |
| Source:* | Bob Flynn, Convida , Flynn.Bob@convidawireless.com |
| Date:* | 2017-07-09 |
| Reason for Change/s:* | To provide TPs for RemoteCSE requirements |
| CR against: Release* | 1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

| TS-0001_remoteCSE_006 | REQ-0001-09062 | 9.6.4 | General description. Perhaps not a good requirement. Describes end state of CSE registration process. |  |
| --- | --- | --- | --- | --- |
| TS-0001_remoteCSE_007 | REQ-0001-09063 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_008 | REQ-0001-09064 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_009 | REQ-0001-09065 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_010 | REQ-0001-09066 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_011 | REQ-0001-09067 | 9.6.4-1 | <subscription> at remoteCSE | TP/oneM2M/CSE/DMR/CRE/BV/001_xx |
| TS-0001_remoteCSE_012 | REQ-0001-09068 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_013 | REQ-0001-09069 | 9.6.4-1 | <schedule> at remoteCSE | TP/oneM2M/CSE/DMR/CRE/BV/001_xx |
| TS-0001_remoteCSE_014 | REQ-0001-09070 | 9.6.4-1 | <nodeAnnc> at remoteCSE |  |
| TS-0001_remoteCSE_015 | REQ-0001-09071 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_016 | REQ-0001-09072 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_017 | REQ-0001-09073 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_018 | REQ-0001-09074 | 9.6.4-1 | <containerAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_019 | REQ-0001-09075 | 9.6.4-1 | <group> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_020 | REQ-0001-09076 | 9.6.4-1 | <groupAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_021 | REQ-0001-09077 | 9.6.4-1 | <accessControlPolicy> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_022 | REQ-0001-09078 | 9.6.4-1 | <accessControlPolicyAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_023 | REQ-0001-09079 | 9.6.4-1 | <subscription> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_025 | REQ-0001-09080 | 9.6.4-1 | <scheduleAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_026 | REQ-0001-09081 | 9.6.4-1 | <nodeAnnc> at remoteCSEAnnc |  |
| TS-0001_remoteCSE_027 | REQ-0001-09082 | 9.6.4-1 |  |  |
| TS-0001_remoteCSE_028 | REQ-0001-09083 | 9.6.4-3 | cseType. IN (M) MN/ASN (O) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_029 | REQ-0001-09084 | 9.6.4-3 | pointOfAccess. (O) M if rr=true | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_030 | REQ-0001-09085 | 9.6.4-3 | CSEBase (M)(WO) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_031 | REQ-0001-09086 | 9.6.4-3 | CSE-ID (M)(WO) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_032 | REQ-0001-09087 | 9.6.4-3 | M2M-Ext-ID (O) |  |
| TS-0001_remoteCSE_033 | REQ-0001-09088 | 9.6.4-3 | Trigger-Recipient-ID (O) |  |
| TS-0001_remoteCSE_034 | REQ-0001-09089 | 9.6.4-3 | RequestReachability (M) | TP/oneM2M/CSE/REG/CRE/BV/011 |
| TS-0001_remoteCSE_035 | REQ-0001-09090 | 9.6.4-3 | nodeLink (O) |  |
| TS-0001_remoteCSE_002 | REQ-0001-10012 | 10.2.2.1-1 | Create remoteCse |  |
| TS-0001_remoteCSE_003 | REQ-0001-10013 | 10.2.2.2-1 | Retrieve remoteCSE |  |
| TS-0001_remoteCSE_004 | REQ-0001-10014 | 10.2.2.3-1 | Update remoteCSE |  |
| TS-0001_remoteCSE_005 | REQ-0001-10015 | 10.2.2.4-1 | Delete remoteCSE |  |

- Change old req id’s to new requirement ids for section 10.2.2

- Identify TP’s for this list. There is a lot of overlap with existing tests, so I cross reference them to existing testcases. This can be entered in the tracking spreadsheet. New mappings shown in bold

### -----------------------Start of change 0-------------------------------------------

### 10.2.2	<remoteCSE> Resource Procedures

#### 10.2.2.1	Create <remoteCSE>

This procedure shall be used for creating a <remoteCSE> resource. It is part of the registration procedure for remote CSEs on the Registrar CSE (which is also the Hosting CSE), as described in clause 10.1.1.2.1.

Table 10.2.2.1-1: <remoteCSE> CREATE

| <remoteCSE> CREATE |
| --- |
| Associated Reference Point | Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: From: Originator CSE-ID Content: The resource content shall provide the information as defined in clause 9.6.4 |
| Processing at Originator before sending Request | According to clause 10.1.1.2.1 |
| Processing at Receiver | According to clause 10.1.1.2.1 If the IN-CSE is the receiver and if the M2M SP policies do allow access to the CSEs across multiple domains, then the IN shall create the appropriate entry in the M2M SP's DNS for successfully registered CSE |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: Address of the created <remoteCSE> resource, according to clause 10.1.1.2.1 |
| Processing at Originator after receiving Response | According to clause 10.1.1.2.1. the Originator upon receipt of successful CREATE response message, shall create <remoteCSE> resource locally and thereafter, it may issue a Retrieve request to its Registrar CSE’s <CSEBase> resource to update the optional attributes of locally created <remoteCSE> resource. |
| Exceptions | According to clause 10.1.1.2.1 |

#### 10.2.2.2	Retrieve <remoteCSE>

This procedure shall be used for retrieving the representation of the <remoteCSE> resource with its attributes.

Table 10.2.2.2-1: <remoteCSE> RETRIEVE

| <remoteCSE> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.2 |
| Processing at Receiver | According to clause 10.1.2 |
| Information in Response message | All parameters defined in table 8.1.3-1 apply with the specific details for: Content: attributes of the <remoteCSE> resource as the Originator requested |
| Processing at Originator after receiving Response | According to clause 10.1.2 |
| Exceptions | According to clause 10.1.2 |

#### 10.2.2.3	Update <remoteCSE>

This procedure shall be used for updating the attributes and the actual data of an <remoteCSE> resource.

Table 10.2.2.3-1: <remoteCSE> UPDATE

| <remoteCSE> UPDATE |
| --- |
| Associated Reference Point | Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply with the specific details for: Content: attributes of the <remoteCSE> resource as defined in clause 9.6.4 which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3 |
| Processing at Receiver | According to clause 10.1.3 |
| Information in Response message | According to clause 10.1.3 |
| Processing at Originator after receiving Response | According to clause 10.1.3 |
| Exceptions | According to clause 10.1.3 |

#### 10.2.2.4	Delete <remoteCSE>

This procedure shall be used for deleting the <remoteCSE> resource with all related information.

Table 10.2.2.4-1: <remoteCSE> DELETE

| <remoteCSE> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-3 apply |
| Processing at Originator before sending Request | According to clause 10.1.4 |
| Processing at Receiver | According to clause 10.1.4 If the IN-CSE is the receiver and it has created an entry in the DNS to allow access to the CSE across multiple M2M domains, then it shall delete the entry from the DNS |
| Information in Response message | According to clause 10.1.4 |
| Processing at Originator after receiving Response | According to clause 10.1.4 |
| Exceptions | According to clause 10.1.4 |

### -----------------------End of change 0-------------------------------------------

# Comments

This applies to our ‘unofficial’ annotated spreadsheet.

REQ-0001-10012

REQ-0001-10013

REQ-0001-10014

REQ-0001-10015