| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST30 |
| Source:* | Martin Bauer, NEC, martin.bauer@neclab.eu |
| Date:* | 2017-07-10 |
| Reason for Change/s:* | Update based on review comments from Convida. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0054 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0045 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | - |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

TR-0045 was reviewed by Convida and their, mostly editorial, comments, were incorporated into the document.

Changes to 10.5 have been included in TST-2017-0206-Fixing_HTTP_Requests_in_TR-0045.

### -----------------------Start of change 1-------------------------------------------

# 1	Scope

The present document provides a simple use case for guiding application developers to develop applications using functionalities provided by a oneM2M service platform with the scope of as follows:

- Objective of the use case,

- The architecture of the use case mapped into a oneM2M service platform including semantic resources,

- The semantic modelling of the devices and the information according to a suitable ontology

- The execution procedures for implementation of the use case with a focus on the semantic aspects, and

- Implementation details of the use case using RDF (Resource Description Framework) for representing semantic descriptions and SPARQL queries on the RDF descriptions to identify fitting resources in the semantic resource discovery.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]	oneM2M TS-0011: "Common Terminology".

[i.3]	oneM2M TS-0012: "Base Ontology"

[i.4]	oneM2M TS-0030: “Generic Interworking”

[i.5]	oneM2M TR-0025: “Application Developer Guide”

[i.6]	oneM2M TS-0001:  “Functional Architecture”

[i.7]	oneM2M TS-0004: “Service Layer Core Protocol”

[i.8] 	oneM2M TS-0009: “HTTP Protocol Binding”

# 3	Definitions, symbols and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in oneM2M TS-0011 [i.2] apply.

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5 	Motivation

The assumption of many existing oneM2M applications is that they interact with other oneM2M applications through known resource structures. They either create the resources themselves or are configured to use specific resources. Information is typically stored in containers, often as base64-encoded content instances, with the implicit assumption that applications have a-priori agreed on the syntax and semantics of this information.

Such an approach works well for small-scale and relatively static settings. When changes happen, the configuration will be updated manually. However, in more dynamic settings where the relevant resources frequently change, this becomes impractical. To satisfy those settings, relevant resources need to be discovered. Since Release 1, discovery of resources based on specific attributes and the use of labels has been made possible. The agreement of a fixed set of labels – which can only be combined using a logical OR operation in a discovery request – could be a viable solution.

For more heterogeneous, dynamic and larger scale scenarios, a more expressive approach for describing and discovering resources is needed. There are heterogeneous underlying technologies that can provide their information according to a different syntax, e.g., Zigbee, Z-Wave, Wi-Fi, etc., according to different units, e.g., Celsius, Fahrenheit and Kelvin. Those technologies may measure different aspects, e.g., indoor temperature, outdoor temperature,fridge temperature, etc., and the quality of the measurement may differ.

Another motivation of semantic annotations is to support the re-use of the same information by multiple applications. For example, in a smart city, applications may need to dynamically discover relevant resources according to multiple criteria at the same time – as sketched in the previous paragraph.

With semantic annotations, all the different aspects of IoT data can be described using RDF, which is a standardized semantic format. The vocabulary used for this description can be defined according to an ontology. With semantic discovery, applications can describe precisely what information they need or can deal with. This is powered by specifying a semantic filter using the SPARQL query language. The SPARQL filter is matched against the respective semantic annotation of each resource within the discovery scope, and the resource is included in the result of the discovery request only if the filter fits.

# 6	Use Case

This clause briefly describes a use case from the perspective of services provided by the oneM2M platform. The physical device components will be introduced in this section.

In the use case, different sensor measure temperature information, but the temperature realtes to different aspects, i.e. indoor, outdoor and fridge temperature and the temperature is measured in different scales. Simply discovering temperature does not solve the problem as the temperatures relate to different aspects.Through semantic annotation and semantic discovery of resources  the resources that are relevant in a particular use case can be found.

An overview of the use case is shown in figure 6.1. The main components include:

- The temperature sensors are connected to a server.

- The server provides a set of services to enable the applications on smartphone #1 to discover and retrieve the relevant temperature information.

- The server provides a set of services to enable the applications on smartphone #2 to manage and semantically annotate the services providing temperature information.

Figure 6.1: Overview of semantic annotation and discovery use case.

# 7	Architecture Configuration

This clause describes the architecture of this use case with components represented by the oneM2M entity roles.

In the oneM2M, two basic types of entities are defined. One is an Application Entity (AE) and the other is a Common Services Entity (CSE). As shown in figure 7.1, the previous use case is modelled using oneM2M entities:

- Each sensor and the smartphone hosts an AE. The AE resides in the Application Dedicated Node is called ADN-AE.

- The server hosts an Infrastructure Node CSE (IN-CSE).

Figure 7.1: oneM2M functional architecture of semantic annotation and discovery use case.

The oneM2M defined Mca reference point is used to interface an AE and CSE. Therefore, in this use case:

- The reference point used between temperature sensor AEs and the IN-CSE or Smartphone AEs and IN-CSE is Mca.

In summary, applications used in the current use case are classified as follows:

- ADN-AE-1: an application embedded in Sensor#1 with capabilities to monitor Sensor#1 and interact with the IN-CSE through the Mca reference point;

- ADN-AE-2: an application embedded in Sensor#2 with capabilities to monitor Sensor#2 and interact with the IN-CSE through Mca reference point;

- ADN-AE-3: an application embedded in Sensor#3 with capabilities to monitor Sensor#3 and interact with the IN-CSE through Mca reference point;

- ADN-AE-4: an application embedded in Sensor#4 with capabilities to monitor Sensor#4 and interact with the IN-CSE through Mca reference point;

- ADN-AE-5: a smartphone application embedded in the smartphone device with capabilities to interact directly with the oneM2M service platform IN-CSE through Mca reference point and discover and retrieve information related to Sensor#1, Sensor#2, Sensor#3 and Sensor#4.

- ADN-AE-6: a smartphone application embedded in the smartphone device with capabilities to interact directly with the oneM2M service platform IN-CSE through Mca reference point and manage and semantically annotate resources related to Sensor#1, Sensor#2, Sensor#3 and Sensor#4.

# 8	Semantic Modelling

The semantic modelling is typically based on an ontology that specifies classes and properties, i.e. the ontology defines the vocabulary to be used for the semantic description. In Figure 8-1, a simple ontology for the semantic annotation and discovery use case is visualized. Table 8-1 shows the actual OWL (Web Ontology Language) ontology in an RDF representation.

Figure 8-1: Simple ontology for the semantic annotation and discovery use case.

Table 8-1: OWL/RDF representation of the simple ontology for the semantic annotation and discovery use case.

<?xml version="1.0"?> <rdf:RDF xmlns="http://www.onem2m.org/ontology/temperature_example#" xml:base="http://www.onem2m.org/ontology/temperature_example" xmlns:rdf="http://www.w3.org/1999/02/22-rdf-syntax-ns#" xmlns:owl="http://www.w3.org/2002/07/owl#" xmlns:xml="http://www.w3.org/XML/1998/namespace" xmlns:xsd="http://www.w3.org/2001/XMLSchema#" xmlns:rdfs="http://www.w3.org/2000/01/rdf-schema#"> <owl:Ontology rdf:about="http://www.onem2m.org/ontology/temperature_example"/> <!-- Classes --> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#Fridge"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#House"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <owl:Class rdf:about="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/> <!-- Object Properties --> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasFridgeTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#Fridge"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasIndoorTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#House"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasOutdoorTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#House"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasTemperatureMeasuringFunction"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureSensor"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/> </owl:ObjectProperty> <owl:ObjectProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#measuresTemperature"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureMeasuringFunction"/> <rdfs:range rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> </owl:ObjectProperty> <!-- Data properties --> <owl:DatatypeProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasDatatype"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <rdfs:range rdf:resource="http://www.w3.org/2001/XMLSchema#string"/> </owl:DatatypeProperty> <owl:DatatypeProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#hasUnit"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <rdfs:range rdf:resource="http://www.w3.org/2001/XMLSchema#string"/> </owl:DatatypeProperty> <owl:DatatypeProperty rdf:about="http://www.onem2m.org/ontology/temperature_example#valueIsStoredIn"> <rdfs:domain rdf:resource="http://www.onem2m.org/ontology/temperature_example#TemperatureProperty"/> <rdfs:range rdf:resource="http://www.w3.org/2001/XMLSchema#anyURI"/> </owl:DatatypeProperty> </rdf:RDF>

Annex A shows how the simple ontology for the semantic annotation and discovery use case can be mapped to the oneM2M Base Ontology [i.3]. As a result, it is semantically integrated with the core concepts that have been identified for oneM2M itself. Such a mapping may be helpful to semantically relate to other parts of the oneM2M system, but is not required, i.e., depending on what is to be achieved, the above ontology can be used “stand-alone” as the basis for supporting semantic annotation and discovery in a particular use case as shown in this developer guide.

Figure 8-2: Semantic description of the scenario according to the ontology.

Figure 8-2 shows all the instances needed for modelling the semantic annotation and discovery use case, their respective types and their relations (in different colours and styles (e.g. dashed), but without annotations indicating the name of the respective relation) Each sensor will be represented by an AE and all the semantic instances related to the given sensor will be contained in the semantic descriptor. For example, IndoorTempSensor1 models the sensor, which has a function called TempFunction1, which measures IndoorProperty1, which in turn describes the indoor temperature of House 1. In addition there are some datatype properties like the unit of measurement, which are not shown in this figure.

# 9	Procedures

## 9.1	Introduction

In order to implement the presented use case based on oneM2M, required procedures are classified and shown below. This clause focuses on the core semantic aspects. Typical common aspects such as the creation of appropriate access control policies are not included. The interested reader is referred to other developer guides, e.g. TR-0025 [i.5].

- Application Registration: This procedure contains sensor application registration and smartphone application registration.

- Initial resource creation: This procedure contains container resources creation and contentInstance resources creation.

- Semantic descriptor resource creation: This procedure shows the creation of semantic descriptor resources by a smartphone application that is annotating the resources created earlier by the sensor applications.

- Semantic discovery of relevant sensor reources: This procdure shows how all sensor applications that fit the semantic filter criteria specified in SPARQL are discovered by a smartphone application.

- Retrieval of semantic descriptor and sensor information: This procedure shows how the smartphone application first retrieves the semantic descriptor resources of the discovered resource and then, based on the information contained in the semantic descriptor, retrieves the contentInstance resource containing the latest sensor reading.

## 9.2	Call Flows

### 9.2.1 	Application registration

Figure 9.2.1-1 depicts how the applications register with oneM2M and can be described as follows:

- Sensor applications (ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4) register with the oneM2M service platform (IN-CSE).

- Smartphone applications (ADN-AE5 and ADN-AE6) register with the oneM2M service platform (IN-CSE).

Figure 9.2.1-1: Registration phase call flows.

### 9.2.2 	Initial resource creation

Call flows regarding the initial resource creation phase depicted in figure 9.2.2-1 can be described as follows:

- Four container resources are created in the oneM2M service platform (IN-CSE) to store the the temperature values measured by Sensor#1, Sensor#2, Sensor#3 and Sensor#4 under the registered application ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4, respectively (in figure 9.2.2-1 this is only shown for ADN-AE1 and ADN-AE2, ADN-AE3 and ADN-AE4 are handled in exactly the same way).

- Content Instance resources are created by the applications (ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4) under each created container and represent the measured temperatures (in figure 9.2.2-1 this is only shown for the respective first contentInstances of ADN-AE1 and ADN-AE2, ADN-A3 and ADN-AE4 are handled in exactly the same way and contentInstances are created continuously).

Figure 9.2.2-1: Initial resource creation phase call flows.

### 9.2.3	Semantic descriptor resource creation

Call flows regarding the semantic descriptor resource creation phase are depicted in figure 9.2.3-1 and can be described as follows:

- ADN-AE5 creates a semantic descriptor resource under each of the ADN resources representing a sensor application instance (i.e ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4).The semantic information has been provided by a human user using the smartphone application. It provides information about the sensor, the sensor measurements (e.g. unit of measurement) and what is being measured. In the given example these are the information measured by the sensor (temperature), the unit of measurement (Celsius or Fahrenheit), and the relaton to the Thing for which the value is being measured (house or fridge).

Figure 9.2.3-1: Semantic descriptor resource creation phase call flows.

### 9.2.4	Semantic discovery of relevant sensor reources

Call flows regarding the discovery are depicted in figure 9.2.4-1 and can be described as follows:

- Smartphone application (ADN-AE6) sends a RETRIEVE request including the parameter  filterUsage and specific semantic filter criteria condition(s) provided in SPARQL for discovery of sensor application resources stored in the oneM2M service platform (IN-CSE).

- The oneM2M service platform (IN-CSE) responds with URIs of the discovered sensor resources, if any, to the smartphone application (ADN-AE6) according to the filter criteria.

Figure 9.2.4-1: Semantic discovery phase call flows.

### 9.2.5	Retrieval of semantic descriptor and sensor information

Call flows regarding the retrieval of the semantic descriptor and the contentInstance resources are depicted in figure 9.2.5-1 and can be described as follows:

- The smartphone application (ADN-AE6) sends GET requests for retrieval of the semantic descriptor child resources of the discovered sensor resources.

- The oneM2M service platform (IN-CSE) returns the requested semantic descriptor child resources.

- Based on the respective information contained in the retrieved semantic descriptor, the smartphone application (ADN-AE6)  requests the latest content instance provided by the sensor application containing the sensor measurement.

- The oneM2M service platform (IN-CSE) returns the requested content instance containing the sensor information.

Figure 9.2.5-1: Retrieval of semantic descriptor and sensor information phase call flows.

# 10	Implementation

## 10.1 	Introduction

Clause 10 presents necessary procedures required for the implementation of the semantic annotation and discovery use case, including conditions that must be met for the correct implementation of the current use case, and resource tree etc.

## 10.2 	Assumptions

Assumptions are presented as below in order to ensure the semantic annotation and discovery use case can be correctly implemented.

- Security is not considered in the current use case;

- HTTP binding of oneM2M primitives is used in the current use case;

- XML serializations of oneM2M primitives are used in the current use case;

- All mandatory HTTP headers are presented in the HTTP requests while optional headers are selectively used in the current use case;

- All mandatory resource attributes for resources presented in the current use case are presented in the HTTP requests while optional resource attributes are selectively used in the current use case;

- All AEs in the current use case are initially registered with the IN-CSEs and the identifier of the AEs are assigned by it acting as the Registrar CSE of the AE;

- All resources created in the current use case are addressable with the oneM2M Resource Identifier form of Hierarchical address;

- Short names for the representation of the resources and attributes are used in the current use case;

- Default access control policy has already been created under IN-CSE;

- All request originators send Blocking Requests for accessing resources located in CSEs.

## 10.3 	Resource Structure

### 10.3.1 	Introduction

The development of an oneM2M application includes the design of the resource trees of service capability layers, which is the IN-CSE in the current use case. The resource tree is constructed with child resources created according to the high level procedures presented in clause 9. All the child resources shown in the resource trees are mandatorily required in order to correctly implement the semantic annotation and discovery use case.

### 10.3.2 	Resource Structure of IN-CSE

The resource tree of IN-CSE starts with a CSEBase named server depicted in figure 10.3.2-1.

The root CSEBase has four direct child resources directly relevant to the semantic annotation and discovery use case, which are the tempsensorae1, tempsensorae2, tempsensorae3 and tempsensorae4 resources, representing ADN-AE1, ADN-AE2, ADN-AE3, and ADN-AE4, respectively. Each AE will have a container named temperature where the content instances (CI1 to CIN) are stored, and a semantic descriptor named SD1. As the substructure of each AE resource is exactly the same, only the substructure of tempsensorae1 is shown.

Figure 10.3.2-1: IN-CSE resource structure.

## 10.4	Role of Entities

### 10.4.1 	oneM2M service platform (IN-CSE)

The oneM2M service platform is modelled as an IN-CSE and is responsible for

- handling the registration requests from all ADN-AEs in the use case;

- creating and managing the resource structures for storing sensor information and semantic annotations;

- executing semantic resource discovery.

### 10.4.2 	Temperature sensor applications (ADN-AE1, ADN-AE2, ADN-AE3 and ADN-AE4)

Each of the temperature sensor applications are modelled as an ADN-AE and are responsible for

- measuring the sensor information;

- registering the temperature sensors with the IN-CSE;

- creating container resources named “temperature”;

- creating content instance resources under the container “temperature” that contain the temperature measurements.

### 10.4.3 	Semantic Annotation Application (ADN-AE5)

The semantic annotation application, which is expected to run on a smartphone or other device with user interface is responsible for the following

- enable the user to create semantic annotations for resources representing senors;

- create semantic descriptor resources as child resources of sensor AE resources that contain the semantic annotations.

### 10.4.4 	Semantic Discovery Application (ADN-AE6)

The semantic discovery application, which is ecpected to run on a user device, is responsible for the following:

- enable the user to formulate the semantic filter for the semantic discovery (in SPARQL);

- retrieve the semantic annotation for discovered resources;

- retrieve sensor measurements based on the semantic annotations.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex A:
Mapping to oneM2M Base Ontology

Figure A-1 shows the mapping of the specific concepts of the simple ontology for the semantic annotation and discovery use case to the more general concepts of the oneM2M Base Ontology [i.3]. Thus the semantic integration with the concepts identified for oneM2M itself is achieved.

Figure A-1: Mapping of the introduced concepts to the oneM2M Base Ontology.

When comparing to the concepts available in the complete oneM2M Base Ontology, it can be seen that the focus of the modelling here has been on the semantic aspects,  It is assumed that the functional aspects sre implemented by oneM2M AEs using the Mca interface. In the case of using non-oneM2M technologies and applications for the sensors, an interworking proxy would be needed to translate between oneM2M and the native technology. Using Generic Interworking as described in [i.4] with a complete modelling of the functionality according to the oneM2M Base Ontology (or an ontology that has been mapped to the oneM2M Base Ontology in a similar way as shown in Figure A-1) would allow the automatic creation of a oneM2M resource structure for the case and enable tool-support for the partially automated creation of the required interworking proxy.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?