| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST #31.2 |
| Source:* | Abdullah Aziz, Sejong University, G2016FFM082@sju.ac.kr Ting Martin MIAO, KETI, martin.miao@keti.re.kr JaeYoung Hwang, Sejong University, forest62590@sju.ac.kr Miguel Angel Reina Ortega, miguelangel.reinaortega@etsi.org |
| Date:* | 2017-07-28 |
| Reason for Change/s:* | Correct triggering message |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0019 |
| Clauses * | 5.4.2.2 Upper Tester Control Primitives |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0019 v0.3.0 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Clarify the triggering message format in terms of binding protocol level message. Update examples of triggering message and associated oneM2M request message in terms of HTTP binding.

Update of triggering message format after offline discussions.

### -----------------------Start of change 1-------------------------------------------

# 5	Abstract Test Method (ATM)

#### 5.4.2.2	Upper Tester Control Primitives

##### 5.4.2.2.1	Introduction

The upper tester triggering message is used to transport control commands between Test System and the Upper Tester Application. The control command will contain essential parameters that are required for certain testcase.

The upper tester triggering message type maps to particular message formats for exchanging data and those message formats are defined by TTCN-3 primitive as shown at table 5.4.2.2.1-1, UtTrigger and UtTriggerAck primitive.

Table 5.4.2.2.1-1 Mapping of TTCN-3 Primitives to oneM2M Service Primitives

| Upper TesterControl Message Type | TTCN-3 Primitives | Direction |
| --- | --- | --- |
|  |  | TS | UT |
| Trigger | UtTrigger Primitive | ( |
| Trigger Acknowledgement | UtTriggerAck Primitive | ( |

##### 5.4.2.2.2	UtTrigger and UtTriggerAck Primitives

The UtTrigger primitive is initialized by the Test System to send triggering message to the target IUT as depicted in Figure 5.4.2.2.2-1. The IUT will send acknowledgement message back to the Test System using UtTriggerAck primitive if trigger message is successfully transported to the IUT. Then IUT starts interaction with Test System through oneM2M request and response primitives.

Figure 5.4.2.2.2-1 Trigger message flow

Table 5.4.2.2.2-2  defines UtTrigger and UtTriggerAck primitives including oneM2M data types to which are mapped as well as examples to show how to implmenet UtTrigger and UtTriggerAck primitives.

Table 5.4.2.2.2-2 UtTrigger and UtTriggerAck Primitive

| Ut Control Primitive | Mapping to oneM2M data types | Description | Reference | Triggering Message | HTTP message |
| --- | --- | --- | --- | --- | --- |
| UtTrigger Primitive | request Primtive | ONLY essential parameters included for certain testcase* NOTE: Additional rules defined in Table 5.4.2.2.2-3 are also applied. | TS-0004 [ ] | Example-A: If the test objective is to test “Test System triggers IUT to execute a testcase for creation of <AE> with labels attribute under a CSEBase resource”, then the triggering message would be serialized as following: |
|  |  |  |  | Request { "rqp" :{ "op": 1, //indicate CREATE operation "ty": 2, //indicate AE resource type "to": {TEST_SYSTEM_ADDRESS}, "pc": { "ae": { "lbl":"UNINITIALIZED" //indicate that attribute labels needs to be included } } } } | Request POST /{SUT_UT_APPLICATION_URL} HTTP/1.1 Host: {SUT_IP_ADDRESS:PORT} Content-Length: {PAYLOAD_LENGTH} Content-Type: application/json { "rqp" :{ "op": 1, //indicate CREATE operation "ty": 2, //indicate AE resource type "to": {TEST_SYSTEM_ADDRESS}, "pc": { "ae": { "lbl":"UNINITIALIZED" //indicate that attribute labels needs to be included } } } } |
|  |  |  |  | Example-B: If the test objective is to test “Test System triggers IUT to execute a testcase for delete of a <AE> resource.”, then the triggering message would be serialized as following: |
|  |  |  |  | Request { "rqp" :{ "op": 4, //indicate DELETE operation "to": {TARGET_AE_RESOURCE_ADDRESS} //indicate Target AE resouce address } } | Request POST /{SUT_UT_APPLICATION_URL} HTTP/1.1 Host: {SUT_IP_ADDRESS:PORT} Content-Length: {PAYLOAD_LENGTH} Content-Type: application/json { "rqp" :{ "op": 4, //indicate DELETE operation "to": {TARGET_AE_RESOURCE_ADDRESS} //indicate Target AE resouce address } } |
| UtTriggerAck Primitive | responsePrimitive | ONLY responseStatusCode attribute included Note: Attribute response status code is defined at Table 5.4.2.2.2-3. | TS-0004 [ ] | Response { "rsp": { "rsc": 2000 } } For any triggering response, it only contains a response status code, and the response status code for the triggering operation can only be set to either 2000 (OK) or 4000 (BAD_REQUEST) according to the rules for triggering operations. | Response HTTP/1.1 200 OK X-M2M-RSC: 2000 |

Table 5.4.2.2.2-3 Rules for defining UtTrigger and UtTriggerAck primitives

UtTrigger primitive is represented in requestPrimitive serialized in JSON format. Parameters within UtTrigger are listed as following: operation: (mandatory)operation type that IUT is triggered to perform. resourceType: (optional)resource type of a target resource against which IUT is triggered to perform certain operation to: (mandatory)target resource against which IUT is triggered to perform certain operation. primitiveContent:(optional)represents the resource attributes that shall be included in the requestPrimitive.

Table 5.4.2.2.2-3 Definition of ResponseStatusCode for UtTriggerAck primitive

| Response Status Code Description | Response Status Code Value | Interpretation |
| --- | --- | --- |
| OK | 2000 | The SUT receives successfully the triggering message from Test System |
| BAD_REQUEST | 4000 | The SUT does not interpret correctly the UtTrigger primitive |
| Note: Only above two response status codes are allowed to use in UtTriggerAck primitive. |

##### 5.4.2.2.3	Control Communication Protocol

Protocol used for proceeding communications between TS and Upper Tester Application is designated to the Hypertext Transfer Protocol (HTTP) protocol owning it is an application protocol that is widely supported by most all IoT devices and various intrinsic features such as persistent connection, ease of programming, flexibility etc.

##### 5.4.2.2.4	Control Message Serialization

Control commands that are wrapped within a request body of HTTP message shall be serialized into JavaScript Object Notation (JSON) because it is very lightweight and easy to parse and generate for machines.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?