| Input Contribution |
| --- |
| Meeting ID* | TST#31.2 |
| Title:* | Implementation of Functional Entities |
| Source:* | In Song Lee, KETI, insong@keti.re.kr |
| Date:* | 2017-12-19 |
| Input related to* | TS-0017 Section A5 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0017 v0.1.0 |
| Decision requested or recommendation:* | Missing attributes which were found while updating TS-0018 document. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution provides Functional Entities and Resource Addressing Methods information.

### --------------------------------Start of change 1-----------------------------------------------

# A.5.1 Functional Entities, Roles and Reference Points

OneM2M functional entities, roles, and reference points defined in TS-0001 [1] is listed in table A.5.1.1, A.5.1.2, and A5.1.3, respectively.

Table A.5.1. 1 oneM2M Functional Entities

| Item | Entity Type | Mnemonic | Reference | Condition | Support |
| --- | --- | --- | --- | --- | --- |
| 1 | Application Entity |  | [1] 5.2.1 | C.1 | O Yes O No |
| 2 | Common Services Entity |  | [1] 5.2.1 | C.1 | O Yes O No |

C.1: The IUT shall be explicitly checked which entity type is going to be tested.

### --------------------------------End of change 1-----------------------------------------------

### --------------------------------Start of change 2-----------------------------------------------

A.5.2 Resource Addressing Methods

This section presents resource addressing methods specified in the oneM2M standard. There are two different methods for addressing a resource within the oneM2M resource structure with three different variants each depending on the scope of the request to access the resource. The ways how the resource IDs shall be constructed in each case are as follows:

Table A.5.2. 1 Resource Addressing Methods

| Item | Resource Addressing Methods | Mnemonic | Reference | Condition | Support |
| --- | --- | --- | --- | --- | --- |
| 1 | Non-Hierarchical | CSE-Relative |  | [1] 9.3.1 | C.1 | O Yes O No |
|  |  | SP-Relative |  | [1] 9.3.1 | C.1 | O Yes O No |
|  |  | Absolute |  | [1] 9.3.1 | C.1 | O Yes O No |
| 2 | Hierarchical | CSE-Relative |  | [1] 9.3.1 | C.1 | O Yes O No |
|  |  | SP-Relative |  | [1] 9.3.1 | C.1 | O Yes O No |
|  |  | Absolute |  | [1] 9.3.1 | C.1 | O Yes O No |

C.1: The IUT shall be explicitly declared resource addressing methods per testing session.

### --------------------------------End of change 2-----------------------------------------------