| Input Contribution |
| --- |
| Meeting ID* | TST33.2 |
| Title:* | New test purposes for 3GPP triggering |
| Source:* | Flynn Bob, Convida Wireless, Flynn.Bob@convidawireless.com |
| Date:* | 2018-02-27 |
| Input related to* | TS-0018 V3.0.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

3GPP Interworking is provide in Release 3.0.

This contribution provides some test purposes for the triggering functionality.

Upon review of TS-0026, I found that many of the procedures do not allow for easy/reasonable testing.  I am working on contributions to address that. In the meantime, I am writing a test purpose for a single purpose with the intent to be able to identify the additions needed to the test system.

One of the uses of the triggering request is to have the UE re-establish connectivity with the IN-CSE.  There is an implicit form of this request (requestReachability is FALSE therefore the IN-CSE initiates the request). There is also an explicit form of this request, an AE sends a <triggerRequest> to the IN-CSE, which is then used by the IN-CSE to generate the request.

These two test purposes are captured below.

TP1 – Check that the IUT sends an explicit 3GPP Device Trigger Request when it receives a valid <triggerRquest> from an AE.

TP2 – Check that the IUT sends an implicit 3GPP Device Trigger Request when it receives a <notification> request targeted for an AE hosted on a UE.

Using – “3GPP” to represent 3GPP Interworking

### -----------------------Start of new text 1-------------------------------------------

###### TP/oneM2M/CSE/3GPP/001

| TP Id | TP/oneM2M/CSE/3GPP/001 |
| --- | --- |
| Test objective | Check that the IUT sends an explicit 3GPP Device Trigger Request when it receives a valid <triggerRquest> from an AE. |
| Reference | TS-0026 7.5.1 |
| Parent Release | Release 3 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE1 and the AE1 being hosted on a 3GPP UE and the IUT allowing to register an AE2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE request from AE2 containing To set to AE2_RESOURCE_ADDRESS and From set to AE2_ID and Resource Type set to ?? (triggerRequest) and Content containing triggerRequest resource representation } | IUT ( AE1 |
|  | then { the IUT sends a Request to the SCEF containing 3GPP Device Trigger Request message containing A valid 3GPP Device Trigger Request } | IUT ( SCEF |

###### TP/oneM2M/CSE/3GPP/002

| TP Id | TP/oneM2M/CSE/3GPP/002 |
| --- | --- |
| Test objective | Check that the IUT sends an implicit 3GPP Device Trigger Request when it receives a valid <notification> from an AE. |
| Reference | TS-0026 7.5.1 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE1 and the AE1 being hosted on a 3GPP UE and the AE1 having subscribed to CONTAINER_RESOURCE_ADDRESS and the AE1 being not reachable and the IUT allowing to register an AE2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives the UPDATE request from the AE2 containing To set to CONTAINER_RESOURCE_ADDRESS containing From set to AE2_ID and Content containing container resource containing valid labels attribute } | IUT ( AE1 |
|  | then { the IUT sends a Request to the SCEF containing 3GPP Device Trigger Request message containing A valid 3GPP Device Trigger Request } | IUT ( SCEF |

-----------------------End of new text 1---------------------------------------------