| CHANGE REQUEST |
| --- |
| Meeting:* | TST TP34 |
| Source:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Date:* | 2018-02-20 |
| Contact:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Reason for Change/s:* | Add new content for Use case and Architecture Section |
| CR against: Release* | <Release3> |
| CR against: WI* | Active < WI-0058 - 3GPP_&_Cellular_IoT_IWK > MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0047-V0_0_2 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is add content for procedure of  UE reachability use case.

### -----------------------Start of change 1-------------------------------------------

# 8	Implementation

<Text> Describe the detail implementation procedure of the specified use case.

8.1 Implementation for UE Reachability monitoring

## 8.1.1 	Introduction

## This clause presents necessary procedures required for the implementation of the use case in clause 5.1, including conditions that should be met for the correct implementation of the current use case, and resource tree etc.

## 8.1.2 	Assumptions

Assumptions are presented as below in order to ensure the use case can be correctly implemented.

Security is not considered in the current use case;

CoAP binding of oneM2M primitives is used in the current use case, required features according to [i.3];

JSON serializations of oneM2M primitives is used in the current use case;

Short names for the representation of the resources and attributes are used in the current use case;

Each oneM2M entity including AE and CSE are addressable with correct host address that can be IP addresses or FQDN addresses resolved to IP addresses by DNS network services according to addressing rules specified in oneM2M standards.

The IN-CSE and ASN-CSE entities presented in this use case are addressable with the following identifiers, using SP-relative structured format.

IN-CSE:

CSE-ID: /in-cse

Resource ID: cse127865gu57fa

resourceName of IN-CSE’s CSEBase resource: server

ASN-CSE:

CSE-ID: /asn-cse

Resource ID: cse463432er91er

M2M-Ext-ID: 123456789@domain.com which should be pre-provioned in the 3GPP network.

ResourceName of CSEBase resource: terminal

### 8.1.3 	Resource Structure

See Figure: 7.1-2: Resource structure.

### 8.1.4	Implementation Procedures

| Step | Message Example in Clause 7.1 |
| --- | --- |
| 1 | CoAP Request: Method: 0.02(POST) Uri-Host: in-cse.provider.com:5683 Uri-Path: ~ Uri-Path: in-cse Uri-Path: cse127865gu57fa Content-Type: application/vnd.onem2m-res+json oneM2M-TY: 16 oneM2M-FR: asn-cse oneM2M-RQI: 0001 { "m2m: csr": { "rn": "asn-cse" "cb": "cse463432er91er", "csi": "asn-cse", } } |
| 2 | CoAP Response: 2.01 Created oneM2M-RSC: 2001 oneM2M-RQI: 0001 Location-Path: server/asn-cse |
| 3 | CoAP Request: Method: 0.02(POST) Uri-Host: in-cse.provider.com:5683 Uri-Path: ~ Uri-Path: in-cse Uri-Path: cse127865gu57fa Content-Type: application/vnd.onem2m-res+json oneM2M-TY: 14 oneM2M-FR: asn-cse oneM2M-RQI: 0001 { "m2m: nod": { "ni": "node123", "hcl": "asn-cse" } } |
| 4 | The same as Step2. |
| 5 | CoAP Request: Method: 0.02(PUT) Uri-Host: in-cse.provider.com:5683 Uri-Path: ~ Uri-Path: in-cse Uri-Path: cse127865gu57fa Content-Type: application/vnd.onem2m-res+json oneM2M-TY: 16 oneM2M-FR: asn-cse oneM2M-RQI: 0001 { "m2m: csr": { "nl": "node123" } } |
| 6 | CoAP Response: 2.04 Changed oneM2M-RSC: 2001 oneM2M-RQI: 0001 |
| 7 | CoAP Request: Method: 0.02(POST) Uri-Host: in-cse.provider.com:5683 Uri-Path: in-cse Uri-Path: cse127865gu57fa Uri-Path: node123 Content-Type: application/vnd.onem2m-res+json oneM2M-TY: 18 oneM2M-FR: in-ae oneM2M-RQI: 0001 { "m2m: sch": { "se": "* 0-30 0-23/2 * * * *",, " nco": TRUE } } |
| 8 | The same as Step2. |
| 9 | CoAP Request: Method: 0.02(POST) Uri-Host: in-cse.provider.com:5683 Uri-Path: in-cse Uri-Path: in-ae Uri-Path: cse127865gu57fa Uri-Path: cse463432er91er Uri-Path: node123 Uri-Path: schedule Content-Type: application/vnd.onem2m-res+json oneM2M-TY: 23 oneM2M-FR: in-ae oneM2M-RQI: 0003 { "m2m: sub": { " nu": "ae.provider.com/in-ae/application", " nct": 1 } } |
| 10 | CoAP Response: 2.01 Created oneM2M-RSC: 2001 oneM2M-RQI: 0001 Location-Path: server/in-ae |
| 11 | Editor Note: this step could not be specified until 3GPP CT3 has finished the API interface. |
| 12 | CoAP Request: Method: 0.02(POST) Uri-Host: ae.provider.com:5683 Uri-Path: ~ Uri-Path: in-ae Uri-Path: application Content-Type: application/vnd.onem2m-res+json oneM2M-TY: 18 oneM2M-FR: in-cse oneM2M-RQI: 0004 { "m2m: sch": { "se": "* 5-35 0-23/2 * * * *", } } |
| 13 | CoAP Response: 2.01 Created oneM2M-RSC: 2001 oneM2M-RQI: 0004 Location-Path: /in-ae/ae137849axcfrd/ |
| 14 | CoAP Request: Method: 0.02(POST) Uri-Host: asn-cse.provider.com:5683 Uri-Path: ~ Uri-Path: asn-cse Uri-Path: cse463432er91er Uri-Path: container1 Content-Type: application/vnd.onem2m-res+json oneM2M-TY: 4 oneM2M-FR: in-ae oneM2M-RQI: 0003 { "m2m:cin": { "cnf": "text/plains:0", "con": "off" } } |

### -----------------------End of change 1---------------------------------------------

## -----------------------Start of change 2---------------------------------------------2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]	oneM2M TS-0001 (V3.10.0): "Functional Architecture".

[i.3]	oneM2M TS-0008 (V3.0.0): "CoAP Protocol Binding".

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

修改为to