| Input Contribution |
| --- |
| Meeting ID* | TST34 |
| Title:* | TR-0051-AE resource API |
| Source:* | Laurent Velez, ETSI, laurent.velez@etsi.org |
| Date:* | 2018-03-10 |
| Input related to* | TR-0051 API Guide |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | To agree contribution to be implemented in TR-0051 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes add the clause 6.2.4 related the <AE> resource API for CREATE, RETRIEVE, UPDATE and DELETE.

================= start of input 1  =============================

### 6.2.4 	<AE> Resource

#### 6.2.4.0	Introduction

The <AE> resource represents information about an Application Entity that is registered to a CSE. The originator of a <AE> create request is and only can be an AE. A CSE is not allowed to initiate a <AE> create request.

The <AE> resource which resides in different kind of nodes such as Application Dedicated Node, Middle Node, Infrastructure Node etc. An Application Dedicated Node could reside in a constrained M2M device, while a Middle Node could reside in an M2M gateway and an Infrastructure Node could reside in an M2M Service Infrastructure. For example, in smart home scenario, light bulbs are modelled as Application Dedicated Node which communicate with home gateway which is modelled as a Middle Node and in resource registration phase, light bulbs can be registered as an <AE> resource.

#### 6.2.4.1	API-AE-CRE

| API Id | API/AE/CRE/001 API/AE/CRE/001_RCN/0 API/AE/CRE/001_RCN/1 API/AE/CRE/001_RCN/2 API/AE/CRE/001_RCN/3 |
| --- | --- |
| API Name | AE CREATE with resultContent parameter |
| Target Resource | <CSEBase> resource of the requested <AE> resource |
| Description | The interface is used by a AE Registree to send a <AE> CREATE request to a Registrar CSE and the Registrar CSE creates a <AE> resource and sends back a response to the AE Registree according to the configured resultContent parameter. When resultContent is set to 0: The response contains the response status code ONLY with no information of the created <AE> resource. When no resultContent or resultContent is set to 1 : The response contains a response status code as well as the <AE> resource information (attributes). When resultContent is set to 2: The response contains a response status code as well as the hierarchical address of the created <AE> resource information. When resultContent is set to 3: The response contains a response status code, the hierarchical address, and attributes of the created <AE> resource. Note that mandatory attributes for creation of the <AE> are highlighted in create request. A temperature sensor is registered to the platform by sending a <AE> registration request to the CSEBase. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | POST /mn-name POST /mn-name?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json; ty=2 |
| Example with RCN=0 | API/AE/CRE/001_RCN/0 HTTP Request: POST /mn-name?rcn=0 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: C Content-Type: application/json;ty=2 X-M2M-RI: 1234 { "m2m:ae": { "api": "A01.com.company.Temperature1", "lbl": ["indoor_temperature", "room_1"], "rr": true , "rn": "temp_sensor" } } HTTP Response: 201 Created Content-Location:/mnID/CAE858883098078930650 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 |
| Example with RCN=1 or No RCN | API/AE/CRE/001_RCN/1 HTTP Request: POST /mn-name?rcn=1 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: C Content-Type: application/json;ty=2 X-M2M-RI: 1234 { "m2m:ae": { "api": "A01.com.company.Temperature", "lbl": ["indoor_temperature", "room_1"], "rr": true , "rn": "ae_sensor" } } HTTP Response: 201 Created Content-Length:512 Content-Location:/mnID/CAE1505863946149808457 X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:ae" : { "rn" : "ae_sensor", "ty" : 2, "ri" : "/mnID/CAE7351383887726228787", "pi" : "/mnID", "ct" : "20180301T190714", "lt" : "20180301T190714", "lbl" : [ "indoor_temperature", "room_1" ], "acpi" : [ "/mnID/acp-2001585595046718886", "/mnID/acp-8048958765725327635" ], "et" : "20180301T190714", "api" : "A01.com.company.Temperature", "aei" : "CAE7351383887726228787", "poa" : [ ], "rev" : false, "rr" : true } } |
| Example with RCN=2 | API/AE/CRE/001_RCN/2 HTTP Request: POST /mn-name?rcn=2 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: C Content-Type: application/json;ty=2 X-M2M-RI: 1234 { "m2m:ae": { "api": "A01.com.company.Temperature", "lbl": ["indoor_temperature", "room_1"], "rr": true , "rn": "ae_sensor" } } HTTP Response: 201 Created Content-Location:/mnID/mn-name/ae_sensor X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 |
| Example with RCN=3 | API/AE/CRE/001_RCN/3 HTTP Request: POST /mn-name?rcn=3 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: C Content-Type: application/json;ty=2 X-M2M-RI: 1234 { "m2m:ae": { "api": "A01.com.company.Temperature", "lbl": ["indoor_temperature", "room_1"], "rr": true , "rn": "ae_sensor" } } HTTP Response: 201 Created Content-Location:/mnID/mn-name/ae_sensor X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:ae" : { "rn" : "ae_sensor", "ty" : 2, "ri" : "/mnID/CAE6676722585590805629", "pi" : "/mnID", "ct" : "20180301T191419", "lt" : "20180301T191419", "lbl" : [ "indoor_temperature", "room_1" ], "acpi" : [ "/mnID/acp-2001585595046718886", "/mnID/acp-199432176537153454" ], "et" : "20180301T191419", "api" : "A01.com.company.Temperature", "aei" : "CAE6676722585590805629", "poa" : [ ], "rev" : false, "rr" : true } } |

#### 6.2.4.2	API-AE-RET

| API Id | API/AE/RET/002_RCN/1 API/AE/RET/002_RCN/4 |
| --- | --- |
| API Name | AE RETRIEVE with resultContent parameter |
| Target Resource | The <AE> resource located under <CSEBase> |
| Description | The interface is used to send a <AE> RETRIEVE request attached with resultContent to the <AE> resource located under the <CSEBase> of the CSE, and the hosting CSE will send back a response according to the configured resultContent. When no resultContent or resultContent is set to 1: The response contains the attributes information of the requested <AE> resource. When resultContent is set to 4: The response contains both the attributes and child resources (if any) of the requested <AE> resource. This option is usuallt used to retrieve all child resources under a <AE> resource. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | GET /mn-name/ae_sensor GET /mn-name/ae_sensor?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with RCN=1 or No RCN | API/AE/RET/001_RCN/1 HTTP Request: GET /mn-name/ae_sensor?rcn=1 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: CAE1135360352263476883 Accept: application/json { "m2m:ae": { "api": "A01.com.company.Temperature1", "lbl": ["indoor_temperature", "room_1"], "rr": true , "rn": "temp_sensor" } } HTTP Response: 200 OK Content-Length:511 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2000 { "m2m:ae": { "rn": "ae_sensor", "ty": 2, "ri": "/mnID/CAE1135360352263476883", "pi": "/mnID", "ct": "20180301T191734", "lt": "20180301T191734", "lbl": [ "indoor_temperature", "room_1" ], "acpi": [ "/mnID/acp-2001585595046718886", "/mnID/acp-238706737653647361" ], "et": "20180301T191734", "api": "A01.com.company.Temperature", "aei": "CAE1135360352263476883", "poa": [], "rev": false, "rr": true } } |
| Example with RCN=4 | API/AE/RET/001_RCN/4 HTTP Request: GET /mn-name/ae_sensor?rcn=4 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: CAE1135360352263476883 Accept: application/json { "m2m:ae": { "api": "A01.com.company.Temperature1", "lbl": ["indoor_temperature", "room_1"], "rr": true , "rn": "temp_sensor" } } // In the example, the <AE> has 2 child <container> resource cont_temp1 and cont_temp2 HTTP Response: 200 OK Content-Length:511 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2000 { "m2m:ae": { "rn": "ae_sensor", "ty": 2, "ri": "/mnID/CAE3878123815422295646", "pi": "/mnID", "ct": "20180308T160039", "lt": "20180308T160039", "lbl": [ "indoor_temperature", "room_1" ], "acpi": [ "/mnID/acp-3006317496082032192", "/mnID/acp-3515261675190598034" ], "et": "20180308T160039", "api": "A01.com.company.Temperature", "aei": "CAE3878123815422295646", "poa": [], "rev": false, "rr": true, "cnt": [ { "rn": "cont_temp1", "ty": 3, "ri": "/mnID/cnt-1487951813418166085", "pi": "/mnID/CAE3878123815422295646", "ct": "20180308T161309", "lt": "20180308T161309", "lbl": [], "acpi": [ "/mnID/acp-3006317496082032192", "/mnID/acp-3515261675190598034" ], "et": "20180308T161309", "st": 0, "mni": 10000, "mbs": 0, "mia": 0, "cni": 0, "cbs": 0, "ol": "/mnID/mn-name/ae_sensor/cont_temp1/ol", "la": "/mnID/mn-name/ae_sensor/cont_temp1/la" }, { "rn": "cont_temp2", "ty": 3, "ri": "/mnID/cnt-5951235706464486326", "pi": "/mnID/CAE3878123815422295646", "ct": "20180308T161658", "lt": "20180308T161658", "lbl": [], "acpi": [ "/mnID/acp-3006317496082032192", "/mnID/acp-3515261675190598034" ], "et": "20180308T161658", "st": 0, "mni": 10000, "mbs": 0, "mia": 0, "cni": 0, "cbs": 0, "ol": "/mnID/mn-name/ae_sensor/cont_temp2/ol", "la": "/mnID/mn-name/ae_sensor/cont_temp2/la" } ] } } |

#### 6.2.4.3	API-AE-UPD

| API Id | API/AE/UPD/003 API/AE/UPD/003_RCN/0 API/AE/UPD/003_RCN/1 |
| --- | --- |
| API Name | AE UPDATE with resultContent set |
| Target Resource | The <AE> resource located under <CSEBase> resource of CSE |
| Description | The interface is used to send a <AE> UPDATE request to the target <AE> resource under the CSE, and the hosting CSE will send back a response only containing the response status code indicating the request processing status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | PUT /mn-name/temp_sensor PUT /mn-name/temp_sensor?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with RCN=0 | API/AE/UPD/003_RCN/0 HTTP Request: PUT /mn-name/ae_sensor?rcn=0 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: CAE1135360352263476883 Accept: application/json { "m2m:ae": { "poa": ["http://ae.temp.com:9090"] } } HTTP Response: 200 OK Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2004 |
| Example with RCN=1 or No RCN | API/AE/UPD/003_RCN/1 HTTP Request: PUT /mn-name/ae_sensor?rcn=1 HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: CAE1135360352263476883 Accept: application/json { "m2m:ae": { "poa": ["http://ae.temp.com:9090"] } } HTTP Response: 200 OK Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2004 { "m2m:ae": { "lt": "20180308T152401", "poa": [ "http://ae.temp.com:9090" ] } } |

#### 6.2.4.4	API-AE-DEL

| API Id | API/AE/DEL/004 |
| --- | --- |
| API Name | AE DELETE |
| Target Resource | The <AE> resource located under <CSEBase> resource of CSE |
| Description | The interface is used to send a <AE> DELETE request to the hosting CSE, and the hosting CSE will delete the <AE> and send back a response containing a response status code indicating the DELETE request status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | DELETE /mn-name/temp_sensor |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
|  | API/AE/DEL/004 HTTP Request: DELETE /mn-name/ae_sensor HTTP/1.1 Host: 127.0.0.1:8282 X-M2M-Origin: CAE1135360352263476883 Accept: application/json HTTP Response: 200 OK Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2002 |

================= end of input 1  =============================