| Input Contribution |
| --- |
| Meeting ID* | TST34 |
| Title:* | TR-0051-container resource API |
| Source:* | Laurent Velez, ETSI, laurent.velez@etsi.org Khalil Drira, LAAS-CNRS, drira@laas.fr Mahdi Ben Alaya, Sensinov, benalaya@sensinov.com |
| k | 2018-03-10 |
| Input related to* | TR-0051 API Guide |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | To agree contribution to be implemented in TR-0051 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes add the clause 6.2.5 related the <container> resource API for CREATE, RETRIEVE, UPDATE and DELETE.

================= start of input   =============================

### 6.2.5 	<container> Resource

#### 6.2.5.0	Introduction

The <container> resource represents a container for data instances. It is used to share information with other entities and potentially to track the data. A <container> resource has no associated content. It has only attributes and child resources.

The <container> resource can be seen as a container of a group of data instances with same characteristics, for example, sensor measurement of temperature, humidity, illumination, CO2 etc. For example, when a temperature sensor is modelled as application dedicated node and registered with an <AE> resource, a <container> resource can be created under the created <AE> as its child resource to contain temperature measurements. Note that <container> resource has no associated content and the real data is contained in a child resource of container called <contentInstance> which will be introduced in clause 6.2.6.

#### 6.2.5.1	API-CONT-CRE

| API Id | API/CONT/CRE/001 API/CONT/CRE/001_RCN0 API/CONT/CRE/001_RCN1 API/CONT/CRE/001_RCN2 API/CONT/CRE/001_RCN3 |
| --- | --- |
| API Name | container CREATE with and without resultContent parameter |
| Target Resource | <AE> resource as a parent resource of the requested <container> resource |
| Description | The interface is used to send a <container> CREATE request attached with resultContent under the <AE> resource located in the <CSEBase> . The hosting CSE will create the <container> resource under the <AE>, and send back a response according to the configured resultContent. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | POST /mn-name/ae_sensor POST /mn-name/ae_sensor?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json; ty=3 |
| Example with No RCN or RCN=1 | API/CONT/CRE/001 API/CONT/CRE/001_RCN1 HTTP Request: POST /mn-name/ae_sensor HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=3 X-M2M-RI: 1234 { "m2m:cnt": { "rn": "cont_temp" } } HTTP Response: 201 Created Content-Length:592 Content-Location:/mnID/cnt-4580755565072050133 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:cnt": { "rn": "cont_temp", "ty": 3, "ri": "/mnID/cnt-4580755565072050133", "pi": "/mnID/CAE3878123815422295646", "ct": "20180308T160054", "lt": "20180308T160054", "acpi": [ "/mnID/acp-3006317496082032192", "/mnID/acp-3515261675190598034" ], "et": "20180308T160054", "st": 0, "mni": 10000, "mbs": 0, "mia": 0, "cni": 0, "cbs": 0, } } |
| Example with RCN=0 | API/CONT/CRE/001_RCN/0 HTTP Request: POST /mn-name/ae_sensor HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=3 X-M2M-RI: 1234 { "m2m:cnt": { "rn": "cont_temp" } } HTTP Response: 201 Created Content-Length:592 Content-Location:/mnID/cnt-4580755565072050133 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 |
| Example with RCN=2 | API/CONT/CRE/001_RCN2 HTTP Request: POST /mn-name/ae_sensor?rcn=2 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=3 X-M2M-RI: 1234 { "m2m:cnt": { "rn": "cont_temp" } } HTTP Response: 201 Created Content-Location:/mnID/mn-name/ae_sensor/cont_temp Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 |
| Example with RCN=3 | API/CONT/CRE/001_RCN3 HTTP Request: POST /mn-name/ae_sensor?rcn=3 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=3 X-M2M-RI: 1234 { "m2m:cnt": { "rn": "cont_temp" } } HTTP Response: 201 Created Content-Location:/mnID/mn-name/ae_sensor/cont_temp Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:cnt" : { "rn" : "cont_temp", "ty" : 3, "ri" : "/mnID/cnt-5951235706464486326", "pi" : "/mnID/CAE3878123815422295646", "ct" : "20180308T161658", "lt" : "20180308T161658", "acpi" : [ "/mnID/acp-3006317496082032192", "/mnID/acp-3515261675190598034" ], "et" : "20180308T161658", "st" : 0, "mni" : 10000, "mbs" : 0, "mia" : 0, "cni" : 0, "cbs" : 0, } } |

#### 6.2.5.2	API-CONT-RET

| API Id | API/CONT/RET/002 API/CONT/RET/002_RCN1 API/CONT/RET/002_RCN4 |
| --- | --- |
| API Name | container RETRIEVE with or without resultContent parameter set |
| Target Resource | Requested <container> resource |
| Description | The interface is used to send a <container> RETRIEVE request attached with resultContent to the <container> resource located in the <CSEBase>. The hosting CSE will send back a response according to the configured resultContent. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | GET /mn-name/ae_sensor/cont_temp GET /mn-name/ae_sensor/cont_temp?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with No RCN or RCN=1 | API/AE/RET/001 API/AE/RET/001_RCN/1 HTTP Request: GET /mn-name/ae_sensor/cont_temp HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3878123815422295646 Accept: application/json HTTP Response: 200 OK Content-Length:592 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2000 { "m2m:cnt": { "rn": "cont_temp", "ty": 3, "ri": "/mnID/cnt-4580755565072050133", "pi": "/mnID/CAE3878123815422295646", "ct": "20180308T160054", "lt": "20180308T160054", "acpi": [ "/mnID/acp-3006317496082032192", "/mnID/acp-3515261675190598034" ], "et": "20180308T160054", "st": 0, "mni": 10000, "mbs": 0, "mia": 0, "cni": 0, "cbs": 0, } } |
| Example with RCN=4 | API/AE/RET/001_RCN4 HTTP Request: GET /mn-name/ae_sensor/cont_temp?rcn=4 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3878123815422295646 Accept: application/json // Container <cont_temp> has 2 child <contentInstance> resources HTTP Response: 200 OK Content-Length:1347 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2000 { "m2m:cnt": { "rn": "cont_temp", "ty": 3, "ri": "/mnID/cnt-4580755565072050133", "pi": "/mnID/CAE3878123815422295646", "ct": "20180308T160054", "lt": "20180308T160054", "acpi": [ "/mnID/acp-3006317496082032192", "/mnID/acp-3515261675190598034" ], "et": "20180308T160054", "st": 2, "mni": 10000, "mbs": 0, "mia": 0, "cni": 2, "cbs": 4, "cin": [ { "rn": "cin_6537328982813822227", "ty": 4, "ri": "/mnID/cin-6537328982813822227", "pi": "/mnID/cnt-4580755565072050133", "ct": "20180308T165713", "lt": "20180308T165713", "st": 0, "cnf": "text/plain:0", "cs": 2, "con": "27" }, { "rn": "cin_2833172679133296348", "ty": 4, "ri": "/mnID/cin-2833172679133296348", "pi": "/mnID/cnt-4580755565072050133", "ct": "20180308T165834", "lt": "20180308T165834", "st": 0, "cnf": "text/plain:0", "cs": 2, "con": "32" } ], } } |

#### 6.2.5.3	API-CONT-UPD

| API Id | API/CONT/UPD/001 API/CONT/UPD/001_RCN0 API/CONT/UPD/001_RCN1 |
| --- | --- |
| API Name | container UPDATE with or without resultContent set |
| Target Resource | Requested <container> resource |
| Description | The interface is used to send a <container> UPDATE request to the target <container> resource located under the CSE, and the hosting CSE will respond with only the response status code to indicate the UPDATE operation status |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | PUT /mn-name/temp_sensor/cont_temp PUT /mn-name/temp_sensor/cont_temp?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with No RCN or RCN=1 | API/CONT/UPD/001 HTTP Request: PUT /mn-name/ae_sensor/cont_temp HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE1135360352263476883 Accept: application/json { "m2m:cnt": { "mni": 10000, "lbl": ["indoor_temperature"] } } HTTP Response: 200 OK Content-Type:application/json Content-Length:592 X-M2M-Origin:/mnID X-M2M-RSC:2004 { "m2m:cnt": { "lt": "20180308T171315", "lbl": [ "indoor_temperature" ], "st": 3, "mni": 10000 } } |
| Example with RCN=0 | API/CONT/UPD/001_RCN0 HTTP Request: PUT /mn-name/ae_sensor/cont_temp?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE1135360352263476883 Content-Type: application/json { "m2m:cnt": { "mni": 10000, "lbl": ["indoor_temperature"] } } HTTP Response: 200 OK Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2004 |

#### 6.2.5.4	API-CONT-DEL

| API Id | API/CONT/DEL/001 API/CONT/DEL/001_RCN0 |
| --- | --- |
| API Name | container DELETE with no resultContent (or resultContent set to 0 ) |
| Target Resource | Requested <container> resource |
| Description | The interface is used to send a <container> DELETE request to a target <container> resource located under the CSE, and the hosting CSE will respond with only response status code to indicate the DELETE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | DELETE /mn-name/temp_sensor/cont_temp DELETE /mn-name/temp_sensor/cont_temp?rcn=0 |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with No RCN or RCN=0 | API/CONT/DEL/001 API/CONT/DEL/001_RCN0 HTTP Request: DELETE /mn-name/ae_sensor/cont_temp HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE1135360352263476883 HTTP Response: 200 OK X-M2M-Origin:/mnID X-M2M-RSC:2002 |

================= end of input   =============================