| Input Contribution |
| --- |
| Meeting ID* | TST34 |
| Title:* | TR-0051-contentInstance resource API |
| Source:* | Laurent Velez, ETSI, laurent.velez@etsi.org Khalil Drira, LAAS-CNRS, drira@laas.fr Mahdi Ben Alaya, Sensinov, benalaya@sensinov.com |
| Date:* | 2018-03-10 |
| Input related to* | TR-0051 API Guide |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | To agree contribution to be implemented in TR-0051 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes add the clause 6.2.6 related the <contentInstance> resource API for CREATE, RETRIEVE and DELETE.

================= start of input   =============================

### 6.2.6 	<contentInstance> Resource

#### 6.2.6.0	Introduction

The <contentInstance> resource represents a data instance stored in the <container> resource. Taking a temperature sensor device as an example, the temperature sensor is designed to collect temperature data of environment and in this case, the real temperature data is modelled as a <contentInstance> resource. In details, we assume both the temperature sensor is registered with <AE> resource and a <container> resource is created under the <AE> to store temperature instances, under this consumption, whenever the temperature data is uploaded into a central server, the temperature data has to be denoted as a value of content attribute of <contentInstance> resource.

The <contentInstance> resource cannot be modified once created, and is able to be deleted explicitly by an AE or may be deleted by the platform based on specific policies. If the platform has policies to manage the <contentInstance> resource, these policies are represented by attributes axByteSize, maxNrOfInstances and/or maxInstanceAge attributes in their parent <container> resource.

The <contentInstance> resource inheritances the same access control policies of its parent <container> resource, and does not have its own accessControlPolicyIDs attribute.

#### 6.2.6.1	API-CI-CRE

| API Id | API/CI/CRE/001 API/CI/CRE/001_RCN/0 API/CI/CRE/001_RCN/1 API/CI/CRE/001_RCN/2 API/CI/CRE/001_RCN/3 |
| --- | --- |
| API Name | contentInstance CREATE with or without resultContent parameter |
| Target Resource | The <container> resource as a parent resource of being created <contentInstance> resource |
| Description | The interface is used to send a <contentInstance> CREATE request attached with resultContent to the target <container> resource located under the CSE, and the hosting CSE will create a new <contentInstance> under the requested <container>, and send back a response containing only the reponse status code to indicate the CREATE operation status. When resultContent is set to 0: The response contains the response status code ONLY with no information of the created <contentInstance> resource. When no resultContent or resultContent is set to 1: The response contains a response status code as well as the <contentInstance> resource information. When resultContent is set to 2: The response contains a response status code as well as the hierarchical address of the created <contentInstance> resource information. When resultContent is set to 3: The response contains a response status code, the hierarchical address, and attributes of the created <contentInstance> resource. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | POST /mn-name/ae_sensor/cont_temp POST /mn-name/ae_sensor/cont_temp?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json; ty=4 |
| Example with No RCN Or RCN=1 | API/CONT/CRE/001 API/CI/CRE/001_RCN/1 HTTP Request: POST /mn-name/ae_sensor/cont_temp HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Length:592 Content-Location:/mnID/cnt-4580755565072050133 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:cin" : { "rn" : "cin_7663115239486391043", "ty" : 4, "ri" : "/mnID/cin-7663115239486391043", "pi" : "/mnID/cnt-5532005569015612527", "ct" : "20180308T201142", "lt" : "20180308T201142", "st" : 0, "cnf" : "text/plain:0", "cs" : 2, "con" : "20" } } |
| Example with rcn=0 | API/CI/CRE/001_RCN/0 HTTP Request: POST /mn-name/ae_sensor/cont_temp?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Location:/mnID/cnt-4580755565072050133 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 |
| Example with RCN=2 | API/CI/CRE/001_RCN/2 HTTP Request: POST /mn-name/ae_sensor/cont_temp?rcn=2 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Location:/mnID/mn-name/ae_sensor/cont_temp/cin_251399441710383097 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 |
| Example with RCN=3 | API/CI/CRE/001_RCN/3 HTTP Request: POST /mn-name/ae_sensor/cont_temp?rcn=3 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Length:351 Content-Location: /mnID/mn-name/ae_sensor/cont_temp/cin_579925401925721153 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:cin" : { "rn" : "cin_5799254019257211538", "ty" : 4, "ri" : "/mnID/cin-5799254019257211538", "pi" : "/mnID/cnt-5532005569015612527", "ct" : "20180308T202316", "lt" : "20180308T202316", "st" : 0, "cnf" : "text/plain:0", "cs" : 2, "con" : "20" } } |

#### 6.2.6.2	API-CI-RET

| API Id | API/CI/RET/001_LA API/CI/RET/001_OL API/CI/RET/001_CI |
| --- | --- |
| API Name | Latest , Oldest or specific contentInstance RETRIEVE |
| Target Resource | <latest> , <oldest> virtual resources or individual <contentInstance> resource of the requested <container> resource |
| Description | The interface is used to send a <contentInstance> RETRIEVE request to the CSE, and the hosting CSE will send back a response containing the result. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | GET /mn-name/ae_sensor/cont_temp/la GET /mn-name/ae_sensor/cont_temp/ol GET /mn-name/ae_sensor/cont_temp/ci |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with latest | API/CI/RET/001_LA HTTP Request: GET /mn-name/ae_sensor/cont_temp/la HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:351 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2000 { "m2m:cin": { "rn": "cin_3119496110835442180", "ty": 4, "ri": "/mnID/cin-3119496110835442180", "pi": "/mnID/cnt-2918839993456309251", "ct": "20180312T155815", "lt": "20180312T155815", "lbl": [], "st": 0, "cnf": "text/plain:0", "cs": 2, "con": "26" } } |
| Example with oldest | API/CI/RET/001_OL HTTP Request: GET /mn-name/ae_sensor/cont_temp/ol HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:351 Content-Type:application/json X-M2M-Origin:/mnID X-M2M-RSC:2000 { "m2m:cin": { "rn": "cin_1114196738284658980", "ty": 4, "ri": "/mnID/cin-1114196738284658980", "pi": "/mnID/cnt-2918839993456309251", "ct": "20180312T155735", "lt": "20180312T155735", "lbl": [], "st": 0, "cnf": "text/plain:0", "cs": 2, "con": "20" } |
| Example with CI name | API/CI/RET/001_CI HTTP Request: GET /mn-name/ae_sensor/cont_temp/cin_1018950784553449755 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:351 Content-Type:application/json X-M2M-Origin:/mnID { "m2m:cin": { "rn": "cin_1018950784553449755", "ty": 4, "ri": "/mnID/cin-1018950784553449755", "pi": "/mnID/cnt-2918839993456309251", "ct": "20180312T155756", "lt": "20180312T155756", "lbl": [], "st": 0, "cnf": "text/plain:0", "cs": 2, "con": "32" } } |

#### 6.2.6.3	API-CI-DEL

| API Id | API/CI/DEL/001_LA API/CI/DEL/001_OL API/CI/DEL/001_CI |
| --- | --- |
| API Name | Latest , Oldest or specific contentInstance DELETE |
| Target Resource | <latest> , <oldest> virtual resources or individual <contentInstance> resource of the requested <container> resource |
| Description | The interface is used to send a <container> DELETE request to the CSE, and the hosting CSE will delete the <contentInstance>, and send back a response containing the response status code to indicate the status of the DELETE operation. . |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | DELETE /mn-name/ae_sensor/cont_temp/la DELETE /mn-name/ae_sensor/cont_temp/ol DELETE /mn-name/ae_sensor/cont_temp/ci |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with latest | API/CI/DEL/001_LA HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/la HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 X-M2M-RI: 1234 HTTP Response: 200 OK X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2002 |
| Example with oldest | API/CI/DEL/001_OL HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/ol HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:351 X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2002 |
| Example with CI name | API/CI/DEL/001_CI HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/cin_temp1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE3650998535091944901 X-M2M-RI: 1234 HTTP Response: 200 OK X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2002 |

================= end of input   =============================