| Input Contribution |
| --- |
| Meeting ID* | TST34 |
| Title:* | TR-0051_supplementation_of_resources |
| Source:* | In Song Lee, KETI, insong@keti.re.kr SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr |
| Date:* | 2018-03-12 |
| Input related to* | TR-0051 V0.0.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution is for TR-0051 API guide.

It was written down based on the CRUD request and response.

I dealt with these resources in this document.

- <group> resource

- <timeSeries> resource

- <timeSeriesInstance> resource

- <accessControlPolicy> resource

### -----------------------Start of new text 1-------------------------------------------

### 6.2.10 	<group> Resource

The <group> resource represents a group of resources of the same or mixed types. It basically designed to handle numerous of resources at the same time. When a request sent through the <group> resource, it distributes the request to each member of the <group> resources, which are indicated by the memberIDs attribute. It also aggregates responses from each resource. The <group> resource is the fundamental feature of the usual service likes data management, subscription, notification, etc. As an example, by using bulk commands notification, the <group> resource can manage actuators such as lamps.

#### 6.2.10.1	API-GRP-CRE

| API Id | API/GRP/CRE/001 API/GRP/CRE/001/RCN0 API/GRP/CRE/001/RCN1 API/GRP/CRE/001/RCN2 API/GRP/CRE/001/RCN3 |
| --- | --- |
| API Name | <group> resource CREATE with resultContent parameter |
| Target Resource | <AE> resource of the requested <group> resource |
| Description | The interface is used to send a <group> CREATE request attached with resultContent to the Registrar CSE, and the Registrar CSE creates a <group> resource, and sends back a response containing a response status code to indicate the CREATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | POST /mn-name/ae_actuator POST /mn-name/ae_actuator?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=9 |
| Example with RCN=0 | API/GRP/CRE/001/RCN0 HTTP Request: POST /mn-name/ae_actuator?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=9 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:grp": { "mid": [ "/mn-name/ae_actuator/lamp_container”, "/mn-name/ae_actuator/lamp_container1” ], "mt": 3, "mnm": 50, "rn": "lamp_group" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Example with no RCN or RCN=1 | API/GRP/CRE/001 API/GRP/CRE/001/RCN1 HTTP Request: POST /mn-name/ae_actuator?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=9 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:grp": { "mid": [ "/mn-name/ae_actuator/lamp_container", "/mn-name/ae_actuator/lamp_container1" ], "mt": 3, "mnm": 50, "rn": "lamp_group" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:grp": { "rn": "lamp_group", "ty": 9, "ri": "/mnID/GRP792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "cr": "CAE5630283216026458665", "mt": 3, "cnm": 2, "mnm": 50, "mid": [ "/mn-name/ae_actuator/lamp_container", "/mn-name/ae_actuator/lamp_container1" ] "mtv": true, "csy": 1 } } |
| Example with RCN=2 | API/GRP/CRE/001/RCN2 HTTP Request: POST /mn-name/ae_actuator?rcn=2 HTTP/1.1 Host: 192.168.0.10:8282192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=9 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:grp": { "mid": [ "/mn-name/ae_actuator/lamp_container", "/mn-name/ae_actuator/lamp_container1" ], "mt": 3, "mnm": 50, "rn": "lamp_group" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:uri": "/mn-name/ae_actuator/group_lamp" } |
| Example with RCN=3 | API/GRP/CRE/001/RCN3 HTTP Request: POST /mn-name/ae_actuator?rcn=3 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=9 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:grp": { "mid": [ "/mn-name/ae_actuator/lamp_container", "/mn-name/ae_actuator/lamp_container1" ], "mt": 3, "mnm": 50, "rn": "lamp_group" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:rcn": { "uri": "/mn-name/ae_actuator/group_lamp" "m2m:grp": { "rn": "lamp_group", "ty": 9, "ri": "/mnID/GRP792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "cr": "CAE5630283216026458665", "mt": 3, "cnm": 2, "mnm": 50, "mid": [ "/mn-name/ae_actuator/lamp_container", "/mn-name/ae_actuator/lamp_container1" ] "mtv": true, "csy": 1 } } } |

#### 6.2.10.2	API-GRP-RET

| API Id | API/GRP/RET/001 API/GRP/RET/001/RCN1 |
| --- | --- |
| API Name | <group> resource RETRIEVE with resultContent set to 1 |
| Target Resource | Requested <group> resource |
| Description | The interface is used to send a <group> RETRIEVE request attached with resultContent set to 1 to the Registrar CSE, and the hosting CSE sends back a retrieved <group> resource information. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | GET /mn-name/ae_actuator/group_lamp GET /mn-name/ae_actuator/group_lamp?rcn=1 |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator |
| Example with no RCN or RCN=1 | API/GRP/RET/001 API/GRP/RET/001/RCN1 HTTP Request: GET /mn-name/ae_actuator/group_lamp?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2000 { "m2m:grp": { "rn": "lamp_group", "ty": 9, "ri": "/mnID/GRP792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "cr": "CAE5630283216026458665", "mt": 3, "cnm": 2, "mnm": 50, "mid": [ "/mn-name/ae_actuator/lamp_container", "/mn-name/ae_actuator/lamp_container1" ] "mtv": true, "csy": 1 } } |

#### 6.2.10.3	API-GRP-UPD

| API Id | API/GRP/UPD/001 API/GRP/UPD/001/RCN0 API/GRP/UPD/001/RCN1 |
| --- | --- |
| API Name | <group> resource UPDATE with resultContent parameter |
| Target Resource | Requested <group> resource |
| Description | The interface is used to send a <group> UPDATE request attached with resultContent to the Registrar CSE, and the Registrar CSE updates a <group> resource, and sends back a response containing a response status code to indicate the UPDATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | PUT /mn-name/ae_actuator/group_lamp PUT /mn-name/ae_actuator/group_lamp?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator |
| Example with RCN=0 | API/GRP/UPD/001/RCN0 HTTP Request: PUT /mn-name/ae_actuator/group_lamp?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:grp": { "mnm": 100 } } HTTP Response: 200 OK Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2004 |
| Example with no RCN or RCN=1 | API/GRP/UPD/001 API/GRP/UPD/001/RCN1 HTTP Request: PUT /mn-name/ae_actuator/group_lamp?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:grp": { "mnm": 100, "rn": "lamp_group" } } HTTP Response: 200 OK Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2004 { "m2m:grp": { "rn": "lamp_group", "ty": 9, "ri": "/mnID/GRP792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "cr": "CAE5630283216026458665", "mt": 3, "cnm": 2, "mnm": 100, "mid": [ "/mn-name/ae_actuator/lamp_container", "/mn-name/ae_actuator/lamp_container1" ] "mtv": true, "csy": 1 } } |

#### 6.2.10.4	API-GRP-DEL

| API Id | API/GRP/DEL/001 API/GRP/DEL/001/RCN0 API/GRP/DEL/001/RCN1 |
| --- | --- |
| API Name | <group> resource DELETE with resultContent parameter |
| Target Resource | Requested <group> resource |
| Description | The interface is used to send a <group> DELETE request attached with resultContent to the Registrar CSE, and the Registrar CSE deletes a <group> resource, and sends back a response containing a response status code to indicate the DELETE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | DELETE /mn-name/ae_actuator/group_lamp DELETE /mn-name/ae_actuator/group_lamp?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json; ty=2 . |
| Example with no RCN or RCN=0 | API/GRP/DEL/001 API/GRP/DEL/001/RCN0 HTTP Request: DELETE /mn-name/ae_actuator/group_lamp?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2002 |
| Example with RCN=1 | API/GRP/DEL/001/RCN1 HTTP Request: DELETE /mn-name/ae_actuator/group_lamp?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_actuator/group_lamp Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2002 { "m2m:grp": { "rn": "lamp_group", "ty": 9, "ri": "/mnID/GRP792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445" } } |

### 6.2.11 	<timeSeries> Resource

The <timeSeries> resource represents a container for Time Series Data Instance. The <timeSeries> resource represents a container for Time Series Data instances. It is used to share information with other entities and potentially to track, detect and report the missing data in Time Series. A <timeSeries> resource has no associated content but it only has attributes and child resources. It is quite similar to the <container> resource since both represent as a container for instances And also both only have attributes and child resources. But the big difference between those two resources is that <timeSeries> resource is designed to store time series data instances.

#### 6.2.11.1	API-TS-CRE

| API Id | API/TS/CRE/001 API/TS/CRE/001/RCN0 API/TS/CRE/001/RCN1 API/TS/CRE/001/RCN2 API/TS/CRE/001/RCN3 |
| --- | --- |
| API Name | <timeSeries> resource CREATE with resultContent parameter |
| Target Resource | <AE> resource of the requested <timeSeries> resource |
| Description | The interface is used to send a <timeSeries> CREATE request attached with resultContent to the Registrar CSE, and the Registrar CSE creates a <timeSeries> resource, and sends back a response containing a response status code to indicate the CREATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | POST /mn-name/ae_sensor POST /mn-name/ae_sensor?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=29 |
| Example with RCN=0 | API/TS/CRE/001/RCN0 HTTP Request: POST /mn-name/ae_sensor?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "rn": timeSeries_cont, "pei": 1, "mdd": true, "mdt": 1 } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Example with no RCN or RCN=1 | API/TS/CRE/001 API/TS/CRE/001/RCN1 HTTP Request: POST /mn-name/ae_sensor?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "rn": timeSeries_cont, "pei": 1, "mdd": true, "mdt": 1 } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:ts": { "rn": "timeSeries_cont", "ty": 29, "ri": "/mnID/TS792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "et": "2021212T170445", "st": "0", "cr": "CAE5630283216026458665", "mni": "3153600000", "mbs": "3153600000", "mia": "31536000", "cni": "0", "cbs": "0", "pei": "1", "mdd": "ture", "mdn": "1000", "mdc": "0", "mdt": "1" } } |
| Example with RCN=2 | API/TS/CRE/001/RCN2 HTTP Request: POST /mn-name/ae_sensor?rcn=2 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "rn": timeSeries_cont, "pei": 1, "mdd": true, "mdt": 1 } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:uri": "/mn-name/ae_sensor/timeSeries_cont" } |
| Example with RCN=3 | API/TS/CRE/001/RCN3 HTTP Request: POST /mn-name/ae_sensor?rcn=3 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "rn": timeSeries_cont, "pei": 1, "mdd": true, "mdt": 1 } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:rce": { "uri": "/mn-name/ae_sensor/timeSeries_cont" "m2m:ts": { "rn": "timeSeries_cont", "ty": 29, "ri": "/mnID/TS792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "et": "2021212T170445", "st": "0", "cr": "CAE5630283216026458665", "mni": "3153600000", "mbs": "3153600000", "mia": "31536000", "cni": "0", "cbs": "0", "pei": "1", "mdd": "ture", "mdn": "1000", "mdc": "0", "mdt": "1" } } } |

#### 6.2.11.2	API-TS-RET

| API Id | API/TS/CRE/001 API/TS/CRE/001/RCN1 |
| --- | --- |
| API Name | <timeSeries> resource RETRIEVE with resultContent parameter |
| Target Resource | Requested <timeSeries> resource |
| Description | The interface is used to send a <timeSeries> RETRIEVE request attached with resultContent set to 1 to the Registrar CSE, and the hosting CSE sends back a retrieved <timeSeries> resource information. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | GET /mn-name/ae_sensor/timeSeries_cont GET /mn-name/ae_sensor/timeSeries_cont?rcn=1 |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator |
| Example with no RCN or RCN=1 | API/TS/RET/001 API/TS/RET/001/RCN1 HTTP Request: GET /mn-name/ae_sensor?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2000 { "m2m:ts": { "rn": "timeSeries_cont", "ty": 29, "ri": "/mnID/TS792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "et": "2021212T170445", "st": "0", "cr": "CAE5630283216026458665", "mni": "3153600000", "mbs": "3153600000", "mia": "31536000", "cni": "0", "cbs": "0", "pei": "1", "mdd": "ture", "mdn": "1000", "mdc": "0", "mdt": "1" } } |

#### 6.2.11.3	API-TS-UPD

| API Id | API/TS/UPD/001 API/TS/UPD/001/RCN0 API/TS/UPD/001/RCN1 |
| --- | --- |
| API Name | <timeSeries> resource UPDATE with resultContent parameter |
| Target Resource | Requested <timeSeries> resource |
| Description | The interface is used to send a <timeSeries> UPDATE request attached with resultContent to the Registrar CSE, and the Registrar CSE updates a <timeSeries> resource, and sends back a response containing a response status code to indicate the UPDATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | PUT /mn-name/ae_sensor/timSeries_cnt PUT /mn-name/ae_sensor/timSeries_cnt?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with RCN=0 | API/TS/UPD/001/RCN0 HTTP Request: PUT /mn-name/ae_sensor/timeSeries_cont?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "mdt": 2 } } HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2004 |
| Example with no RCN or RCN=1 | API/TS/UPD/001 API/TS/UPD/001/RCN1 HTTP Request: POST /mn-name/ae_sensor/timeSeries_cont?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "mdt": 2 } } HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2004 { "m2m:ts": { "rn": "timeSeries_cont", "ty": 29, "ri": "/mnID/TS792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445", "et": "2021212T170445", "st": "0", "cr": "CAE5630283216026458665", "mni": "3153600000", "mbs": "3153600000", "mia": "31536000", "cni": "0", "cbs": "0", "pei": "1", "mdd": "ture", "mdn": "1000", "mdc": "0", "mdt": "2" } } |

#### 6.2.11.4	API-TS-DEL

| API Id | API/TS/DEL/001 API/TS/DEL/001/RCN0 API/TS/DEL/001/RCN1 |
| --- | --- |
| API Name | <timeSeries> resource DELETE with resultContent parameter |
| Target Resource | Requested <timeSeries> resource |
| Description | The interface is used to send a <timeSeries> DELETE request attached with resultContent to the Registrar CSE, and the Registrar CSE updates a <timeSeries> resource, and sends back a response containing a response status code to indicate the DELETE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | DELETE /mn-name/ae_sensor/timSeries_cnt DELETE /mn-name/ae_sensor/timSeries_cnt?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json |
| Example with no RCN or RCN=0 | API/TS/DEL/001 API/TS/DEL/001/RCN0 HTTP Request: DELETE /mn-name/ae_sensor/timeSeries_cont?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2002 |
| Example with RCN=1 | API/TS/DEL/001/RCN1 HTTP Request: DELETE /mn-name/ae_sensor/timeSeries_cont?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=29 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "mdt": 2 } } HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2002 { "m2m:ts": { "rn": "timeSeries_cont", "ty": 29, "ri": "/mnID/TS792482146823489621", "pi": "/mnID/CAE5630283216026458665", "ct": "20171212T170445", "lt": "20171212T170445" } } |

### 6.2.12 	<timeSeriesInstance> Resource

The <timeSeriesInstance> resource represents a data instance in the <timeSeries> resource. As similar to the <contentInstance> resource, <timeSeriesInstance> resource shall not be modified once created. To update the data of this, there should be delete procedure and then make the new <timeSeriesInstance> resource. If the platform has policies for <timeSeriesInstance> resource, these shall be represented by the attributes maxByteSize, maxNrOfInstances and maxInstanceAge attributes in the <timeSeries> resource. If multiple policies are in effect, the strictest policy shall apply. The <timeSeriesInstance> resource inherits the same access control policies of the parent <timeSeries> resource, and does not have its own accessControlPolicyIDs attribute.

#### 6.2.12.1	API-TSI-CRE

| API Id | API/TSI/CRE/001 API/TSI/CRE/001/RCN0 API/TSI/CRE/001/RCN1 API/TSI/CRE/001/RCN2 API/TSI/CRE/001/RCN3 |
| --- | --- |
| API Name | <timeSeriesInstance> resource CREATE with resultContent parameter |
| Target Resource | <timeSeries> resource of the requested <timeSeriesInstance> resource |
| Description | The interface is used to send a <timeSeriesInstance> CREATE request attached with resultContent to the Registrar CSE, and the Registrar CSE creates a <timeSeriesInstance> resource, and sends back a response containing a response status code to indicate the CREATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | POST /mn-name/ae_sensor/timeSeries_cont/tsi_value1 POST /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=30 |
| Example with RCN=0 | API/TSI/CRE/001/RCN0 HTTP Request: POST /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=30 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "dgt": "20180307T123456", "con": "DATA_TACK" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont/tsi_value1 Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Example with no RCN or RCN=1 | API/TSI/CRE/001 API/TSI/CRE/001/RCN1 HTTP Request: POST /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=30 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "dgt": "20180307T123456", "con": "DATA_TACK" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont/tsi_value1 Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:tsi": { "ty": 30, "pi": "/mnID/CAE5630283216026458665", "ri": "/mnID/TSI840674869203617594", "rn": "tsi_value1", "ct": "20180307T012211", "lt": "20180307T012211", "et": "2n0210307T012211", "dgt": "20180307T123456" "con": "DATA_TACK", "cs": 9, "st": 7 } } |
| Example with RCN=2 | API/TSI/CRE/001/RCN2 HTTP Request: POST /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=2 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=30 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "dgt": "20180307T123456", "con": "DATA_TACK" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont/tsi_value1 Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:uri": "/mn-name/ae_sensor/timeSeries_cont/tsi_value1" } |
| Example with RCN=3 | API/TSI/CRE/001/RCN3 HTTP Request: POST /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=3 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=30 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:ts": { "dgt": "20180307T123456", "con": "DATA_TACK" } } HTTP Response: 201 Created Content-Location: /mn-name/ae_sensor/timeSeries_cont/tsi_value1 Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:rce": { "uri": "/mn-name/ae_sensor/timeSeries_cont/tsi_value1" "m2m:tsi": { "ty": 30, "pi": "/mnID/CAE5630283216026458665", "ri": "/mnID/TSI840674869203617594", "rn": "tsi_value1", "ct": "20180307T012211", "lt": "20180307T012211", "et": "2n0210307T012211", "dgt": "20180307T123456" "con": "DATA_TACK", "cs": 9, "st": 7 } } } |

#### 6.2.12.2	API-TSI-RET

| API Id | API/TSI/RET/001 API/TSI/RET/001/RCN1 |
| --- | --- |
| API Name | <timeSeriesInstance> resource RETRIEVE with resultContent parameter |
| Target Resource | Requested <timeSeriesInstance> resource |
| Description | The interface is used to send a <timeSeriesInstance> RETRIEVE request attached with resultContent set to 1 to the Registrar CSE, and the hosting CSE sends back a retrieved <timeSeriesInstance> resource information. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | GET /mn-name/ae_sensor/timeSeries_cont/tsi_value1 GET /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=1 |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=30 |
| Example with no RCN or RCN=1 | API/TSI/RET/001 API/TSI/RET/001/RCN1 HTTP Request: GET /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=30 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont/tsi_value1 Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2000 { "m2m:tsi": { "ty": 30, "pi": "/mnID/CAE5630283216026458665", "ri": "/mnID/TSI840674869203617594", "rn": "tsi_value1", "ct": "20180307T012211", "lt": "20180307T012211", "et": "2n0210307T012211", "dgt": "20180307T123456" "con": "DATA_TACK", "cs": 9, "st": 7 } } |

#### 6.2.12.3	API-TSI-UPD

| API Id | API/TSI/UPD |
| --- | --- |
| API Name | <timeSeriesInstance> resource UPDATE |
| Target Resource | Requested <timeSeriesInstance> resource |
| Description | Update operation is not allowed in <timeSeriesInstance> resource |

#### 6.2.12.4	API-TSI-DEL

| API Id | API/TSI/DEL/001/RCN0 API/TSI/DEL/001/RCN1 |
| --- | --- |
| API Name | <timeSeriesInstance> resource DELETE with resultContent parameter |
| Target Resource | Requested <timeSeriesInstance> resource |
| Description | The interface is used to send a <timeSeriesInstance> DELETE request attached with resultContent to the Registrar CSE, and the Registrar CSE creates a <timeSeriesInstance> resource, and sends back a response containing a response status code to indicate the DELETE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | DELETE /mn-name/ae_sensor/timeSeries_cont/tsi_value1 DELETE /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=30 |
| Example with no RCN or RCN=0 | API/TSI/DEL/001 API/TSI/DEL/001/RCN0 HTTP Request: DELETE /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=30 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont/tsi_value1 Content-Type: application/json X-M2M-Origin: /mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2002 |
| Example with RCN=1 | API/TSI/DEL/001/RCN1 HTTP Request: DELETE /mn-name/ae_sensor/timeSeries_cont/tsi_value1?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=30 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/ae_sensor/timeSeries_cont/tsi_value1 Content-Type: application/json X-M2M-Origin:/mnID/CAE5630283216026458665 X-M2M-RI: 1234 X-M2M-RSC: 2002 { "m2m:tsi": { "rn": "tsi_value1", "ty": 30, "ri": "/mnID/TSI840674869203617594", "pi": "/mnID/CAE5630283216026458665", "ct": "20180307T012211", "lt": "20180307T012211" } } |

### 6.2.13 	<accessControlPolicy> Resource

The <accessControlPolicy> resource is defined to contain a set of access control rules defining for which entities have which privilege to perform operations such as CREATE, RETRIEVE, UPDATE, and DELETE. The allowed operations are defined by an attribute accessControlOperations that associated with each <accessControlPolicy> resource. Each resource can be assigned different access rights to different entities by using one or multiple <accessControlPolicy> resources. It can be set by the value of attribute accessControlPolicyID to the resourceID of the <accessControlPolicy> resource.

#### 6.2.12.1	API-ACP-CRE

| API Id | API/ACP/CRE/001 API/ACP/CRE/001/RCN0 API/ACP/CRE/001/RCN1 API/ACP/CRE/001/RCN2 API/ACP/CRE/001/RCN3 |
| --- | --- |
| API Name | <accessControlPolicy> resource CREATE with resultContent parameter |
| Target Resource | <CSEBase> of the requested <accessControlPolicy> resource |
| Description | The interface is used to send a <accessControlPolicy> CREATE request attached with resultContent to the Registrar CSE, and the Registrar CSE creates a <accessControlPolicy> resource, and sends back a response containing a response status code to indicate the CREATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | POST /mn-name POST /mn-name?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=1 |
| Example with RCN=0 | API/ACP/CRE/001/RCN0 HTTP Request: POST /mn-name?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:acp" : { "et" : "20201221T064952", "pv" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "guest1", "guest2" ] } ] }, "pvs" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "all" ] } ] } } HTTP Response: 201 Created Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Example with no RCN or RCN=1 | API/ACP/CRE/001 API/ACP/CRE/001/RCN1 HTTP Request: POST /mn-name?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:acp" : { "et" : "20201221T064952", "pv" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "guest1", "guest2" ] } ] }, "pvs" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "all" ] } ] } } HTTP Response: 201 Created Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:acp": { "rn": "accessControlPolicy", "ty": 1, "ri": "/mnID/ACP503720698362418574", "pi": "/mnID", "ct": "20180308T115922", "lt": "20180308T115922", "et": "20201221T064952", "pv": { "acr": [ { "acco": [], "acop": 63, "acor": [ "guest1", "guest2" ] } ] }, "pvs": { "acr": [ { "acco": [], "acop": 63, "acor": [ "all" ] } ] } } } |
| Example with RCN=2 | API/ACP/CRE/001/RCN2 HTTP Request: POST /mn-name?rcn=2 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:acp" : { "et" : "20201221T064952", "pv" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "guest1", "guest2" ] } ] }, "pvs" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "all" ] } ] } } HTTP Response: 201 Created Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:uri": "/mn-name/accessControlPolicy" } |
| Example with RCN=3 | API/ACP/CRE/001/RCN3 HTTP Request: POST /mn-name?rcn=3 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:acp" : { "et" : "20201221T064952", "pv" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "guest1", "guest2" ] } ] }, "pvs" : { "acr" : [ { "acco" : [], "acop" : 63, "acor" : [ "all" ] } ] } } HTTP Response: 201 Created Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2001 { "m2m:rce": { "uri": "/mn-name/accessControlPolicy" "m2m:acp": { "rn": "accessControlPolicy", "ty": 1, "ri": "/mnID/ACP503720698362418574", "pi": "/mnID", "ct": "20180308T115922", "lt": "20180308T115922", "et": "20201221T064952", "pv": { "acr": [ { "acco": [], "acop": 63, "acor": [ "guest1", "guest2" ] } ] }, "pvs": { "acr": [ { "acco": [], "acop": 63, "acor": [ "all" ] } ] } } } |

#### 6.2.12.2	API-ACP-RET

| API Id | API/ACP/RET/001 API/ACP/RET/001/RCN1 |
| --- | --- |
| API Name | <accessControlPolicy> resource RETRIEVE with resultContent parameter |
| Target Resource | <CSEBase> of the requested <accessControlPolicy> resource |
| Description | The interface is used to send a <accessControlPolicy> RETRIEVE request attached with resultContent set to 1 to the Registrar CSE, and the hosting CSE sends back a retrieved <accessControlPolicy> resource information. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | GET /mn-name/accessControlPolicy GET /mn-name/accessControlPolicy?rcn=1 |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=1 |
| Example with no RCN or RCN=1 | API/ACP/RET/001 API/ACP/RET/001/RCN1 HTTP Request: RET /mn-name/accessControlPolicy?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2000 { "m2m:acp": { "rn": "accessControlPolicy", "ty": 1, "ri": "/mnID/ACP503720698362418574", "pi": "/mnID", "ct": "20180308T115922", "lt": "20180308T115922", "et": "20201221T064952", "pv": { "acr": [ { "acco": [], "acop": 63, "acor": [ "guest1", "guest2" ] } ] }, "pvs": { "acr": [ { "acco": [], "acop": 63, "acor": [ "all" ] } ] } } } |

#### 6.2.12.3	API-ACP-UPD

| API Id | API/ACP/UPD/001 API/ACP/UPD/001/RCN0 API/ACP/UPD/001/RCN1 |
| --- | --- |
| API Name | <accessControlPolicy> resource UPDATE with resultContent parameter |
| Target Resource | <accessControlPolicy> resource |
| Description | The interface is used to send a <accessControlPolicy> UPDATE request attached with resultContent to the Registrar CSE, and the Registrar CSE creates a <accessControlPolicy> resource, and sends back a response containing a response status code to indicate the UPDATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | PUT /mn-name/accessControlPolicy PUT /mn-name/accessControlPolicy?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=1 |
| Example with RCN=0 | API/ACP/UPD/001/RCN0 HTTP Request: PUT /mn-name/accessControlPolicy?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:acp" : { "pv" : { "acr" : [ { "acor" : [ "student_eduA", " student_eduB" ] } ] }, "pvs" : { "acr" : [ { "acor" : [ "student_eduC", "student_eduD" ] } ] } } HTTP Response: 200 OK Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2004 |
| Example with no RCN or RCN=1 | API/ACP/UPD/001 API/ACP/UPD/001/RCN1 HTTP Request: PUT /mn-name/accessControlPolicy?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache { "m2m:acp" : { "pv" : { "acr" : [ { "acor" : [ "student_eduA", "student_eduB" ] } ] }, "pvs" : { "acr" : [ { "acor" : [ "student_eduC", "student_eduD" ] } ] } } HTTP Response: 200 OK Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2004 { "m2m:acp": { "rn": "accessControlPolicy", "ty": 1, "ri": "/mnID/ACP503720698362418574", "pi": "/mnID", "ct": "20180308T115922", "lt": "20180308T115922", "et": "20201221T064952", "pv": { "acr": [ { "acco": [], "acop": 63, "acor": [ "student_eduA", "student_eduB" ] } ] }, "pvs": { "acr": [ { "acco": [], "acop": 63, "acor": [ "student_eduC", "student_eduD" ] } ] } } } |

#### 6.2.12.4	API-ACP-DEL

| API Id | API/ACP/DEL/001 API/ACP/DEL/001/RCN0 API/ACP/DEL/001/RCN1 |
| --- | --- |
| API Name | <accessControlPolicy> resource DELETE with resultContent parameter |
| Target Resource | <accessControlPolicy> resource |
| Description | The interface is used to send a <accessControlPolicy> DELETE request attached with resultContent to the Registrar CSE, and the Registrar CSE creates a <accessControlPolicy> resource, and sends back a response containing a response status code to indicate the DELETE operation status. |
| Resource Structure |  |
| Call Flow |  |
| Resource URL Information | DELETE /mn-name/accessControlPolicy DELETE /mn-name/accessControlPolicy?rcn=<VALUE> |
| HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/vnd.onem2m-res+json;ty=1 |
| Example with no RCN or RCN=0 | API/ACP/DEL/001 API/ACP/DEL/001/RCN0 HTTP Request: DELETE /mn-name/accessControlPolicy?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: C Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2002 |
| Example with RCN=1 | API/ACP/DEL/001/RCN1 HTTP Request: DELETE /mn-name/accessControlPolicy?rcn=1 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: SuperID Content-Type: application/json;ty=1 X-M2M-RI: 1234 Cache-Control: no-cache HTTP Response: 200 OK Content-Location: /mn-name/accessControlPolicy Content-Type: application/json X-M2M-Origin: SuperID X-M2M-RI: 1234 X-M2M-RSC: 2002 { "m2m:acp": { "rn": "accessControlPolicy", "ty": 1, "ri": "/mnID/ACP503720698362418574", "pi": "/mnID", "ct": "20180308T140118", "lt": "20180308T140118", "et": "20201221T064952" } } |

### -----------------------End of new text 1---------------------------------------------

# Text boxes

mn-name

ae_actuator (AE)

group_lamp

AE Registree

group create request

Response

mn-name

mn-name

ae_actuator (AE)

group_lamp

AE Registree

group retrieve request

Response

mn-name

mn-name

ae_actuator (AE)

group_lamp

AE Registree

group update request

Response

mn-name

mn-name

ae_actuator (AE)

group_lamp

AE Registree

group delete request

Response

mn-name

mn-name

ae_sensor (AE)

timeSeries_cont

(container)

AE Registree

timeSeries create request

Response

mn-name

mn-name

ae_sensor (AE)

timeSeries_cont

(container)

AE Registree

timeSeries retrieve request

Response

mn-name

mn-name

ae_sensor (AE)

timeSeries_cont

(container)

AE Registree

timeSeries update request

Response

mn-name

mn-name

ae_sensor (AE)

timeSeries_cont

(container)

AE Registree

timeSeries delete request

Response

mn-name

mn-name

ae_sensor (AE)

timeSeries_cont

(container)

tsi_value1

(timeSeriesInstance)

tsi_value2

(timeSeriesInstance)

AE Registree

timeSeriesInstance create request

Response

mn-name

mn-name

ae_sensor (AE)

timeSeries_cont

(container)

tsi_value1

(timeSeriesInstance)

tsi_value2

(timeSeriesInstance)

AE Registree

timeSeriesInstance retrieve request

Response

mn-name

mn-name

ae_sensor (AE)

timeSeries_cont

(container)

tsi_value1

(timeSeriesInstance)

tsi_value2

(timeSeriesInstance)

AE Registree

timeSeriesInstance delete request

Response

mn-name

mn-name

ae_sensor (AE)

accessControlPolicy

originator

accessControlPolicy create request

Response

mn-name

mn-name

ae_sensor (AE)

accessControlPolicy

originator

accessControlPolicy retrieve request

Response

mn-name

mn-name

ae_sensor (AE)

accessControlPolicy

originator

accessControlPolicy update request

Response

mn-name

mn-name

ae_sensor (AE)

accessControlPolicy

originator

accessControlPolicy delete request

Response

mn-name