| Work Item |
| --- |
| Work Item Title:* | Conformance Test Specifications Release 3 v1.0.0 |
| Document Number* | WI-00xx |
| Supporting Members or Partner type 2* | KETI, TTA, Convida Wireless, Sensinov, Spirent, NTT |
| Date:* | 2018-03-21 |
| Abstract:* | The WI defines conformance test specifications for oneM2M Release 3. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

1	Title (Acronym)

Conformance Test Specifications Release 3

2	Justification

The present Work Item proposes to update the series of Conformance test specifications TS-0017 (PICS), TS-0018 (TSS&TP) and TS-0019 (ATS & PIXIT) to match the requirements of the Release 3 versions of TS-0001 and TS-0004.

It is also intended to add new tests in order to address the new resources, features and fucntions specified in the Release 3.

3	Intended Output

| Tick all the appropriate cases |  |
| --- | --- |
|  | Change request(s) to existing Technical Specification(s) |
|  | Change request(s) to existing Technical Reports(s) |
| √ | New Normative Technical Specifications(s) |
|  | New Permanent Technical Reports(s) |
|  | New Temporary Technical Reports(s) |

- Impact

###### Impact on other Technical Specifications and Technical Reports

Possible impact on TS-0017, TS-0018 and TS-0019 for Release 2 (WI-0074: conformance test)

###### Impact on other oneM2M Work Items

None expected

5	Scope

The scope of the WI includes identification of the functions and features needed to be tested:

TS-0017 – Implementation Conformance Statements

-	Check list for the ICS.

TS-0018 – Test Suite Structure and Test Purposes

-	Organize the functions and features that need to be tested into test suites.

-	Specify test purposes and test descriptions for conformance test.

-	Define test cases.

TS-0019 – Abstract Test Suite and Implementation eXtra Information for Test

-	Definition of the Abstract Protocol Tester (APT)

-	Definition of TTCN-3 test architecture

-	Development of TTCN-3 test suite, e.g. naming conventions, code documentation, test case structure.

-	IXIT proforma.

6	Schedule and impacted specifications

Provides the schedule of tasks to be performed;

| New Specifications (if any) |
| --- |
| Document Type | Document Number* | Title | Schedule (TP No.) | Lead WG | Impacted WGs | Comments |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |  |
| TS | 0017 | Implementation Conformance Statements | TP35 | TP39 | TP40 | TP41 | TST | None | Rapporteur: In Song Lee & Miguel Angel Reina Ortega |
| TS | 0018 | Test Suite Structure and Test Purposes | TP35 | TP39 | TP40 | TP41 | TST | None | Rapporteur: In Song Lee & Miguel Angel Reina Ortega |
| TS | 0019 | Abstract Test Suite and Implementation eXtra Information for Test | TP35 | TP39 | TP40 | TP41 | TST | None | Rapporteur : Miguel Angel Reina Ortega |

7	Work Item Rapporteur(s)

Miguel Angel Reina Ortega (ETSI)

8	History

| Document history |
| --- |
| V1.0.0 | 21 March 2018 | Initial draft for WI |
|  |  | Uploaded as a permanent document following approval of TP-2018-xxxx |

-------------------------------