| Input Contribution |
| --- |
| Meeting ID* | TST34 |
| Title:* | TR-0051-contentInstance resource API |
| Source:* | Laurent Velez, ETSI, laurent.velez@etsi.org Khalil Drira, LAAS-CNRS, drira@laas.fr Mahdi Ben Alaya, Sensinov, benalaya@sensinov.com |
| Date:* | 2018-04-06 |
| Input related to* | TR-0051 API Guide |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | To agree contribution to be implemented in TR-0051 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes add the clause 6.2.6 related the <contentInstance> resource API for CREATE, RETRIEVE and DELETE.

================= start of input   =============================

### 6.2.6 	<contentInstance> Resource

#### 6.2.6.0	Introduction

The <contentInstance> resource represents a data instance stored in the <container> resource. Taking a temperature sensor device as an example, the temperature sensor is designed to collect temperature data of environment and in this case, the real temperature data is modelled as a <contentInstance> resource. In details, we assume both the temperature sensor is registered with <AE> resource and a <container> resource is created under the <AE> to store temperature instances, under this consumption, whenever the temperature data is uploaded into a central server, the temperature data has to be denoted as a value of content attribute of <contentInstance> resource.

The <contentInstance> resource cannot be modified once created, and is able to be deleted explicitly by an AE or may be deleted by the platform based on specific policies. If the platform has policies to manage the <contentInstance> resource, these policies are represented by attributes axByteSize, maxNrOfInstances and/or maxInstanceAge attributes in their parent <container> resource.

The <contentInstance> resource inheritances the same access control policies of its parent <container> resource, and does not have its own accessControlPolicyIDs attribute.

#### 6.2.6.1	API-CI-CRE

| API Id | API/CI/CRE/001 API/CI/CRE/001_RCN0 API/CI/CRE/001_RCN/1 API/CI/CRE/001_RCN2 API/CI/CRE/001_RCN3 |
| --- | --- |
| API Name | contentInstance CREATE with or without resultContent parameter |
| Target Resource | The <container> resource as a parent resource of being created <contentInstance> resource |
| Description | The interface is used to send a <contentInstance> CREATE request to the target <container> resource located under the CSE, and the hosting CSE will create a new <contentInstance> under the requested <container>, and send back a response containing only the reponse status code to indicate the CREATE operation status. |
| Resource Structure |  |
| Call Flow |  |
| HTTP Header Information | Header Value X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/json; ty=4 |
| Example with No RCN or RCN=1 | API/CI/CRE/001 API/CI/CRE/001_RCN1 HTTP Request: POST /mn-name/ae_sensor/cont_temp HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Length:258 Content-Location:/mnID/cin20180406T1355091405855351047683_cse01 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T135509", "et": "99991231T235959", "lt": "20180406T135509", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1355091405855351047683_cse01", "rn": "cin20180406T1355091405855351047682_cse01", "st": 1, "ty": 4 } } |
| Example with rcn=0 | API/CI/CRE/001_RCN/0 HTTP Request: POST /mn-name/ae_sensor/cont_temp?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Length:0 Content-Location:/mnID/cin20180406T1358251405855267120642_cse01 X-M2M-RI:1234 X-M2M-RSC:2001 |
| Example with RCN=2 | API/CI/CRE/001_RCN2 HTTP Request: POST /mn-name/ae_sensor/cont_temp?rcn=2 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Length:91 Content-Location:/mnID/cin20180406T1400131405855099266562_cse01 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:uri": "mn-name/ae_sensor/cont_temp/cin20180406T1400131405855099266561_cse01" } |
| Example with RCN=3 | API/CI/CRE/001_RCN3 HTTP Request: POST /mn-name/ae_sensor/cont_temp?rcn=3 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 Content-Type: application/json;ty=4 X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Length:356 Content-Location:/mnID/cin20180406T1402131405855770682883_cse01 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2001 { "m2m:rce": { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T140213", "et": "99991231T235959", "lt": "20180406T140213", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1402131405855770682883_cse01", "rn": "cin20180406T1402131405855770682882_cse01", "st": 4, "ty": 4 }, "uri": "mn-name/ae_sensor/cont_temp/cin20180406T1402131405855770682882_cse01" } } |

#### 6.2.6.2	API-CI-RET

| API Id | API/CI/RET/001_LA API/CI/RET/001_OL API/CI/RET/001_CI |
| --- | --- |
| API Name | Latest , Oldest or specific contentInstance RETRIEVE |
| Target Resource | <latest> , <oldest> virtual resources or individual <contentInstance> resource of the requested <container> resource |
| Description | The interface is used to send a <contentInstance> RETRIEVE request to the CSE, and the hosting CSE will send back a response containing the result. |
| Resource Structure |  |
| Call Flow |  |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/json |
| Example with latest | API/CI/RET/001_LA HTTP Request: GET /mn-name/ae_sensor/cont_temp/la HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:258 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2000 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T140213", "et": "99991231T235959", "lt": "20180406T140213", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1402131405855770682883_cse01", "rn": "cin20180406T1402131405855770682882_cse01", "st": 4, "ty": 4 } } |
| Example with oldest | API/CI/RET/001_OL HTTP Request: GET /mn-name/ae_sensor/cont_temp/ol HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:258 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2000 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T135509", "et": "99991231T235959", "lt": "20180406T135509", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1355091405855351047683_cse01", "rn": "cin20180406T1355091405855351047682_cse01", "st": 1, "ty": 4 } } |
| Example with CI name | API/CI/RET/001_CI HTTP Request: GET /mn-name/ae_sensor/cont_temp/cin20180406T1400131405855099266561_cse01 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:258 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2000 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T140013", "et": "99991231T235959", "lt": "20180406T140013", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1400131405855099266562_cse01", "rn": "cin20180406T1400131405855099266561_cse01", "st": 3, "ty": 4 } } |

#### 6.2.6.3	API-CI-DEL

| API Id | API/CI/DEL/001_LA API/CI/DEL/001_LA_RCN0 API/CI/DEL/001_OL API/CI/DEL/001_OL_RCN0 API/CI/DEL/001_CI API/CI/DEL/001_CI_RCN0 |
| --- | --- |
| API Name | Latest , Oldest or specific contentInstance DELETE |
| Target Resource | <latest> , <oldest> virtual resources or individual <contentInstance> resource of the requested <container> resource |
| Description | The interface is used to send a <container> DELETE request to the CSE, and the hosting CSE will delete the <contentInstance>, and send back a response containing the response status code to indicate the status of the DELETE operation. |
| Resource Structure |  |
| Call Flow |  |
| HTTP Header Information | Header Value X-M2M-RI Request ID X-M2M-Origin AE-ID of request originator Content-Type application/json |
| Example with latest (No RCN or RCN=1) | API/CI/DEL/001_LA HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/la HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:258 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2002 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T140213", "et": "99991231T235959", "lt": "20180406T140213", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1402131405855770682883_cse01", "rn": "cin20180406T1402131405855770682882_cse01", "st": 4, "ty": 4 } } |
| Example with latest and RCN=0 | API/CI/DEL/001_LA_RCN0 HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/la?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:0 X-M2M-RI:1234 X-M2M-RSC:2002 |
| Example with oldest (No RCN or RCN=1) | API/CI/DEL/001_OL HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/ol HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:258 Content-Type:application/json X-M2M-RI:1234 X-M2M-RSC:2002 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T135509", "et": "99991231T235959", "lt": "20180406T135509", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1355091405855351047683_cse01", "rn": "cin20180406T1355091405855351047682_cse01", "st": 1, "ty": 4 } } |
| Example with oldest and RCN=0 | API/CI/DEL/001_OL_RCN0 HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/ol?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:0 X-M2M-RI:1234 X-M2M-RSC:2002 |
| Example with CI name (No RCN or RCN=1) | API/CI/DEL/001_CI HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/cin20180406T1400131405855099266561_cse01 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK X-M2M-Origin:/mnID X-M2M-RI:1234 X-M2M-RSC:2002 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T143434", "et": "99991231T235959", "lt": "20180406T143434", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1434341405855518901762_cse01", "rn": "cin20180406T1434341405855518901761_cse01", "st": 9, "ty": 4 } } |
| Example with CI name and RCN=0 | API/CI/DEL/001_CI_RCN0 HTTP Request: DELETE /mn-name/ae_sensor/cont_temp/cin20180406T1400131405855099266561_cse01?rcn=0 HTTP/1.1 Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: 200 OK Content-Length:0 X-M2M-RI:1234 X-M2M-RSC:2002 |

================= end of input   =============================