| Input Contribution |
| --- |
| Meeting ID* | TST35 |
| Title:* | TS-0017-new ICS for 3GPP Interworking and timeSeries |
| Source:* | In Song Lee, KETI, insong@keti.re.kr NakMyoung Sung, KETI, nmsung@keti.re.kr |
| Date:* | 2018-05-22 |
| Input related to* | TS-0017 V2.0.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution is wrote to input new PICS reference for TS-0018.

In TST34, there were contributions for new test cases, such as <timeSeries> resource, 3GPP Interworking etc.

Functions for new test cases are written as follow:

New text 1 is about 3GPP network interworking.

New text 2 is including optional attribute of <timeSeries> and <timeSeiresInstance> resources.

In the TS-0026, 3GPP IoT Features are specified in clause 5.3.

Some parts are excluded as following reasons,

Cluase 1 and 7. Both part are changing or setting configuration, and not about features.

Cluase 2, 3 and 6. are not defined, since these features are not supported in this release of the document.

Cluase 8. Mobile Core Network Issue Reports is also excluded, because it is not about feature.

Rest features, marked as yellow colour, are used.

As per TS-0026:

## 5.3	3GPP Cellular IoT Features and Services

The SCEF exposes the following services to the IN-CSE.  This document describes how the IN-CSE may access each service.

  - Configuring Communication Patterns, see clause 7.6.

  - Configuring Session QoS, see clause 7.9.

  - Configuring Session Sponsorship, see clause 711.

  - Background Data Transfer, see clause 7.10.

  - Monitoring, see clause 7.4.

  - High Latency Communication – Extended S-GW and SCEF Buffering, see clause 7.3.

  - High Latency Communication – Configuring PSM and eDRX, see clause 7.12.

  - Mobile Core Network Issue Reports, see clause 7.8.

  - SMS Based Device Triggering, see clause 7.5.

  - Group Messaging (via MBMS), see clause 7.7.

  - Non-IP Data Delivery, see clause 7.1.

### -----------------------Start of new text 1-------------------------------------------

### A.5.5.1 3GPP Network Interworking

This section presents a group of functionality supporting 3GPP interworking and 3GPP CIoT features.

Table A.5.5.1.1: functions for 3GPP Interworking

| Item | Profile Identifier | Reference | Condition | Support |
| --- | --- | --- | --- | --- |
| 1 | Non-IP Data Delivery | [8] 7.1 | C.1 | O Yes O No |
| 2 | UE Reachability Monitoring | [8] 7.4.1 | C.1 | O Yes O No |
| 3 | Device Triggering | [8] 7.5 | C.1 | O Yes O No |
| 4 | Group Message Delivery | [8] 7.7 | C.1 | O Yes O No |
| 5 | Background Data Transfer | [8] 7.10 | C.1 | O Yes O No |

C.1: Optional to support one or more than one of the above listed functions per testing session.

### -----------------------End of new text 1---------------------------------------------

### -----------------------Start of new text 2-------------------------------------------

Table A.5.7.9: Optional Attributes of <timeSeries> resource

| Item | Resource Type | Reference | Condition | Support |
| --- | --- | --- | --- | --- |
| 1 | accessControlPolicyIDs | [1] 9.6.36 | C.1 | O Yes O No |
| 2 | labels | [1] 9.6.36 | C.1 | O Yes O No |
| 3 | announceTo | [1] 9.6.36 | C.1 | O Yes O No |
| 4 | announcedAttribute | [1] 9.6.36 | C.1 | O Yes O No |
| 5 | dynamicAuthorizationConsultationIDs | [1] 9.6.36 | C.1 | O Yes O No |
| 6 | maxNrOfInstances | [1] 9.6.36 | C.1 | O Yes O No |
| 7 | maxByteSize | [1] 9.6.36 | C.1 | O Yes O No |
| 8 | maxInstanceAge | [1] 9.6.36 | C.1 | O Yes O No |
| 9 | periodicInterval | [1] 9.6.36 | C.1 | O Yes O No |
| 10 | missingDataDetect | [1] 9.6.36 | C.1 | O Yes O No |
| 11 | ontologyRef | [1] 9.6.36 | C.1 | O Yes O No |
| 12 | missingDataMaxNr | [1] 9.6.36 | C.1 | O Yes O No |
| 13 | missingDataList | [1] 9.6.36 | C.1 | O Yes O No |
| 14 | missingDataCurrentNr | [1] 9.6.36 | C.1 | O Yes O No |
| 15 | missingDataDetectTimer | [1] 9.6.36 | C.1 | O Yes O No |

C.1: The IUT shall be explicitly declared to one or more than one of the above listed resource types per testing session.

Table A.5.7.10: Optional Attributes of <timeSeriesInstance> resource

| Item | Resource Type | Reference | Condition | Support |
| --- | --- | --- | --- | --- |
| 1 | labels | [1] 9.6.37 | C.1 | O Yes O No |
| 2 | announceTo | [1] 9.6.37 | C.1 | O Yes O No |
| 3 | announcedAttribute | [1] 9.6.37 | C.1 | O Yes O No |
| 4 | sequenceNr | [1] 9.6.37 | C.1 | O Yes O No |

C.1: The IUT shall be explicitly declared to one or more than one of the above listed resource types per testing session.

### -----------------------End of new text 2---------------------------------------------