| Input Contribution |
| --- |
| Meeting ID* | TST36 |
| Title:* | TR-0051_example of notification |
| Source:* | In Song Lee, KETI, insong@keti.re.kr Il Yeup Ahn, KETI, iyahn@keti.re.kr |
| Date:* | 2018-07-16 |
| Input related to* | TR-0051 V0.1.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution is written to add notification use case in TR-0051 and contains below clauses.

A.1.0 Introduction

A.1.1 API-NOTI-NET1

A.1.2 API-NOTI-NET2

A.1.3 API-NOTI-NET3

A.1.4 API-NOTI-NET4

Notifcation shall be sent in many different situation, but examples only focus on the notificationEventType. Other examples may be added.

### -----------------------Start of new text 1-------------------------------------------

Annex A (informative):
Example of notification

## A.1.0	Introduction

The notify operation shall be used for notify any event. AE or CSE which has privilege shall make a <subscription> resource as a child resource of the subscribed-to resource. The <subscription> resource includes notification policies that specify which, when, and how notifications are sent.

In this clause, notification examples are provided for the understanding of notification procedure. Especially, examples have different notificationEnentType in the eventNotificationCriteria. The notificationEventType value is specified in the Table 6.2.14-1 and set when notification shall be sent.

Table 6.2.14-1: Interpretation of notificationEventType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Update_of_Resource | Default |
| 2 | Delete_of_Resource |  |
| 3 | Create_of_Direct_Child_Resource |  |
| 4 | Delete_of_Direct_Child_Resource |  |

### A.1.1	API-NOTI-NET1

| API Id | API/NOTI/NET1/STEP01 API/NOTI/NET1/STEP02 API/NOTI/NET1/STEP03 |
| --- | --- |
| API Name | Notification procedure when the <subscription> resource has notificationEventType set to 1(Hosting CSE sends notification when the subscribed-to resource has been updated) |
| Target Resource | Update Target: Requested <container> resource Notification Target: originator |
| Description | Figure below depicts the procedure for notification. Initial condition: MN(Hosting CSE) has a <container> resource. The originator is AE1 in this clause, but can be CSE. Step 01: The originator sends a <subscription> resource CREATE request to the <container> resource on the Registrar CSE. In the request, notificationEventType set to 1 and notificationURI attribute set to originator. The Registrar CSE creates a <subscription> resource and sends back a response. Step 02: An AE2 sends an UPDATE request to the <container> resource. The Registrar CSE updates a <container> resource and sends back a response. Step 03: The Hosting CSE sends notification as soon as update succeed. The originator sends back an ACK message. |
| Step 01 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json;ty=23 |
|  | Example | API/NOTI/NET1/STEP01 HTTP Request: POST /mn-name/cont_temp? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=23 X-M2M-RI: 1234 { "m2m:sub": { "enc": { "net": [1] }, "nu": ["AE1"], "rn": "cont_sub" } } HTTP Response: 201 Created Content-Location: mn-name/cont_temp Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Step 02 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET1/STEP02 HTTP Request: PUT /mn-name/cont_temp? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T08463114 Content-Type: application/json; X-M2M-RI: 1234 { "m2m:cnt": { "mni": "300" } } HTTP Response: 200 OK Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2004 { "m2m:cnt": { "cbs": 10, "cni": 0, "ct": "20180406T125807", "et": "99991231T235959", "lbl": [ "indoor_temp" ], "lt": "20180406T130109", "mbs": 60000000, "mia": 1600, "mni": 300, "pi": "CAE0120180406T0846311405855351047680_cse01", "ri": "cnt20180406T1258071405855183193603_cse01", "rn": "cont_temp", "st": 1, "ty": 3 } } |
| Step 03 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET1/STEP03 HTTP Request: POST HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: mn-name Content-Type: application/json; X-M2M-RI: 1234 { "m2m:sgn": { "sur": " mn-name/cont_temp/cont_sub", "nev": { "net":1, "rep": { "m2m:cnt": { "cbs": 10, "cni": 0, "ct": "20180406T125807", "et": "99991231T235959", "lbl": [ "indoor_temp" ], "lt": "20180406T130109", "mbs": 60000000, "mia": 1600, "mni": 300, "pi": "CAE0120180406T0846311405855351047680_cse01", "ri": "cnt20180406T1258071405855183193603_cse01", "rn": "cont_temp", "st": 1, "ty": 3 } } } } } HTTP Response: 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2000 |

### A.1.2	API-NOTI-NET2

| API Id | API/NOTI/NET2/STEP01 API/NOTI/NET2/STEP02 API/NOTI/NET2/STEP03 |
| --- | --- |
| API Name | Notification procedure when the <subscription> resource has notificationEventType set to 2(Hosting CSE sends notification when the subscribed to resource has been deleted) |
| Target Resource | Delete Target: Requested <container> resource Notification Target: originator |
| Description | Figure below depicts the procedure for notification. Initial condition: MN(Hosting CSE) has a <container> resource. The originator is AE1 in this clause, but can be CSE. Step 01: The originator sends a <subscription> resource CREATE request to the <container> resource on the Registrar CSE. In the request, notificationEventType set to 2 and notificationURI attribute set to originator. The Registrar CSE creates a <subscription> resource and sends back a response. Step 02: An AE2 sends a DELETE request to the <container> resource. The Registrar CSE deletes a <container> resource and sends back a response. Step 03: The Hosting CSE sends notification as soon as delete succeed. The originator sends back an ACK message. |
| Step 01 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json;ty=23 |
|  | Example | API/NOTI/NET2/STEP01 HTTP Request: POST /mn-name/cont_temp? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=23 X-M2M-RI: 1234 { "m2m:sub": { "enc": { "net": [2] }, "nu": ["AE1"], "rn": "cont_sub" } } HTTP Response: 201 Created Content-Location: mn-name/cont_temp Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Step 02 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET2/STEP02 HTTP Request: DELETE /mn-name/cont_temp? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T08463114 Content-Type: application/json; X-M2M-RI: 1234 HTTP Response: 200 OK Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2004 { "m2m:cnt": { "cbs": 10, "cni": 0, "ct": "20180406T125807", "et": "99991231T235959", "lbl": [ "indoor_temp" ], "lt": "20180406T130109", "mbs": 60000000, "mia": 1600, "mni": 300, "pi": "CAE0120180406T0846311405855351047680_cse01", "ri": "cnt20180406T1258071405855183193603_cse01", "rn": "cont_temp", "st": 1, "ty": 3 } } |
| Step 03 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET2/STEP03 HTTP Request: POST HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: mn-name Content-Type: application/json; X-M2M-RI: 1234 { "m2m:sgn": { "sur": " mn-name/cont_temp/cont_sub", "nev": { "net":2, "rep": { "m2m:cnt": { "cbs": 10, "cni": 0, "ct": "20180406T125807", "et": "99991231T235959", "lbl": [ "indoor_temp" ], "lt": "20180406T130109", "mbs": 60000000, "mia": 1600, "mni": 300, "pi": "CAE0120180406T0846311405855351047680_cse01", "ri": "cnt20180406T1258071405855183193603_cse01", "rn": "cont_temp", "st": 1, "ty": 3 } } } } } HTTP Response: 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2000 |

### A.1.3	API-NOTI-NET3

| API Id | API/NOTI/NET3/STEP01 API/NOTI/NET3/STEP02 API/NOTI/NET3/STEP03 |
| --- | --- |
| API Name | Notification procedure when the <subscription> resource has notificationEventType set to 3(Hosting CSE sends notification when the direct child resource has been created) |
| Target Resource | Create <contentIntance> target: Requested <container> resource Notification Target: originator |
| Description | Figure below depicts the procedure for notification. Initial condition: MN(Hosting CSE) has a <container> resource. The originator is AE1 in this clause, but can be CSE. Step 01: The originator sends a <subscription> resource CREATE request to the <container> resource on the Registrar CSE. In the request, notificationEventType set to 3 and notificationURI attribute set to originator. The Registrar CSE creates a <subscription> resource and sends back a response. Step 02: An AE2 sends a CREATE request of the <contentInstance> resource to the <container> resource. The Registrar CSE creates a <contentInstance> resource and sends back a response. Step 03: The Hosting CSE sends notification as soon as create succeed. The originator sends back an ACK message. |
| Step 01 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json;ty=23 |
|  | Example | API/NOTI/NET3/STEP01 HTTP Request: POST /mn-name/cont_temp? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=23 X-M2M-RI: 1234 { "m2m:sub": { "enc": { "net": [3] }, "nu": ["AE1"], "rn": "cont_sub" } } HTTP Response: 201 Created Content-Location: mn-name/cont_temp Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Step 02 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET3/STEP02 HTTP Request: POST /mn-name/cont_temp? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T08463114 Content-Type: application/json; X-M2M-RI: 1234 { "m2m:cin": { "con": "20" } } HTTP Response: 201 Created Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2004 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T135509", "et": "99991231T235959", "lt": "20180406T135509", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1355091405855351047683_cse01", "rn": "cin20180406T1355091405855351047682_cse01", "st": 1, "ty": 4 } } |
| Step 03 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET3/STEP03 HTTP Request: POST HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: mn-name Content-Type: application/json; X-M2M-RI: 1234 { "m2m:sgn": { "sur": " mn-name/cont_temp/cont_sub", "nev": { "net":3, "rep": { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T135509", "et": "99991231T235959", "lt": "20180406T135509", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1355091405855351047683_cse01", "rn": "cin20180406T1355091405855351047682_cse01", "st": 1, "ty": 4 } } } } } HTTP Response: 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2000 |

### A.1.4	API-NOTI-NET4

| API Id | API/NOTI/NET4/STEP01 API/NOTI/NET4/STEP02 API/NOTI/NET4/STEP03 |
| --- | --- |
| API Name | Notification procedure when the <subscription> resource has notificationEventType set to 4(Hosting CSE sends notification when the direct child resource has been deleted) |
| Target Resource | Delete <contentIntance> target: Requested <container> resource Notification Target: originator |
| Description | Figure below depicts the procedure for notification. Initial condition: MN(Hosting CSE) has a <container> resource. At the same time, <container> resource has <contentInstance> resource as a direct child resource. The originator is AE1 in this clause, but can be CSE. Step 01: The originator sends a <subscription> resource CREATE request to the <container> resource on the Registrar CSE. In the request, notificationEventType set to 4 and notificationURI attribute set to originator. The Registrar CSE creates a <subscription> resource and sends back a response. Step 02: An AE2 sends a DELETE request of the <contentInstance> resource to the <container> resource. The Registrar CSE deletes a <contentInstance> resource and sends back a response. Step 03: The Hosting CSE sends notification as soon as delete succeed. The originator sends back an ACK message. |

| Step 01 | Resource Structure before Sending Request |  |
| --- | --- | --- |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json;ty=23 |
|  | Example | API/NOTI/NET4/STEP01 HTTP Request: POST /mn-name/cont_temp? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE5630283216026458665 Content-Type: application/json;ty=23 X-M2M-RI: 1234 { "m2m:sub": { "enc": { "net": [4] }, "nu": ["AE1"], "rn": "cont_sub" } } HTTP Response: 201 Created Content-Location: mn-name/cont_temp Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2001 |
| Step 02 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET4/STEP02 HTTP Request: DELETE /mn-name/cont_temp/ci_temp_value1? HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: CAE0120180406T08463114 Content-Type: application/json; X-M2M-RI: 1234 HTTP Response: 200 OK Content-Type: application/json X-M2M-RI: 1234 X-M2M-RSC: 2004 { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T135509", "et": "99991231T235959", "lt": "20180406T135509", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1355091405855351047683_cse01", "rn": "cin20180406T1355091405855351047682_cse01", "st": 1, "ty": 4 } } |
| Step 03 | Resource Structure before Sending Request |  |
|  | Call Flow |  |
|  | HTTP Header Information | Header Value Accept application/json X-M2M-RI Request ID X-M2M-Origin AE-ID of Originator Content-Type application/json; |
|  | Example | API/NOTI/NET4/STEP03 HTTP Request: POST HTTP/1.1 Accept: application/json Host: 192.168.0.10:8282 X-M2M-Origin: mn-name Content-Type: application/json; X-M2M-RI: 1234 { "m2m:sgn": { "sur": " mn-name/cont_temp/cont_sub", "nev": { "net":4, "rep": { "m2m:cin": { "con": "20", "cs": 2, "ct": "20180406T135509", "et": "99991231T235959", "lt": "20180406T135509", "pi": "cnt20180406T1353041405855518901760_cse01", "ri": "cin20180406T1355091405855351047683_cse01", "rn": "cin20180406T1355091405855351047682_cse01", "st": 1, "ty": 4 } } } } } HTTP Response: 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2000 |

### -----------------------End of new text 1---------------------------------------------

# Text boxes

originator

(AE1)

subscription create request to the container

Response

mn-name

AE2

container resource update request

Response

Notification send

ACK

Step 01

Step 02

Step 03

mn-name

(CSEBase)

cont_temp

(container)

originator

(AE)

originator

(AE1)

subscription create request

Response

mn-name

mn-name

(CSEBase)

cont_temp

(container)

cont_sub

(subscription)

mn-name

container update request

Response

AE2

mn-name

(CSEBase)

cont_temp

(container)

cont_sub

(subscription)

AE1

Notification send

ACK

mn-name

originator

(AE1)

subscription create request to the container

Response

mn-name

AE2

container resource delete request

Response

Notification send

ACK

Step 01

Step 02

Step 03

mn-name

(CSEBase)

cont_temp

(container)

originator

(AE)

originator

(AE1)

subscription create request

Response

mn-name

mn-name

(CSEBase)

cont_temp

(container)

cont_sub

(subscription)

mn-name

container delete request

Response

AE2

mn-name

(CSEBase)

AE1

Notification send

ACK

mn-name

originator

(AE1)

subscription create request to the container

Response

mn-name

AE2

contentInstance create request

Response

Notification send

ACK

Step 01

Step 02

Step 03

mn-name

(CSEBase)

cont_temp

(container)

originator

(AE)

originator

(AE1)

subscription create request

Response

mn-name

mn-name

(CSEBase)

cont_temp

(container)

cont_sub

(subscription)

mn-name

contentInstance create request

Response

AE2

mn-name

(CSEBase)

cont_temp

(container)

ci_temp_value1

(contentInstance)

cont_sub

(subscription)

AE1

Notification send

ACK

mn-name

originator

(AE1)

subscription create request to the container

Response

mn-name

AE2

contentInstance delete request

Response

Notification send

ACK

Step 01

Step 02

Step 03

mn-name

(CSEBase)

cont_temp

(container)

ci_temp_value1

(contentInstance)

originator

(AE1)

subscription create request

Response

mn-name

mn-name

(CSEBase)

cont_temp

(container)

ci_temp_value1

(contentInstance)

cont_sub

(subscription)

mn-name

contentInstance delete request

Response

AE2

mn-name

(CSEBase)

cont_temp

(container)

cont_sub

(subscription)

AE1

Notification send

ACK

mn-name