| Input Contribution |
| --- |
| Meeting ID* | TST36.1 |
| Title:* | TR-0051-remoteCSE resource API |
| Source:* | Laurent Velez, ETSI, laurent.velez@etsi.org |
| k | 2018-08-01 |
| Input related to* | TR-0051 API Guide |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | To agree contribution to be implemented in TR-0051 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes add the clause 6.2.3 related to the <remoteCSE> resource API for  operations.

================= start of input   =============================

#### 6.2.3	Resource Type remoteCSE

#### 6.2.3.0	Introduction

The <remoteCSE> resource represents a Registree CSE that is registered into a Registrar CSE, and <remoteCSE> locates directly under the <CSEBase> of the Registrar CSE. Similarly, one <remoteCSE> resource will also be created under the <CSEBase> of the Registree CSE to represent the Registrar CSE when the Registree CSE is successfully registered into the Registrar CSE.

#### 6.2.3.1	API-CSR-CRE

| API Id | API/CSR/CRE/001 API/CSR/CRE/001_RCN/1 API/CSR/CRE/001_RCN/2 API/CSR/CRE/001_RCN/3 API/CSR/CRE/001_RCN/4 |
| --- | --- |
| API Name | remoteCSE CREATE with or without resultContent parameter |
| Target Resource | <remoteCSE> resource |
| Description | The interface is used to send a <remoteCSE> resource CREATE request to CSE, and receive response from the CSE. The CREATE request is initialized with an associated result content (RCN) parameter to in order to get preferred response from the CSE as following: When resultContent is set to 0 (zero): The response contains the response status code ONLY with no information of the created <remoteCSE> resource. When resultContent is set to 1 (one): The response contains a response status code as well as the <remoteCSE> resource information (attributes) that represents the registree (MN-CSE). When resultContent is set to 2 (two): The response contains a response status code as well as the hierarchical address of the created <remoteCSE> resource information. When resultContent is set to 3 (three): The response contains a response status code, the hierarchical address, and attributes of the created <remotecSE> resource that represent the Registree CSE (MN-CSE). |
| Resource Structure |  |
| Call Flow |  |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin Entity ID of request originator Content-Type application/json;ty=16 |
| Example with RCN=1 or No RCN | API/CSR/CRE/001 API/CSR/CRE/001_RCN1 HTTP Request: GET /cse-name?rcn=1 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: HTTP/1.1 201 Created X-M2M-RI: 1234 X-M2M-RSC: 2001 Content-Length:227 Content-Type:application/json Content-Location: /cseID/cse2ID { "m2m:csr": { "cb": "//192.168.56.102:8282/cse-name2", "csi": "/cse2ID", "ct": "20180801T091626", "et": "99991231T235959", "lt": "20180801T091626", "pi": "cseID", "poa": [ "http://192.168.56.2:8282" ], "ri": "cse2ID", "rn": "cse-name2", "rr": true, "ty": 16 } } |
| Example with RCN=0 | API/CSR/CRE/001_RCN0 HTTP Request: GET /cse-name?rcn=0 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: HTTP/1.1 201 Created X-M2M-RI: 1234 X-M2M-RSC: 2001 Content-Length:0 Content-Type:application/json Content-Location: /cseID/cse2ID |
| Example with RCN=2 | API/CSR/CRE/001_RCN2 HTTP Request: GET /cse-name?rcn=2 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: HTTP/1.1 201 Created X-M2M-RI: 1234 X-M2M-RSC: 2001 Content-Length:30 Content-Type:application/json Content-Location: /cseID/cse2ID {"m2m:uri":"cse-name/cse-name2"} |
| Example with RCN=3 | API/CSR/CRE/001_RCN3 HTTP Request: GET /cse-name?rcn=3 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: HTTP/1.1 201 Created X-M2M-RI: 1234 X-M2M-RSC: 2001 Content-Length:264 Content-Type:application/json Content-Location: /cseID/cse2ID { "m2m:rce": { "m2m:csr": { "cb": "//192.168.56.2:8282/cse-name2", "csi": "/cse2ID", "ct": "20180801T093501", "et": "99991231T235959", "lt": "20180801T093501", "pi": "cseID", "poa": [ "http://192.168.56.2:8282" ], "ri": "cse2ID", "rn": "cse-name2", "rr": true, "ty": 16 }, "uri": "cse-name/cse-name2" } } |

#### 6.2.3.2	API-CSR-RET

| API Id | API/CSR/RET/001 API/CSR/RET/001_RCN/1 |
| --- | --- |
| API Name | remoteCSE RETRIEVE with or without resultContent parameter |
| Target Resource | <remoteCSE> resource located under <CSEBase> of the hosting CSE |
| Description | The interface is used to send a <remoteCSE> RETRIEVE request attached with resultContent to a hosting CSE, and the hosting CSE will send back a response containing attributes of the requested <remoteCSE> resource. |
| Resource Structure |  |
| Call Flow |  |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin Entity ID of request originator |
| Example with RCN=1 or No RCN | API/CSR/RET/001 API/CSR/RET/001_RCN1 HTTP Request: GET /cse-name/cse-name2?rcn=1 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: HTTP/1.1 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2000 Content-Length:227 Content-Type:application/json { "m2m:csr": { "cb": "//192.168.56.2:8282/cse-name2", "csi": "/cse2ID", "ct": "20180801T093501", "et": "99991231T235959", "lt": "20180801T093501", "pi": "cseID", "poa": [ "http://192.168.56.2:8282" ], "ri": "cse2ID", "rn": "cse-name2", "rr": true, "ty": 16 } } |

#### 6.2.3.3	API-CSR-UPD

| API Id | API/CSR/UPD/001 API/CSR/UPD/001_RCN/0 API/CSR/UPD/001_RCN/1 |
| --- | --- |
| API Name | remoteCSE UPDATE with or without resultContent parameter |
| Target Resource | <remoteCSE> resource located under <CSEBase> of the hosting CSE |
| Description | The interface is used to send a <remoteCSE> UPDATE request attached with resultContent to a hosting CSE, and the hosting CSE will send back a response according to the configured resultContent value as following: When resultContent is set to 0 (zero): The response contains the response status code ONLY with no information of the requested <remoteCSE> resource. When resultContent is set to 1 (one): The response contains a response status code as well as the <remoteCSE> resource information (attributes) that represents the Originator CSE. |
| Resource Structure |  |
| Call Flow |  |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin CSE-ID of request originator |
| Example with RCN=1 or No RCN | API/CSR/UPD/001 API/CSR/UPD/001_RCN1 Example: Demonstrate the update of the <pointOfAccess> attribute of <remoteCSE> resource. HTTP Request: PUT /cse-name/cse-name2?rcn=1 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 { "m2m:csr": { "poa": ["http://192.168.0.100:8282"] } } HTTP Response: HTTP/1.1 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2004 Content-Length:228 Content-Type:application/json { "m2m:csr": { "cb": "//192.168.56.2:8282/cse-name2", "csi": "/cse2ID", "ct": "20180801T093501", "et": "99991231T235959", "lt": "20180801T095839", "pi": "cseID", "poa": [ "http://192.168.0.100:8282" ], "ri": "cse2ID", "rn": "cse-name2", "rr": true, "ty": 16 } } |
| Example with RCN=0 | API/CSR/UPD/001_RCN0 Example: Demonstrate the update of the <pointOfAccess> attribute of <remoteCSE> resource. HTTP Request: PUT /cse-name/cse-name2?rcn=0 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 { "m2m:csr": { "poa": ["http://192.168.0.101:8282"] } } HTTP Response: HTTP/1.1 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2004 Content-Length:0 |

#### 6.2.3.4	API-CSR-DEL

| API Id | API/CSR/DEL/001 API/CSR/DEL/001_RCN/0 API/CSR/DEL/001_RCN/1 |
| --- | --- |
| API Name | remoteCSE DELETE with or without resultContent parameter |
| Target Resource | <remoteCSE> resource located under <CSEBase> of the hosting CSE |
| Description | The interface is used to send a <remoteCSE> DELETE request attached with resultContent set to 0 to the hosting CSE, and the hosting CSE will delete the <remoteCSE> resource and send back a response containing the response status code of the DELETE operation. |
| Resource Structure |  |
| Call Flow |  |
| HTTP Header Information | Header Value Accept application/ json X-M2M-RI Request ID X-M2M-Origin CSE-ID of request originator |
| Example with RCN=1 or No RCN | API/CSR/DEL/001 API/CSR/DEL/001_RCN1 Example: Demonstrate the update of the <pointOfAccess> attribute of <remoteCSE> resource. HTTP Request: PUT /cse-name/cse-name2?rcn=1 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 { "m2m:csr": { "poa": ["http://192.168.0.100:8282"] } } HTTP Response: HTTP/1.1 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2004 Content-Length:228 Content-Type:application/json { "m2m:csr": { "cb": "//192.168.56.2:8282/cse-name2", "csi": "/cse2ID", "ct": "20180801T093501", "et": "99991231T235959", "lt": "20180801T100431", "pi": "cseID", "poa": [ "http://192.168.0.101:8282" ], "ri": "cse2ID", "rn": "cse-name2", "rr": true, "ty": 16 } } |
| Example with RCN=0 | API/CSR/DEL/001_RCN0 HTTP Request: PUT /cse-name/cse-name2?rcn=0 HTTP/1.1 Host: 192.168.56.102:9011 Accept: application/json X-M2M-Origin: C0120180406T0846311405855351047680_cse01 X-M2M-RI: 1234 HTTP Response: HTTP/1.1 200 OK X-M2M-RI: 1234 X-M2M-RSC: 2002 Content-Length:0 |

================= end of input   =============================