| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST #36.1 |
| Source:* | In Song Lee, KETI, insong@keti.re.kr Il-Yeop Ahn, KETI, iyahn@keti.re.kr |
| Date:* | 2018-08-08 |
| Reason for Change/s:* | Fix minor error in pollingChannel TP |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-v2.5.0 |
| Clauses * | 7.2.1.8.1, 7.2.2.9.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contirubtion is provided to fix minor error in pollingChannel test purposes. And it also include one new test case for AE.

- TP/oneM2M/CSE/PCH/003

- Two changes has been made. Test objective has been rephrased since it was a bit vague to understand. Secondly, expected behaviour did not include response for Notify Request from the AE. The expected behaviour need to include not only forwarding the response to Originator, but also sending the response about Notify Request from the AE.

- TP/oneM2M/AE/PCH/002

- This is new test case for AE which testing whether it can send Retrieve Request to pollingChannelURI resource.

### -----------------------Start of change 1-------------------------------------------

TP/oneM2M/CSE/PCH/003

| TP Id | TP/oneM2M/CSE/PCH/003 |
| --- | --- |
| Test objective | Check that the IUT performs both forwarding the polling response message to the CSE and sending response to AE after receiving a Notify Request from the AE |
| Reference | TS-0001 [1], clause 10.2.13.8, TS-0004 [2], clause 7.4.22.2.2 |
| Config Id | CF02 |
| Parent Release | Release 2 |
| PICS Selection | PICS_PCH |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered an AE and the AE1 having a child <pollingChannel> resource and the IUT having received a retrieve Request from the AE containing To set to POLLINGCHANNELURI_RESOURCE_ADDRESS and the IUT having received a NOTIFY Request from the CSE containing To set to AE_RESOURCE_ADDRESS and From set to CSE_ID and the IUT sends a Response to the AE containing Response Status Code set to 2000 (OK) Content containing the Request received from the CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a NOTIFY Request from the AE containing To set to POLLINGCHANNELURI_RESOURCE_ADDRESS and Content containing Response Status Code set to RESPONSE_STATUS_CODE } | IUT ( AE |
|  | then { the IUT sends a Response to the CSE Response Status Code set to RESPONSE_STATUS_CODE the IUT sends the valid NOTIFY Response to the AE } | IUT ( CSE IUT ( AE |
| Note: Based on figure 10.2.13.1-1 in TS-0001[1] step 005 and 006 |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of new text 1-------------------------------------------

TP/oneM2M/AE/PCH/002

| TP Id | TP/oneM2M/AE/PCH/002 |
| --- | --- |
| Test objective | Check that the IUT sends an RETRIEVE Request to <pollingChannelURI> resource See the Note below. |
| Reference | TS-0001 [1], clause 10.2.13.6, TS-0004 [2], clause 7.4.22.2.2 |
| Config Id | CF02 |
| Parent Release | Release 2 |
| PICS Selection | PICS_PCH |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the AE having a child <pollingChannel> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to POLLINGCHANNELURI _RESOURCE_ADDRESS } | NA |
|  | then { the IUT sends a valid RETRIEVE Request containing To set to POLLINGCHANNELURI _RESOURCE_ADDRESS From set to AE_ID } | IUT ( CSE |
| Note: Based on figure 10.2.5.12-1 in TS-0001[1] step 001. |

### -----------------------End of new text 1---------------------------------------------