| CHANGE REQUEST |
| --- |
| Meeting:* | TP37 |
| Source:* | Xie Qian, caict,xieqian@caict.ac.cn |
| Date:* | 2018-09-17 |
| Contact:* | Xie Qian, caict,xieqian@caict.ac.cn |
| Reason for Change/s:* | Edit text of TR-0051 V0.1.0 |
| CR against: Release* | V0.1.0 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0051 V0.1.0 |
| Clauses/Sub Clauses* | 6.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is edit text for TR-0051 V0.1.0 in chapter 6.2 to keep consistency.

### -----------------------Start of change 1-------------------------------------------

#### 6.2.4.0	Introduction

The <AE> resource represents information about an Application Entity that is registered to a CSE. The originator of an <AE> create request is and only can be an AE. A CSE is not allowed to initiate an <AE> create request.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 6.2.4.1API-AE-CRE

| API Id | API/AE/CRE/001 API/AE/CRE/001_RCN0 API/AE/CRE/001_RCN1 API/AE/CRE/001_RCN2 API/AE/CRE/001_RCN3 |
| --- | --- |
| API Name | AE CREATE with or without resultContent parameter |
| Target Resource | <CSEBase> resource of the requested <AE> resource |
| Description | The interface is used by an AE Registree to send an <AE> CREATE request to a Registrar CSE and the Registrar CSE creates an <AE> resource and sends back a response to the AE Registree according to the configured resultContent parameter. A sensor is registered to the platform by sending an <AE> registration request to the CSEBase. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 6.2.4.2 API-AE-RET

| API Id | API/AE/RET/001_RCN1 API/AE/RET/001_RCN4 |
| --- | --- |
| API Name | AE RETRIEVE with or without resultContent parameter |
| Target Resource | The <AE> resource located under <CSEBase> |
| Description | The interface is used to send an <AE> RETRIEVE request attached with resultContent to the <AE> resource located under the <CSEBase> of the CSE, and the hosting CSE will send back a response according to the configured resultContent. |

-----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

#### 6.2.4.3 API-AE-UPD

| API Id | API/AE/UPD/001 API/AE/UPD/001_RCN0 API/AE/UPD/001_RCN1 |
| --- | --- |
| API Name | AE UPDATE with or without resultContent set |
| Target Resource | The <AE> resource located under <CSEBase> resource of CSE |
| Description | The interface is used to send an <AE> UPDATE request to the target <AE> resource under the CSE, and the hosting CSE will send back a response only containing the response status code indicating the request processing status. |

-----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

#### 6.2.4.4 API-AE-DEL

| API Id | API/AE/DEL/001 API/AE/DEL/001_RCN0 API/AE/DEL/001_RCN1 |
| --- | --- |
| API Name | AE DELETE |
| Target Resource | The <AE> resource located under <CSEBase> resource of CSE |
| Description | The interface is used to send an <AE> DELETE request to the hosting CSE, and the hosting CSE will delete the <AE> and send back a response containing a response status code indicating the DELETE request status. |

-----------------------End of change 5---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?