| CHANGE REQUEST |
| --- |
| Meeting ID:* | TST #38 |
| Source:* | Bob Flynn(bob.flynn@convidawireless.com) |
| Date:* | 2018-12-02 |
| Reason for Change/s:* | See Introduction |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0047v0.2.2 |
| Clauses * | 5.1.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## R01 – During joint ARC/TST feedback was provided to questions in my comments.  I removed the comments and made changes to reflect the feedback.

## 1 – specific details of what a 3GPP identifier are SP specific.  We will not be able to add that clarity at this point.

## 2/4 – even though there are no MEF implementations at this point, for completeness, ARC wants to retain the MEF call flows in the document.  The primitives are defined, so this should be fine,

## 3 – the UE interface is manufacturer dependent. This document cannot add a specific implementation at this point.

### -----------------------Start of change 1-------------------------------------------

### 5.1.1 UE Provisioning and Deployment

When new UE based devices are deployed they can be provisioned remotely using the 3GPP identifier assigned by the core network service provider. Using oneM2M APIs a remote device can be provisioned with a designated registrar CSE as needed. Additionally, a device can be remotely reconfigured or decommissioned.

- The infrastructure application (IN-AE) enrols a device by specifying the UE device using its 3GPP identifiers and providing the location of a oneM2M Enrolment Function Service (MEF). The oneM2M <triggerRequest> resource is sent in a primitive to an infrastructure node (IN-CSE).

- The infrastructure node (IN-CSE) will send a message to the 3GPP SCEF interface to trigger the AE or CSE hosted on the UE specified by the 3GPP identifier.

- The AE or CSE receives the 3GPP trigger message from the UE and sends an Enrollment Request to the MEF specified in the message.

- The oneM2M Enrolment Function responds with identifiers and credentials that the AE/CSE can use to register to the oneM2M Service Layer.

- The AE/CSE sends a registration request to the oneM2M Service Layer.

- The oneM2M Service Layer notifies the infrastructure application that the device is registered.

In clause 7.1 the specific messages are described in further detail.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?