| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS 38.2 |
| Source:* | Andreas Kraft, a.kraft@telekom.de |
| Date:* | 2019-02-01 |
| Reason for Change/s:* | SDT 4.0 - Support for excluding certain components when inheriting |
| CR against: Release* | Release 4 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | SDT UML diagram |
| Clauses * | Extend |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR presents changes of oneM2m’s Gitlab SDT repository (see https://git.onem2m.org/MAS/SDT) to reflect the transition towards version 4.0 of the Smart Device Template.

This CR proposes to introduce a mechanism to exclude certain components when inheriting / extending a component. This is done by allowing for zero or many <exclude> sub-elements for the <extend> element. These sub-elements having a mandatory attribute name and an optional attribute type. When present, the type attribute must contain one of the following identifier:

| Type Identifier | Remark |
| --- | --- |
| datapoint | The name attribute refers to a DataPoint. This is the default when the type attribute is left out. |
| action | The name attribute refers to an Action of the same name. |
| event | The name attribute refers to an Event of the same name. |
| moduleclass | The name attribute refers to a ModuleClass of the same name. |
| subdevice | The name attribute refers to a SubDevice of the same name. |
| property | The name attribute refers to a property of the same name. |

The type identifiers from this table are represented as an <<enumeration>> in the UML diagram.

When extending a parent definition then all the respective elements specified by the <exclude> sub-elements, that are of the specified type, are not inherited.

This CR provides changes in the UML diagram as well as an explanation on how this feature is expected to be used.

To improve consistency with other elements in the SDT UML diagram and resulting XSD it is proposed to change the name of the original <extends> element to upper case and singular form: <Extend>.

The images referenced in “docs/SDT_Components.md” etc are NOT updated according with the changes proposed in this CR. They need to be consolidated when all changes are integrated, but the change to the data types part of the UML diagram looks as follows:

See the new branch in gitlab:

https://git.onem2m.org/MAS/SDT/tree/MAS-2018-0161-SDT_4_0_-_Support_for_excluding_certain_components_when_inheriting

# Comments

Editor’s note: Check later when integrating all contributions whether it is more consistent to have a list of element names in one single <exclude> element (in the name attribute), or to have separate XML elements.