| CHANGE REQUEST |
| --- |
| Meeting ID:* | TP#39 |
| Source:* | Kei Harada, NTT, kei.harada.by@hco.ntt.co.jp |
| Date:* | 2019-02-18 |
| Reason for Change/s:* | Add the figure expressing the mapping relationship between BO and SDT. |
| CR against: Release* | Release-4 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < WI-0084> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0030 V3.0.1 |
| Clauses * | Annex A |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | TS-0023, TS-0012 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The Mapping rules between SDT and oneM2M Base Ontology (BO) is written in TS-0023 but it has not spread effectively to other TSs like TS-0030, TS-0012.

To solve this situation, this CR proposes to add the figure expressing the mapping relationship between BO and SDT into TS-0030.

This CR is based on the result of descussion done at MAS#38 with MAS-2018-0146R01-Description_the_Mapping_Rule_between_SDT_and_BO.

### -----------------------Start of change 1-------------------------------------------

Annex A (informative):
Example for ontology based interworking

# A.1	Overview

This example extends the example - a (simplified) washing machine - of clause B.1.3.3 of oneM2M TS-0012 [3].
However in contrast to oneM2M TS-0012 in this example it is assumed that the washing machine is not a 'native' oneM2M application but is interworked with the oneM2M System via ontology based interworking.

In contrast to oneM2M TS-0012 the semantic description (contained in the descriptor attribute of the <semanticDescriptor> resource) is not of interest but rather the structure of the specialized <flexContainer> resources to which these <semanticDescriptor>s belong. 
Also Functions and Commands (which are only described in RDF form in the sematic descriptors) are not considered, but only Services, Input- / OutputDatapoints and Operations, which are the resources containing data for communication with the washing machine are handled here.

The example given here is a (simplified) washing machine, based on class:WashingMachine, specified in SAREF [i.2].

It is assumed the washing machine has been manufactured by manufacturer XYZ. 
The ontology that describes XYZ washingmachines is identified by the IRI: http://www.XYZ.com/WashingMachines.

It is assumed the XYZ washing machines are compliant with SAREF. Also, as described in clause B.1 of oneM2M TS-0012 [3], SAREF is compliant with the oneM2M base ontology.
That implies that every class/property of the XYZ ontology is either a subclass/sub-property of SAREF or - if no suitable class/property exists in SAREF - is a subclass/sub-property of the base ontology.

The classes/properties that are taken from SAREF are prefixed with: "saref:"
The classes/properties that are taken from XYZ ontology are prefixed with: "XYZ:"
The classes/properties that are taken from the base ontology are prefixed with: "BO:"

The model of the type of washing machine is class XYZ:XYZ_Cool

which is a sub-class of class saref:WashingMachine

which in turn is subclass of BO:InterworkedDevice

The state of the washing machine is given by XYZ:WashingMachineStatus that can take the values "WASHING" or "STOPPED" or "ERROR".

XYZ:WashingMachineStatus is a sub-class of saref:state

which in turn is subclass of BO:OutputDataPoint

This WashingMachineStatus is provided as an the OutputDataPoint of a service XYZ:MonitorService which exposes the MonitoringFunction to the network.

Class XYZ:MonitorService is a sub-class of saref:Service

which in turn is subclass of BO:Service

The related function of the washing machine is described by class XYZ:MonitoringFunction.

Class XYZ:MonitoringFunction is a sub-class of saref: Function

which in turn is subclass of BO:Function

The function of the washing machine to control the washing machine is in class XYZ:StartStopFunction which has three commands: ON_Command, OFF_Command, Toggle_Command.

NOTE:	Since classes for Functions and Commands are not needed for interworking as they only appear in the RDF description in <sematicDescriptor> resources the XYZ:MonitoringFunction and XYZ:StartStopFunction are not further considered here. They are, however, described in the related example of clause B.1.3.3 of oneM2M TS-0012 [3].

The related service of the washing machine that represents that XYZ:StartStopFunction is class: XYZ:SwitchOnService. It has:
an InputDataPoint: XYZ:BinaryInput (to expose command ON_Command and OFF_Command) and
an Operation: XYZ:ToggleBinary (to expose command Toggle_Command)

Class XYZ: SwitchOnService is a sub-class of saref:SwitchOnService

which in turn is subclass of BO:Service

InputDataPoint: XYZ:BinaryInput is a sub-class of BO:InputDataPoint

Operation: XYZ:ToggleBinary is a sub-class of BO:Operation

XYZ describes this type of washing machine with a XYZ:Description as "Very cool Washing Machine"

XYZ:Description os a sub-class of BO:ThingProperty

The following figure shows the relationship of the ontology that describes model XYZ_cool of XYZ washingmachines with the oneM2M base ontology.

Figure 7: Relationship of the ontology that describes model XYZ_cool
of XYZ washingmachines with the oneM2M base ontology

The following figure shows the mapping rules between oneM2M base ontology and SDT based on TS-0023 [5].

### -----------------------End of change 1---------------------------------------------