| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 39 |
| Source:* | Andrew Min-gyu Han, Hansung University,andyhan@hansung.ac.kr Joong-kwon Lim,Hansung University, naulim@hansung.ac.kr Hanbeag Cho, ETRI, hbcho@etri.re.kr Jinho Jo, KT, jh.jo@kt.com |
| Date:* | 2019-02-18 |
| Reason for Change/s:* | Add a trainborne terminal as a device model of the Railway Domain |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <WI-0084> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.1.0 |
| Clauses * | 2.2, 3.2, 5.3, 5.5.7, 5.6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR adds a trainborne terminal as a device model of the Railway Domain.

The balise is installed in between the track rail or rail-side. When the train goes over the balise, the balise antenna of the train (locomotive) gives tele-powering to balise, gets up-link from balise as well.

The BTM gets the information from the up-link and using connectivity, sends the information to Radio Block Centre.

The RBC indicates the train location and controls(gives information) other train to avoid different train in the same rail.

To do this, in railway domain, RDM needs to add trainborne terminal.

<Fig> Balise operation as a part of ATP

### -----------------------Start of change 1-------------------------------------------

### 5.5.7.y deviceTrainborneTerminal

A trainborne terminal is a device of the Railway Domain. The trainborne terminal is usually equipped in locomotive and used between the train driver, controller, crew and rail-side worker to share their work status via voice communication. As a part of ATP(Automatic Train Protection) system as well, it collects train operation information from various railway domain devices such as the locomotive, passenger cars and balises on the rail, and sends the information to the Radio Block Centre which controls the railway operations.

Table 5.5.7.y-1: Modules of deviceTrainborneTerminal Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.1.12. |
| audioVolume | audioVolume | false | See clause 5.3.1.8 |
| clock | clock | true | See clause 5.3.1.18. |
| energyConsumption | energyConsumption | true | See clause 5.3.1.32. |
| keypad | keypad | false | See clause 5.3.1.49. |
| operationMode | operationMode | true | See clause 5.3.1.57. |
| phoneCall | phoneCall | false | See clause 5.3.1.64. |
| PTTButton | pushButton | false | See clause 5.3.1.69. |
| runState | runState | true | See clause 5.3.1.75. |
| signalStrength | signalStrength | true | See clause 5.3.1.78. |
| baliseTransmission | baliseTransmissionModule | true | See clause 5.3.x.y |
| connectivity | connectivity | true | See clasue 5.3.1.25 |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.3.x Railway Domain

### 5.3.x.y baliseTransmissionModule

A balise is an electronic beacon or transponder placed between the rails of a railway as part of an automatic train protection (ATP) system.

The Balise Transmission Module(BTM) ModuleClasses provides capabilities to indicate and to get balise information.

Table 5.3.x.y-1: DataPoints of baliseTransmissionModule Class

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| baliseSystemId | hd:enumBaliseSystemIndicator | R | true |  | Get the hd:enumBaliseSystemIndicator (see clause 5.6.x). |
| telegramMessage | xs:string | R | true |  | The telegramMessage is system-specific. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.6.x	hd:enumBaliseSystemIndicator

Used for the “baliseTransmissionModule” ModuleClass.

Table 5.6.x-1: Interpretation of hd:enumBaliseSystemIndicator

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | ATC | Korea [i.x] |
| 2 | ATP | Korea [i.x] |
| 3 | CTCS-3 | China [i.y] |
| NOTE: The Note shows countries which are using a balise system which is indicated on left-hand side. |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

## 2.2	Informative references

[i.x]	Ju-Hun Park, Hui Sik Kim, Sang-A Hong, Sun Young Jang,
“A Study on the Definition of Terms for Domestic Train Control System”, Korean Society for Railway,  2015,
http://railway.or.kr/Papers_Conference/201502/pdf/KSR2015A114.pdf

[i.y]	CTCS-3级列控系统总体技术方案 (Train Technical Solution), 中国铁道出版社(Chinese Railway Press), 2008, ISBN: 9787113091590

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

## 3.2	Abbreviations

ATP	Automatic Train Protection

BTM	Balise Transmission Module

RBC	Radio Block Centre

### -----------------------End of change 5---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?