| Input Contribution |
| --- |
| Meeting ID* | RDM#40 |
| Title:* | Use Case on the Release of Emergency Mode |
| Source:* | Taehyun KIM, SyncTechno thyun.kim@synctechno.com SeungMyeong JEONG, KETI sm.jeong@keti.re.kr |
| Date:* | 2019-05-23 |
| Input related to* | TR-0046 (Study on Public Warning Service Enabler) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | n/a |
| Decision requested or recommendation:* | Incorporate the text into TR-0046 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes a result of study for the public warning service use cases and potential requirements.

### -----------------------Start of input 1-------------------------------------------

## 6.x Release of Emergency Mode

### 6.x.1	Description

A device perform a predefined emergency task in an emergency mode when a warning message, that is compatible with the Public Warning Information Model, is received. It is necessary to terminate a predefined emergency task and release an emergency mode when an emergency situation ends when following cases happen.

- A warning originator sends a warning message indicating the termination of an emergency situation.

- A timer that a device has and is triggered to start when a warning message is received is expired.

- A user of a device receiving a warning message and performing a pre-defined emergency task manually terminates the emergency mode of a device.

### 6.x.2	Source

None

### 6.x.3	Actors

- Warning originator: Responsible for providing warning notification to citizens in emergency situation

- M2M Service Platform (MSP): M2M service platform that communicates with UDs and PDs in its M2M system

- Device: M2M/IoT devices which perform pre-defined emergency tasks  in emergency situation.

- User: a person in charge of the management of a device

### 6.x.4	Pre-conditions

- A device supports the Public Warning Information Model

- A device performs emergency tasks in the emergency mode.

### 6.x.5	Triggers

It is triggered when following cases happen.

- A warning originator sends a warning message indicating the termination of an emergency situation.

- A timer that a device has and is triggered to start when a warning message is received is expired.

- A user of a device receiving a warning message and performing a pre-defined emergency task manually terminates the emergency mode of a device.

### 6.x.6	Normal Flow

Figure 6.x.6-1 Normal flow for the release of emergency mode

- A warning originator sends a warning message indicating the termination of an emergency situation.

- A M2M service platform forwards a warning message indicating the termination of an emergency situation received from a warning originator.

- A device switches to normal mode when a warning message is received.

- A device performs normal tasks.

### 6.x.7	Alternative Flow

A. Triggered by timer.

Figure 6.x.7-1 Alternative flow on triggering by a timer

- A device receives a warning message.

- The device switches to the emergency mode when a warning message is received and then performs  emergency tasks.

- The device starts a timer to alarm the time to terminate the emergency tasks.

- The timer is expired

- The device switches to the normal mode to perform normal tasks

B. Triggered by a user

Figure 6.x.7-2 Alternative flow on triggering by a user

- A user controls the device to terminate the emergency mode.

- The device switches to the normal mode to perform the normal tasks

### 6.x.8	Post-conditions

None

### 6.x.9	High Level Illustration

Figure 6.x.9-1 High level illustration of the release of emergency mode

### 6.x.10	Potential Requirements

Additionally a new requirement is needed.

Table 6.x.10-1 New potential requirement

| Requirement ID | Description |
| --- | --- |
| HLR-xxx | oneM2M System shall support Public Warning Information Model that contains the emergency mode of a device including timer information. |

-----------------------End of input 1---------------------------------------------