| Input Contribution |
| --- |
| Meeting ID* | RDM#40 |
| Title:* | Requirements on geo-location and geo-functions |
| Source:* | SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr Jiho Lee, KETI, jlee7123@keti.re.kr |
| Date:* | 2019-05-23 |
| Input related to* | TS-0001 v4.6.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | n/a |
| Decision requested or recommendation:* | Incorporate the proposed requirements into the TS-0002 |
| Template Version: November 2018 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

With the contribution SDS-2019-0255-discussion_on_locationPolicy_clarification, the SDS WG confirmed that oneM2M specifications have no 1) location information syntax and semantics, 2) geospatial functions support.

This contribution proposes to add two requriements on the technical topics above.

For information, the existing location related requirements are:

| OSR-006 | The oneM2M System shall be able to reuse the services offered by Underlying Networks to M2M Applications and/or M2M Services by means of open access models (e.g. OMA, GSMA OneAPI framework). Examples of available services are: IP Multimedia communications. Messaging. Location. Charging and billing services. Device information and profiles. Configuration and management of devices. Triggering, monitoring of devices. Small data transmission. Group management. (see note 1). | Partially implemented (see note 10) |
| --- | --- | --- |
| OSR-047 | The oneM2M System shall be able to support mechanism for the M2M Devices and/or Gateways to report their geographical location information to M2M Applications (see note 7). | Implemented in Rel-1 |
| OSR-048 | The oneM2M System shall provide an M2M Service that allows M2M Devices and/or Gateways to share their own or other M2M Devices' geographical location information (see note 7). | Implemented in Rel-1 |
| OSR-117 See REQ-2017-0030R05 | The oneM2M System shall support setting the configuration for Geo-Fence based location services by a M2M Application. | Implemented in Rel-2 |
| OSR-120 See REQ-2017-0031R05 | The oneM2M System shall be able to provide the service capability for location based services | Implemented |
| OSR-131 See REQ-2017-0031R05 | The oneM2M System shall be able to verify geographical location information from moving objects regardless of information accuracy. | Rel-3/ future releases? |
| OSR-0151 See REQ-2018-0011R03 | The oneM2M System shall enable services to receive and utilize location-based information about available access networks, their congestion level and other related network information when the information is provided by the Underlying Network. | Rel-4/ future releases? |
| OSR-181 See REQ-2018-0067R01 | The M2M System shall provide capabilities to request from the underlying network either the last known location information or current location information, if supported by the underlying networks. | 4 |
| OSR-184 See REQ-2018-0070R04 | The oneM2M System shall support dynamic and variable vehicle Geo-Fence setting configuration for location-based services (e.g. boundary reshaping) | Rel-4 |
| SER-026 | The oneM2M System shall be able to provide mechanism for the protection of Confidentiality of the geographical location information (see note 2). | Implemented in Rel-1 |

=========================== Start of New Input 1 ===========================

## 6.1	Overall System Requirements

Table 1: Overall System Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-00x | The oneM2M System shall support geometry objects (e.g. Point, Polygon) to represent the geo-location of a M2M Device, M2M Gateway and a Thing. |  |
| OSR-00y | The oneM2M System shall support syntax and semantics of geometry objects to assure location information interoperability for M2M Applications. |  |
| OSR-00z | The oneM2M System shall support discovery of identifiers of Things with geospatial function execution against geometry objects representing the Things. |  |

=========================== End of New Input 1 ===========================