| Input Contribution |
| --- |
| Meeting ID* | RDM#41 |
| Title:* | Use cases that selectively respond to emergency types |
| Source:* | Taehyun KIM, SyncTechno Inc., thyun.kim@synctechno.com |
| Date:* | 2019-07-08 |
| Input related to* | WI-0070, TR-0046 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | N/A |
| Decision requested or recommendation:* | Incorporate the text into TR-0046 |
| Template Version: November 2018 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes a result of study for the public warning service use cases and potential requirements.

### -----------------------Start of input 1-------------------------------------------

## 6.x	Selective respond to emergency types

### 6.x.1	Description

IoT devices are in charge of a given simple task using limited computing resources. The emergency task that triggered by a public warning message is also a given simple task for specific emergency event (e.g. automatic control gas valve when receive earthquake warning). In other words, an IoT device responds to specific type of emergency event rather then all types of emergencies. M2M System may provide a mechanism to deliver public warning message to the device which interested in.

### 6.x.2	Source

None

### 6.x.3	Actors

- Warning originator: Responsible for providing warning notification to citizens in emergency situation

- M2M Service Platform (MSP): M2M service platform that communicates with UDs and PDs in its M2M system

- Device: M2M/IoT devices which perform pre-defined emergency tasks  in emergency situation.

### 6.x.4	Pre-conditions

- A device is configured to enable the public warning service.

### 6.x.5	Triggers

- A warning originator sends a warning message that contain emergency type.

### 6.x.6	Normal Flow

Figure 6.x.6-1 Normal flow for the selective respond to type of emergencies

- A device setup configuration including types of emergencies which device interested in.

- The device subscribe to receive emergency notification for designated types.

- A warning originator sends a warning message including type of emergencies.

- A M2M service platform forwards the received warning message to devices that subscribed on type of emergency event specified in warning message.

- A device switches to emergency mode when a warning message is received.

- A device performs emergency tasks that are pre-defined.

### 6.x.7	Alternative Flow

None

### 6.x.8	Post-conditions

None

### 6.x.9	High Level Illustration

Figure 6.x.9-1 High level illustration of selective respond to type of emergencies

### 6.x.10	Potential Requirements

This use case scenario can be fulfilled by the existing requirements as below.

Table 6.x.10-1 Related exiting requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR -109 See REQ-2017-0008R02 | The oneM2M System shall enable M2M Gateways to distribute notifications according to how data subscriptions have been grouped/aggregated. | Implemented in Rel-3 |
| OSR-110 See REQ-2017-0008R02 | The oneM2M System shall enable subscriptions to changes to multiple data sources (e.g. oneM2M resources) which aim to generate data publication (i.e. automatic notifications) if and only if the expected changes to each of those multiple resources occur concurrently. | Implemented in Rel-3 |

Additionally a new requirement is needed.

Table 6.x.10-2 New potential requirement

| Requirement ID | Description |
| --- | --- |
| HLR-xxx | oneM2M System should support Public Warning Information Model that contains an event type for each emergency situation. (Emergency situation can be earthquake, tsunami, etc.) |

### -----------------------End of input 1---------------------------------------------