| Input Contribution |
| --- |
| Meeting ID* | RDM#41 |
| Title:* | Public warning service information models |
| Source:* | Taehyun KIM, SyncTechno Inc., thyun.kim@synctechno.com |
| Date:* | 2019-07-08 |
| Input related to* | WI-0070, TR-0046 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | N/A |
| Decision requested or recommendation:* | Incorporate the text into TR-0046 |
| Template Version: November 2018 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes an abstract information model for public warning service.

### -----------------------Start of input 1-------------------------------------------

## 9.2	Abstract information models

### 9.2.1	Definition of Data Types

#### 9.2.1.1	Enumeration types

This clause provides enumeration type descriptions for the public warning service domain. To clarify terms for the public warning service domain, the “pws” namespace qualifier will be used in following clauses.

A. pws:enumAlertStatus

The pws:enumAlertStatus enumeration type represents the appropriate handling of the alert message receiver.

Table 9.2.1.1-1: Interpretation of pws:enumAlertStatus

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Actual | Actionable by all targeted recipients |
| 2 | Exercise | Actionable only by designated exercise participants |
| 3 | System | For messages that support alert network internal functions |
| 4 | Test | Technical testing only, all recipients disregard |
| 5 | Draft | A preliminary template or draft, not actionable in its current form |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

B. pws:enumMessageType

The pws:enumMessageType represents the nature of the alert message.

Table 9.2.1.1-2: Interpretation of pws:enumMessageType

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Alert | Initial information requiring attention by targeted recipients |
| 2 | Update | Updates and supercedes the earlier message(s) |
| 3 | Cancel | Cancels the earlier message(s) |
| 4 | Ack | Acknowledges receipt and acceptance of the message(s) |
| 5 | Error | Indicates rejection of the message(s) |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

C. pws:enumAlertScope

The pws:enumAlertScope represents the intending scope of distribution for this alert message.

Table 9.2.1.1-3: Interpretation of pws:enumAlertScope

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Public | For general dissemination to unrestricted audiences |
| 2 | Restricted | For dissemination only to users with a known operational requirement |
| 3 | Private | For dissemination only to specified addresses |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

D. pws:enumEventCategory

The pws:enumEventCategory represents the category of the alerting event of the alert message.

Table 9.2.1.1-4: Interpretation of pws:enumEventCategory

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Geo | Geophysical (inc. landslide) |
| 2 | Met | Meteorological (inc. flood) |
| 3 | Safety | General emergency and public safety |
| 4 | Security | Law enforcement, military, homeland and local/private security |
| 5 | Rescue | Rescue and recovery |
| 6 | Fire | Fire suppression and rescue |
| 7 | Health | Medical and public health |
| 8 | Env | Pollution and other environmental |
| 9 | Transport | Public and private transportation |
| 10 | Infra | Utility, telecommunication, other non-transport infrastructure |
| 11 | CBRNE | Chemical, Biological, Radiological, Nuclear or High-Yield Explosive threat or attack |
| 12 | Other | Other events |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

E. pws:enumResponseType

The pws:enumResponseType represents the type of recommended response action for the target audience when the alert message received.

Table  9.2.1.1-5: Interpretation of pws:enumResponseType

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Shelter | Take shelter in place |
| 2 | Evacuate | Relocate to evacuate area |
| 3 | Prepare | Make preparations process |
| 4 | Execute | Execute a pre-planned activity |
| 5 | Avoid | Avoid the subject event |
| 6 | Monitor | Attend to information sources |
| 7 | Assess | Evaluate the information in this message |
| 8 | AllClear | The subject event no longer poses a threat or concern |
| 9 | None | No action recommended |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

F. pws:enumUrgency

The pws:enumUrgency represents the urgency of the subject event of the alert message.

Table 9.2.1.1-6: Interpretation of pws:enumUrgency

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Immediate | Responsive action should be taken immediately |
| 2 | Expected | Responsive action should be taken soon (within next hour) |
| 3 | Future | Responsive action should be taken in the near future |
| 4 | Past | Responsive action is no longer required |
| 5 | Unknown | Urgency not known |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

G. pws:enumSeverty

The pws:enumSeverty represents the severity of the subject event of the alert message.

Table 9.2.1.1-7: Interpretation of pws:enumSeverty

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Extreme | Extraordinary threat to life or property |
| 2 | Severe | Significant threat to life or property |
| 3 | Moderate | Possible threat to life or property |
| 4 | Minor | Minimal to no known threat to life or property |
| 5 | Unknown | Severity unknown |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

H. pws:enumCertainty

The pws:enumCertainty represents the certainty of the subject event of the alert message.

Table 9.2.1.1-8: Interpretation of pws:enumCertainty

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Observed | Determined to have occurred or to be ongoing |
| 2 | Likely | Likely (p > ~50%) |
| 3 | Possible | Possible but not likely (p <= ~50%) |
| 4 | Unlikely | Not expected to occur (p ~ 0) |
| 5 | Unknown | Certainty unknown |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

#### 9.2.1.2	Complex data types

This clause provides complex data types descriptions for the public warning service domain. To clarify terms for the public warning service domain, the “pws” namespace qualifier will be used in following clauses.

A. pws:TargetArea type

If the originator wants to specify the geographical area which the public warning message will be propagated, the geographical information for the target region may be specified. The Area data type can be used to deliver target geospatial data to which a warning message will be propagated. The geolocation data should be applied to the standard such as GeoJSON to improve machine interpretability.

Table 9.2.1.2-3: Structure of pws:TargetArea type

| Name | Description | Type | Mandatory/ Optional |
| --- | --- | --- | --- |
| polygon | The sequence of coordinate pair to define the polygon that identify the affected area of the alert message. Each coordinate value contains geolocation position value as specified in [WGS84] standard. | GeoJSON | O |
| circle | The sequence of numeric values to represent a center position and a radius that identify the affected area of the alert message. The first two values must [WGS84] geolocation position value represents the center position of the circle, and last value represents the radius delineating in kilometres. | GeoJSON | O |
| geocode | The geographic code identifying the affected area of the alert message. A geocode consists of valueName and value. Multiple geocode can be presented. | List of <Key, Value> pare | O |
| altitude | The specific or minimum altitude in feet above mean sea level of the affected area of the alert message. | Number | O |
| ceiling | The maximum altitude in feet above mean sea level of the affected area of the alert message. | Number | O |

B. pws:ExtraResource type

The pws:ExtraResource type is used to pass information about a media resource that contains additional information which includes the event associated with the warning message. For example, if an earthquake warning message generated by an authority includes information about a guide video for an earthquake, the TV may display a warning message and play the guide video by referring to the media resource information included in the pws:ExtraResource.

Table 9.2.1.2-2: Structure of pws:ExtraResource type

| Name | Description | Type | Mandatory/ Optional |
| --- | --- | --- | --- |
| mimeType | The MIME type, as described in [RFC2046], identifier describing the referenced resource file. | String | M |
| size | The approximate size of the resource file in bytes indicating the size of the referenced resource file. | Number | O |
| uri | The hyperlink URL that can be used to retrieve the resource over the Internet. | URI | O |
| derefUri | An alternative to the uri resource hyperlink giving the Base64 encoded content of the resource file. | String | O |
| digest | The SHA-1 hash value of the resource file for validation. | String | O |

C. pws:WarningInfo type

The pws:WarningInfo type contains key information that the authority wants to propagate to the public. This information can be used to recognize and respond to emergencies. Since all data elements contained in WarningInfo need to be machine-readable, the data are passed in the enumeration type defined in section 8.2.1.1. If necessary, additional information of pws:ExtraResource type and pws:TargetArea which clarify the warning area can be included.

Table 9.2.1.2-1: Structure of pws:WarningInfo type

| Name | Description | Type | Mandatory/ Optional |
| --- | --- | --- | --- |
| language | Contains a [RFC 3066] code value denoting the language of the info sub-element of the alert message. | string | O |
| category | The code denoting the category of the alerting event of the alert message. Multiple caterory can be presented in an <info> element. | Array of pws:enumEventCatetory | M |
| responseType | The code denoting the type of recommended response action for the target audience when the alert message received. Multiple responseType can be presented. | Array of pws:enumResponseType | O |
| urgency | The code representing the urgency of the subject event of the alert message. | pws:enumUrgency | M |
| severity | The code representing the severity of the subject event of the alert message. | pws:enumServerity | M |
| certainty | The code representing the certainty of the subject event of the alert message. | pws:enumCertainty | M |
| effective | The effective time of the information of the alert message. If this value is not presented, effective time is assumed to be the same time as in “sent” | DateTime | O |
| onset | The expected time of the beginning of the subject event of the alert message. | DateTime | O |
| expires | The expiry time of the information of the alert message. If this value is not presented, recipient can set own expiration policy. | DateTime | O |
| parameter | The definitions of system-specific parameter associated with the alert message. Multiple parameter can be presented. | List of <Key, Value> pare | O |
| resource | The definitions of all component parts of the resource referes to an additional file. This definition to be used to provide multimedia file to recipients. Multiple resource can be presented. | Array of pws:ExtraResource type | O |
| area | The definition of all component parts of the area identifying an affected area. A <info> element may contain one or multiple area definition to identify union of all the included area. | Array of pws:TargetArea type | O |

### 9.2.2	Definition of Message Formats

This clause defines the "Public Warning Message information model" shown in Figure 9.1.1-1. This is a specification of the message that is sent from the authority message to the M2M System to deliver to the device. This message specification can be defined as in Table 9.2.2-1, for the public warning message format for the oneM2M system by extracting machine interpretable attributes among CAP to keep interoperable with CAP 1.2 standard.

Editor’s Note: How to carry the information defined in this clause in oneM2M primitives needs to be further described for clarifying.

Table 9.2.2-1: Structure of public warning message format

| Name | Description | Type | Mandatory/ Optional |
| --- | --- | --- | --- |
| identifier | The identifier of the alert message, contains a number or string value that uniquely identifying this message. | String | M |
| sender | The identifier of the originator of this alert message. This value must guaranteed by assigner to be unique globally. | String | M |
| sent | The time and date of the origination of this alert message. | DateTime | M |
| status | The code to represent the appropriate handling of the alert message receiver. | pws:enumAlertStatus | M |
| msgType | The code to represent the nature of the alert message. | pws:enumMessageType | M |
| scope | The code to represent the intending scope of distribution for this alert message. | pws:enumScope | M |
| references | The list of identifiers for earlier message(s) referenced by this alert message. | Array of String | O |
| info | The container for all component parts of the info sub-element of the alert message. Multiple occurrences are permitted within a single <alert> element to support multiple language or sequence of alert information for an alert message. | Array of pws:WarningInfo type | O |

### 9.2.3	Definition of ModuleClasses

A. configurePWS

Table 9.2.3-1: configurePWS ModuleClass

| Doc | ConfigurePWS provides capabilities to change device settings which is related to public warning service including opt-out public warning service. |
| --- | --- |
| Action | Name | Doc | Argument | Return type |
|  | OptoutWarningMessage | Setup opt-out status of the device | Name: "command" Type: enum_EMERGENCY_TYPE | enum_EMERGENCY_TYPE |
| DataPoint | Name | Doc | Type | Read/Write |
|  | OptoutState | Current opt-out state of the device: Off: the device receive all public warning messages. On: all receive public warning messages will be discarded except opt-out not allowed warning message. | Boolean | Read/Write |
| Property | Name | Doc | Type |
|  | N/A |  |  |
| Event | Name | Doc | DataPoint |
|  | N/A |  |  |

B. emergencyTaskTriggering

Table 9.2.3-2: emergencyTaksTriggering ModuleClass

| Doc | EmergencyTaksTriggering provides capabilities to trigger the public warning service enabled devices when a public warning message received. |
| --- | --- |
| Action | Name | Doc | Argument | Return type |
|  | ExecuteEmergenceTask | Change operation mode to emergency mode and execute emergency tasks | Name: "PWSMessage" Type: pws:PWSMessage | enum_OPERATION_MODE |
| DataPoint | Name | Doc | Type | Read/Write |
|  | OperationMode | Current operation mode of the device: Null or 0 --- Normal mode 1 --- Emergency Mode | enum_OPERATION_MODE | Read/Write |
|  | OptoutState | Current opt-out state of the device. | String | Read only |
|  | ReceivedPWSMessages | List of received public warning messages. This list can be used to check duplicated warning message. | pws:PWSMessage Array | Read only |
| Property | Name | Doc | Type |
|  | N/A |  |  |
| Event | Name | Doc | DataPoint |
|  | EventTimerExpired | A expiry time specified in a received public warning message has expired | N/A |

C. emergencyModeTermination

Table 9.2.3-3: emergencyModeTermination ModuleClass

| Doc | EmergencyModeTermination provides capabilities to stop emergency task which triggered by a public warning message and terminate emergency mode. |
| --- | --- |
| Action | Name | Doc | Argument | Return type |
|  | TerminateEmergenceTask | Stop emergency tasks and change operation mode to normal mode | None | None |
| DataPoint | Name | Doc | Type | Read/Write |
|  | OperationMode | Current operation mode of the device: Null or 0: Normal mode 1: Emergency Mode | enum_OPERATION_MODE | Read/Write |
| Property | Name | Doc | Type |
|  | TBD… |  |  |
| Event | Name | Doc | DataPoint |
|  | TBD… |  |  |

### 9.2.4	Definition of Device

This clause provides the definition of virtual device information for public warning service supporting device using ModulClasses defined in clause 9.2.3.

Table 9.2.4-1: Modules and properties of devicePWS Device Model

| Type | Name | Description | Type | Mandatory/ Optional |
| --- | --- | --- | --- | --- |
| Module | configurePWS | See table 9.2.3 -1 | - | O |
|  | emergencyTaksTriggering | See table 9.2.3 -2 | - | M |
|  | emergencyModeTermination | See table 9.2.3 -3 | - | O |
| Property | initialOptoutStatus | Initial value for opt-out settings | Boolean | O |
|  | Location | Location of PWS device | Location | O |

### -----------------------End of input 1---------------------------------------------