| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#42 |
| Source:* | Xiaotao Li, CMCC, lixiaotao@chinamobile.com Yawen Niu, CMCC, niuyawen@chinamobile.com |
| Date:* | 2019-09-18 |
| Reason for Change/s:* | Adding a new Device model |
| CR against: Release* | Rel.4 |
| CR against: WI* | Active WI-0017 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.1.0 |
| Clauses * | clauses in 6.3.2 new clause 5.5.4.30 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a new Device model

-----------------------Start of change 1-------------------------------------------

#### 5.5.4.30 deviceBottleWarmer

A bottle warmer is an appliance designed for the purpose of warming the feeding bottle.

Table 5.5.4.30-1: Modules of deviceBottleWarmer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.1.12. |
| temperature | temperature | false | See clause 5.3.1.87. |
| runState | runState | true | See clause 5.3.1.75. |

-----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------6.3.2  Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| Device3DPrinter | dTDPr |
| deviceAirConditioner | deACr |
| deviceAirPurifier | deAPr |
| deviceAirQualityMonitor | dAQMr |
| deviceAudioReceiver | deARr |
| deviceBloodPressureMonitor | dBPMr |
| deviceCamera | devCa |
| deviceClothesDryer | deCDr |
| deviceClothesWasher | deCWr |
| deviceClothesWasherDryer | dCWDr |
| deviceCoffeeMachine | deCMe |
| deviceCookerHood | deCHd |
| deviceCooktop | devCp |
| deviceDehumidifier | devDr |
| deviceDishWasher | deDWr |
| deviceDoor | devD0 |
| deviceDoorLock | deDLk |
| deviceElectricVehicleCharger | dEVCr |
| deviceFan | devFn |
| deviceFoodProbe | deFPe |
| deviceFreezer | devFr |
| deviceGlucosemeter | devGr |
| deviceHeartRateMonitor | dHRMr |
| deviceHomeCCTV | dHCCT |
| deviceHumidifier | devHr |
| deviceKettle | devKe |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceMultiFunctionPrinter | dMFPr |
| deviceOutdoorLamp | deOLp |
| deviceOven | devOn |
| devicePrinter | devPr |
| devicePulseOximeter | dePOr |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceScanner | devSr |
| deviceSecurityPanel | deSPl |
| deviceSetTopBox | dSTBx |
| deviceSmartElectricMeter | dSEMr |
| deviceSmartPlug | deSPg |
| deviceSteamCloset | deSCt |
| deviceStorageBattery | deSBy |
| deviceSwitch | devSh |
| deviceTelevision | devTn |
| deviceThermometer | devTr |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWaterValve | deWVe |
| deviceWeightScaleAndBodyCompositionAnalyser | dWSAB |
| deviceWindowShade | deWSe |
| deviceBottleWarmer | deBWr |

### -----------------------End of change 2---------------------------------------------