| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#42 |
| Source:* | Rong Long, CMCC, longrong@chinamobile.com |
| Date:* | 2019-09-16 |
| Reason for Change/s:* | Adding a new DataPoints item for waterMeterAlarm ModuleClass |
| CR against: Release* | Rel.4 |
| CR against: WI* | Active WI-0017 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.1.0 |
| Clauses * | New clauses in 5.3.1.101 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a new alarm item into waterMeterAlarm ModuleClass to indicate the customer leakage

-----------------------Start of change 1-------------------------------------------

Table 5.3.1.94-1: DataPoints of waterMeterAlarm ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| highFlowAlarmThreshold | xs:float | RW | false | m3 | The threshold of continuous high flow alarm. |
| highFlowDuration | xs:integer | RW | true | s | The duration of high water flow. |
| highFlowAlarm | xs:boolean | R | false |  | Continuous high water flow alarm |
| lowFlowAlarmThreshold | xs:float | RW | true | m3 | The threshold of continuous low flow alarm. |
| lowFlowDuration | xs:integer | RW | true | s | The duration of low water flow. |
| lowFlowAlarm | xs:boolean | R | true |  | Continuous low water flow alarm |
| reverseFlowAlarmThreshold | xs:float | RW | true | m3 | The threshold of continuous reverse flow alarm. |
| reverseFlowDuration | xs:integer | RW | true | s | The duration of reverse water flow. |
| reverseFlowAlarm | xs:boolean | R | false |  | Reverse flow alarm |
| highPressureAlarmThreshold | xs:float | RW | false | bar | The threshold of high water pressure alarm. |
| highPressureAlarm | xs:boolean | R | false |  | High water pressure alarm |
| lowPressureAlarmThreshold | xs:float | RW | false | bar | The threshold of low water pressure alarm. |
| lowPressureAlarm | xs:boolean | R | false |  | Low water pressure alarm |
| highTemperatureAlarmThreshold | xs:float | RW | false | C | The threshold of maximum water temperature alarm. |
| highTemperatureAlarm | xs:boolean | R | false |  | High water temperature alarm |
| lowTemperatureAlarmThreshold | xs:float | RW | false | C | The threshold of minimum water temperature alarm. |
| lowTemperatureAlarm | xs:boolean | R | false |  | Low water temperature alarm |
| highTemperatureInnerlAlarmThreshold | xs:float | RW | true | C | The threshold of high temperature alarm inside water meter. |
| innerhHighInternalTemperatureAlarm | xs:boolean | R | true |  | Internal high temperature alarm |
| innerErrorAlarm | xs:boolean | R | true |  | Internal error alarm |
| innerTempratureSensorFault | xs:boolean | R | true |  | Internal temperature sensor failure |
| tamperAlarm | xs:boolean | R | true |  | Data was tampered alarm |
| waterTempratureSensorFault | xs:boolean | R | false |  | Water temperature sensor failure |
| pressureSensorFault | xs:boolean | R | true |  | Pressure sensor failure |
| communicationAlarm | xs:boolean | R | true |  | Communication abnormality alarm |
| magneticInterference | xs:boolean | R | true |  | Magnetic interference warning |
| storageFault | xs:boolean | R | true |  | Storage failure alarm |
| urgencyButtonPush | xs:boolean | R | true |  | Indicate the event of the urgency button being pushed. Pushing the urgency button may give a user a temporary right to still use the water meter (e.g. for 3 days) after an unpaid bill. |
| buttonFault | xs:boolean | R | true |  | Button error flag |
| demolitionAlarm | xs:boolean | R | true |  | Demolition sign |
| impulseFault | xs:boolean | R | true |  | Pulse anomaly flag |
| vibrationSensorFault | xs:boolean | R | true |  | Vibration sensor failure |
| CustomerLeakage | xs:boolean | R | true |  | indicating continual usage (e.g. greater than 5 L/h for 24 hours and the flow never returning to zero at any time). |

### -----------------------End of change 1---------------------------------------------